## Slide 1
D.A. Salamatin1,2,3, M.V. Mikhin2, A.V. Salamatin2,
A.V. Tsvyashchenko3, M. Budzynski4
1Moscow Institute of Physics and Technology (MIPT), SU, Dolgoprudny, Russia
2Joint Institute for Nuclear Research (JINR), Dubna, Russia
3Vereshchagin Institute for High Pressure Physics (HPPI), RAS, Moscow, Troitsk, Russia
4Institute of Physics, M. Curie-Sklodowska University, Lublin, Poland
Компактный цифровой спектрометр
возмущенных угловых гамма-гамма корреляций (ВУК)
Compact digital time differential perturbed angular
gamma-gamma correlation (TDPAC)-spectrometer

## Slide 2: Time differential perturbed angular gamma-gamma correlation (TDPAC) method

## Slide 3: The applications of TDPAC
111Cd-TDPAC study of pressure effect on the valence of Yb in the YbGe2.85 cubic phase
A.V. Tsvyashchenko et al. JALCOM (2013)
doi: 10.1016/j.jallcom.2012.10.02
Hyperfine field assessment of the magnetic structure of ZrZn2
A.V. Tsvyashchenko et al. PRB (2015)
doi: 10.1103/PhysRevB.91.104423
Incommensurate antiferromagnetism induced by a charge density wave in the cubic phase of TbGe2.85
A.V. Tsvyashchenko et al. PRB (2015)
doi: 10.1103/PhysRevB.92.104426

## Slide 4: The block-scheme of the setup

## Slide 5: LaBr3 detectors
 | Energy resolution @ 137Cs | Time resolution @ 511-511 keV, ps | Density, g/cm3 | Light yield, photons/keV | Decay time, ns
LaBr3:Ce (BrilLanCe 380) | 3 % | 250 | 5.1 | 65 | 16
BaF2 | 10 % | 150 | 4.9 | 2/10 | 0.7/630
NaI:Tl | 7 % | > 1000 | 3.7 | 39 | 250
PMT: Hamamatsu R6231-100, risetime = 8 ns

## Slide 6: The signals from the detector

## Slide 7: Energy algorithms
 | Amplitude of the signal | Integration of the signal (QDC) | Trapezoidal pulse shaping filter
Average resolution at 511 keV | 8.0 % | 4.0 % | 3.2 %
Algorithm implementation |  |  | 

## Slide 8: Time algorithms
 | Digital CFD line interpolation | Digital CFD cubic interpolation | Gaussian approximation
Average resolution at 1173 - 1333 Kev @ 60Co | 425 ps | 400 ps | 400 ps
Algorithm implementation |  |  | 

## Slide 9: Tests: energy resolution (1)

## Slide 10: Tests: energy resolution (2)
FWHM (%) =

## Slide 11: Tests: time resolution

## Slide 12: Tests: TDPAC for 44Ti in TiO2 (rutile phase)
ωQ (Mrad/s) | η | Ref.
16.1 | 0.94 | T. Butz et al. PRB (2008) ¦ LaBr3
16.4 | 0.93 | Старая установка (2016) ¦ NaI

## Slide 13: Tests: TDPAC for 181Ta in HfO2 (monoclinic phase)
ωQ (Mrad/s) | η | Ref.
126.0 | 0.36 | Baudry et al. HI (1983) ¦ BaF2
123.0 | 0.34 | A. Ayala et al. PRB (1994) ¦ CsI
119.0 | 0.32 | Старая установка (2002) ¦ BaF2

## Slide 14: Old setup vs the modern one
35 electronic modules
~55 cables
5 electronic modules
9 cables
Toroid high-pressure cell:
P < 8 GPa, T = 300 K
Helium cryostat
Piston-cylinder (P < 2 GPa, T > 4 K) and diamond anvil (P < 20 GPa, T > 4 K)
high-pressure cells

## Slide 15: Spectrometer software

## Slide 16
Thank you for you attention!