## Slide 1: Simulation of stand MiniSPD on Geant4
Elina Kasyanova
15.10.2020

## Slide 2
Run a simulation of the stand MiniSPD on of cosmic rays particles (μ, e, p)
with different energies
2
Purpose of my work

## Slide 3
Stand MiniSPD
The purpose of the stand is testing straw-station
and collaboration of all detectors
3
Trigger system:
• three scintillators
Calorimeter - 396 mm
Lead - 375 mm
Stand (aluminum)
Stand (steel)
[Temur Enik (temur.enik@cern.ch)]
MiniSPD project is an international collaboration
• two GEM detectors
three silicon detectors
two straw detectors

## Slide 4
Testing on cosmic rays
Muons are the most numerous charged particles at sea level.
The mean energy of muons at the ground is ≈ 4 GeV.
4
Сosmic rays

## Slide 5: Simulation of stand MiniSPD
5
Lead
Scintillator N1
Scintillator N3
Straw stations
Calorimeter
SI N2
GEM N1
Scintillator N2
GEM N2
SI N3
SI N1
Git.Jinr: https://git.jinr.ru/aivanov/MiniSPD.git
Stand Al
Steel stand
Simulation of Stand MiniSPD
(The first simulation was made by Artem Ivanov)
the position of the detectors based on the last alignment (22.05.2020)

## Slide 6: Quantity of materials of stand MiniSPD
6
Stand steel
Stand Al
GEM
Calorimeter (220 slices)
Straw
Scintillator
Silicon
12 mk Outer Kapton
2.3 mm Carbon
0.3 mm Silicon
0.25 mm FRA4 top
1.5 mm scintillator
0.3 mm Pb
3 mm PMM
5 mm scintillator
2 mm PLA Plastic
0.25 mm FRA4 bottom
7 mk Glue
40 mk Inner kapton
Gas ArCo2
30 mk Tungsten wire
0.9 mm ArCo2

## Slide 7: Simulation of stand MiniSPD on time 15.10.2020
7
Lead
Scintillator N3
Calorimeter
GEM N2
Scintillator N2
Straw stations
GEM N1
Scintillator N1
SI N2
SI N1
SI N3
Simulation settings:
10 000 events
PV (10, 10, -80) mm
point source
• e-, μ-, proton
100 MeV, 1, 10, 100 GeV
Stand Al
Stand steel
• material of World volume – Air
Starting conditions

## Slide 8: Simulation of stand MiniSPD
μ- beam (10000 particles) with energy of 1 GeV
8

## Slide 9: μ- beams
1 GeV
10 GeV
100 GeV
9
SI N1
SI N2
SI N3
Straw
100MeV

## Slide 10: e- beams ( + shower e+e-)
1 GeV
10 GeV
100 GeV
10
SI N1
SI N2
SI N3
Straw
100MeV

## Slide 11: proton beams
1 GeV
10 GeV
100 GeV
11
SI N1
SI N2
SI N3
Straw
100MeV

## Slide 12
• Take into account the cosmic ray flux angular distributions.
• Include RS simulation
12
Planned in the near future

## Slide 13
Thank you for your attention !