## Slide 1: Appearance miniSPD
Detectors
Climate control
Gas system
DAQ
Detector power systems

## Slide 2: Functional structure of the stand

## Slide 3: DAQ crate

## Slide 5: Trigger
- 16 channels, 50 Ohm
- TDC: time-stamping, 25ps bin size
- Amplitude (charge) measurement: 10/14 bit, 80 MS/s ADC
- On-board trigger matching logic
- 2 Scintillators ( (SiPm 4ch)
- 1 Scintillator (Pmt 1ch)
- TQDC

## Slide 6: BM@N Silicon detector module design
Size: 63x63x0,3 mm3 (on 4” – FZ-Si wafers)
Topology: double sided microstrip (DSSD)
(DC coupling)
Pitch p+ strips: 95 μm;
Pitch n+ strips 103 μm;
Stereo angle between p+/n+ strips: 2.50
Number of strips/DSSD: 640 (p+)(n+)
Number of strips/module: 640 (p+)(n+)
Pitch Adapter (n+) side
sapphire plates with Si-epitaxial layer Silicon On Insulator (SOI)
Number of channels: 640
Value of poly-Si resistors: 1 MΩ
Value of integrated capacitors: 120 pF
Capacitor working voltage: 100 V
Capacitor breakdown voltage: >150 V
ASIC VATAGP7.1 (5 chips on each side of module)
Number of CSA: 128 channels
Dynamic range: 30 fC
Peaking time (slow/fast shaper): 500 ns/ 50ns
Noise (ENC): 70e +12e/pF (typ.)
Voltage supply: +1.5 V, -2.0 V
Gain from input to output buffer: 16.5 µA/fC
Output Serial analog multiplexer clock speed: 3.9 MHz
Power dissipation per channel: 2.2 mW
[M.Kapishin , Status of Baryonic Matter at Nuclotron, October 2018]
Positions of Forward and Vertex Silicon Detector at BM@N technical run March 2018

## Slide 7: Silicon detector

## Slide 8
Silicon detector

## Slide 9: Events reconstruction
hitX, cm
hitY,
cm
hitX, cm
hitY,
cm
hitX, cm
hitY,
cm
a)
b)
c)
Hits plots in BM@N Si-modules;
Reconstructed track in muon stand (based on bmnroot framework);
c) BM@N Silicon modules;

## Slide 10: STRAW
2 station
straw tube with 6mm diameter, in the centre a 30mrm diameter gold-plated tungsten wire
Length straw 20 cm
Precision measurement of 0.2 mm
6mm
Straw winding. Two film strips are wound around the mandrel

## Slide 11
STRAW data monitoring
The r(t) relation (isochrone relation or “V-shape”) for straw tubes 30-33

## Slide 12: GEM

## Slide 13
GEM data monitoring

## Slide 14
ECAL
ECAL MIP spectra in corresponding cells (top view)

## Slide 15: ECAL
ECAL module (110x110 mm2)design
Module consist of 4 cells 55x55x440 mm3:
220 Layers Lead and Scintillator
1.5 mm – Scintilator
0.3 mm - Lead

## Slide 16: Alignment

## Slide 17: Gas supply system

## Slide 18: Slow control
TQDC16

## Slide 19: Geant4
10
MiniSPD: - 100 GeV
MiniSPD: - 10 GeV
MiniSPD: - 100 MeV
MiniSPD: - 1 GeV