## Slide 1: Vacuum system of NICA project
A.Smirnov, A.Galimov, A.Svidetelev, A.Tikhomirov
JINR, Dubna, Russia
Alushta, Crimea
05/09/2017

## Slide 2
Fixed Target Area
BM@N
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20
Ion sources
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 600 MeV/u
Linac HILac
KRION HIS
NICA: Structure and Operation Regimes
Stripping
Two SC
collider rings
~ 22 bunches per ring

## Slide 3: Vacuum systems of particle accelerators
Accelerator | Length, m | Pressure, Pa | Pump types | Status
LU-20 | 20 | 10-4 | Turbo pumps + cryopump | Upgraded
HILAC | 11,5 | 10-5 | Turbo pumps + ion pumps | Assembled
Nuclotron | 251,5 | 10-7 | Turbo pumps + ion pumps | Upgraded
Booster | 211 | 10-9 | Ion pumps + getters | Start version (turbopump)
Collider | 503 | 10-9 | Ion pumps + getters | Under design

## Slide 4: Booster vacuum systems
Name | Status | Chamber manufacturer | Pumping system *
Electron cooling system | Assembling at JINR | BINP, Novosibirsk | Ion pump, TSP, NEG
Injection septum Cold kicker | Design is finished Prototype | 1) BINP, Novosibirsk 2) Cryosystems, Moscow Bulgaria | Ion pump + TSP + CT, NEG
RF-station Pumping post | Testing at JINR Production | BINP, Novosibirsk MILLAB, Moscow | Ion pump + TSP + CT, NEG
Extraction system | Production | BINP, Novosibirsk | Ion pump + TSP + CT
Cold arcs Pick-up stations | Production Prototype | FRAKOTERM, Poland Bulgaria | 1) Turbo pump 2) Ion pump + NEG 3) + TSP @ LN
* TSP – titanium sublimation pump, LN – temperature of liquid nitrogen
CT – cryogenic trap, NEG – non evaporated getter

## Slide 5: Beam lifetime due to recombination on rest gas at booster
P = 10-9 Pa, T = 293 K, k = 1.38 10-23 J/K, β = 0.083 (3.2 MeV/u)
 = P  β c / T k – beam lifetime
t_life = 1000 s,  = 1.63 10-22 m2 (Au31+, H2 rest gas)
t_life = 25 s,  = 68.6 10-22 m2 (Au31+, N2 rest gas)

## Slide 6
1. Gun, 2. Collector, 3. Sublimation pump TSP-IKG «VACOM», 4. Bent chamber,
5. Toroid section, 6. Pick-up station, 7. Cooling section, 8. Dipole section, 9. Bellows,
10. NEG position, 11. Vacuum valve, 12. Bellows, 13. Ion pump, 14. Connector.
Vacuum chamber of electron cooling system (BINP)
Chart: WARM-UP VALUES
| 09.00 | 11.00 | 13.00 | 15.00 | 17.00 | 19.00 | 21.00 | 23.00 | 01.00 | 03.00 | 05.00 | 07.00 | 09.00 | 11.00 | 13.00 | 15.00 | 17.00 | 19.00 | 21.00 | 23.00 | 01.00 | 03.00 | 05.00 | 07.00 | 09.00 | 11.00 | 13.00 | 15.00 | 17.00
T, ˚C | 30 | 63 | 122 | 170 | 200 | 229 | 229 | 229 | 229 | 229 | 229 | 229 | 229 | 230 | 235 | 237 | 240 | 240 | 240 | 240 | 240 | 240 | 240 | 240 | 240 | 220 | 178 | 130 | 90
P, m bar | 1 | 31 | 230 | 140 | 140 | 66 | 35 | 25 | 21 | 18 | 17 | 15 | 14 | 14.3 | 21.4 | 20.7 | 20.4 | 20.6 | 20.8 | 21.2 | 21.8 | 21.7 | 21.2 | 20.1 | 18.4 | 10 | 4.9 | 3.3 | 3.06

## Slide 7: Vacuum system of injection section (Cryosystems)
Ion pump + NEG
Ion pump
IK1
IES
IK2
IK3
IES
IK2

## Slide 8: Pump station (MILLAB) with RF-station (BINP)

## Slide 9: Extraction system of booster (BINP)

## Slide 10
Booster vacuum chambers of cold arcs (FRAKOTERM)
Pump station @ RT
TSP @ LN
Dipole chamber
Quadrupole & pick-up chamber
Pick-up

## Slide 11: 1) Startup version of vacuum scheme for booster cold arcs is included turbopumps only

## Slide 12: Prototype of vacuum stand (Vakuum Praha)
S
100
100/40
100
40
63
100x5
63x3
100/63
63
16x3
16
16
1
2
3
4
5
6
7
18
13
10
12
11
16
19
16x3
40/16
14
15
17
20
8
9
40x4
21
24
23
22

## Slide 13: Evolution of vacuum distribution
In accordance with V.Ziemann for same temperatures:
For different temperatures terms
are replaced on:
where V – chamber volume, P – pressure, Δt – time step, L – distance,
C – conductance, S – pump speed, Q – outgassing, j – point number.

## Slide 14: Real distribution of pressure and density
, k = 1.38 10-23 J/K ,
Warm sections @ room temp
Cold sections @ cryogenic temp

## Slide 15: Input File for BetaVacuum Code (MAD format)
var : T_0 = 15
var : T_1 = 293
pump : pump0 = 0.5
pump : pump1 = 0
pump : pump2 = 0
pump : pump3 = 2
leak : leak0 = 0
//tube: name = length, temp, square, conduct, outgas, pump
tube : tube1 = 0.304, T_0, 0.02, 0.426, 2.51e-11, 0
tube : quad = 0.639, T_0, 0.0065, 0.071, 1.56e-11, 0
tube : tube2 = 0.660, T_0, 0.02, 0.426, 2.51e-11, 0
line : duplet0 = tube1, pump0, quad, tube2, quad, tube1
line : duplet1 = tube1, pump1, quad, tube2, quad, tube1

## Slide 16
tube : tube3 = 0.444, T_0, 0.02, 0.426, 2.51e-11, 0
tube : dipole = 2.456, T_0, 0.0065, 0.071, 1.56e-11, 0
line : dipole2 = tube3, dipole, pump2, tube3, dipole, tube3
line : super0 = pump2, dipole2, duplet0
line : super1 = pump2, dipole2, duplet1
line : super5 = super1, super0, super1, super0, super1
tube : warm = 2.5, T_1, 0.2, 2, 5e-10, 0
line : booster4 = warm, pump3, warm, duplet1, super5
line : booster = booster4, booster4, booster4, booster4
ini : booster = 2e-8, 293, 0.1 ; pressure, temperature, length step
run : pump = 5, 0.5, 0.082, 1e9 ; pump time, time step, beta, Nion
pump : pump1 = 0.5
run : pump = 5, 0.5, 0.082, 1e9
pump : pump2 = 0.5
run : pump = 5, 0.5, 0.082, 1e9
end

## Slide 17: Simulation of dynamics vacuum and pressure distribution (all gauges at room temperature)
1) Red line – startup vacuum scheme,
2) Blue line – normal vacuum scheme
3) Green line - with additional TSP@LN
between magnets

## Slide 18: 3D Vacuum Evolution
Circumference [m]
Time [s]
Pressure [Pa]

## Slide 19: Collider vacuum chamber sizes
Chart: 1/4 collider circumference from interaction point
Elliptical chamber

## Slide 20: Simulation of pressure distribution (1/4 of collider)
 = 4×10-7 s-1 for  = 68.5 10-28 m2 (1 GeV/u Au79+, N2 rest gas)

## Slide 21: Vacuum chambers for collider cold arcs (FRAKOTERM)

## Slide 22: Collider RF-stations (BINP)

## Slide 23: Multi Purpose Detector