Geometric modeling
in particle physics community
Ovcharenko Egor
LIT JINR, Dubna
AYSS-2017, Dubna, Russia, 04.10.2017

---
Outline
1/18
Geometry representations:
BREP – CAD systems;
CSG – GEANT4, ROOT;
Polygonal – 3dMax, Maya, Blender, ...
        - Triangulated – all 3d applications;
FEM – ANSYS, COMSOL, Abaqus, Nastran, …
- Conversion possibilities;
- “CATIA-GDML geometry builder”;
  - Use-cases.
AYSS-2017, Dubna, Russia, 04.10.2017 Ovcharenko Egor, LIT JINR

---
1. Boundary REPresentation (BREP), solid, p.1
2/18
Point – a 3-tuple of coordinates.
Vertex – a topological entity which lies on a geometrical point.
Line – an equation (usually a parametric equation of 1 parameter p) which defines a set of points in 3d – a 3d curve.
Edge – a topological entity which lies on the line and is limited by 2 vertices.

---
1. Boundary REPresentation (BREP), solid, p.2
3/18
Surface – an equation (usually a parametric equation of 2 parameters u, v) which defines a set of points in 3d – a 3d surface.
Face – a topological entity which lies on a surface and is limited by a closed loop of edges.
Solid is an object limited by a closed shell of faces.

---
1. BREP summary
4/18
- Used in CAD systems.
- The most generic method
  to represent geometry in
  computer.
- BREP allow not only solids, but separate surfaces, lines, and points.
- Most popular exchange formats are STEP and IGES.
- Primary goal – precise representation of any geometry using complex math, if needed.

---
2. Constructive Solid Geometry (CSG)
5/18
- Primitives – box, parallelepiped, hollow tube section, hollow cone section, hollow sphere section, trapezoids, etc…
- Boolean operations – Union, Subtraction, Intersection
- Geometry specification – list of bodies, each body being a Boolean tree.
- Used in CAD systems in their infancy.
- Currently used by GEANT/ROOT
  and in some very specific fields.

---
1. CAD approach to building BREP
6/18
- Shape:
  - Create planar sketches;
  - Create datum elements – axes, planes;
  - Create a solid using one of the four basic features – pad, shaft, rib, multi-section solid;
  - Modify created solid using one of the four basic features.
  - CAD system builds BREP.
- Volume hierarchy:
  - Infinite space with no material;
  - All shapes within this space without overlaps (in a normal situation).
- Geometry specification – complex tree of products – only logical grouping.

---
2. GEANT/ROOT approach
7/18
- Geometry for Monte Carlo (MC) simulation
  of particles propagation.
- Shape:
  - CSG.
- Volume hierarchy:
  - Primary goal – unambiguously
    define material in each point in space;
  - Minimize geometry definition size (in Mb);
  - Thus – volumes (logical) and nodes (physical volumes), positioning matrices.
- Declarative geo description, ROOT “C” macro, advanced software packages (SimpleGeo – dead project, CAD converter – very unstable)
CMS MC geometry

---
3. Polygonal geometry
8/18
Polygons are easily converted into triangles.
Triangles are rendered very fast – this is GPUs primary design goal.
Polygonal geometry is used for visualization, for photo-realistic images generating, cartoons, video games, etc...
Software like Autodesk 3dMax, Autodesk Maya, Blender is used to build, edit and render polygonal geometry.
Polygons can hardly be used to describe solids (with no holes in boundaries).
Primary goal –
nice picture.

---
4. Finite-element geometry
9/18
Used by finite-element model (FEM) solvers to perform physics simulations: mechanical, hydrodynamics, thermodynamics, etc…
The solid is represented as a set of adjacent finite elements, most used being tetrahera.
COMSOL

---
BREP – CSG – FEM – Polygonal
10/18
CSG: Boolean – separate operands
CSG: Boolean, visually equiv. to BREP
Polygonal (triang.) for visualization
FE-model, only triangulated surfaces are seen

---
Conversion
11/18
- CSG into BREP – easily! Full and automatic conversion is possible. All CAD systems can do that. OpenCASCADE Technology library provides C++ functions to do that.
- BREP (CSG) into polygonal (triangulated) – almost as easy! Approximation of original smooth surfaces using Delaunay algorithm. Needs precision parameter value set by the user and quality control in the end.
- BREP (CSG) into FEM – well-developed semi-automatic procedure. Most FEM software can do that, some specialized packages exist.
- Polygonal (FEM) into BREP – (a) reverse polygonalization impossible,
  (b) direct conversion (each polygon into a face) – plain but almost senseless.
- BREP into CSG – impossible, thus different specialized solutions such as “CATIA-GDML geometry builder”.

---
CATIA-GDML geometry builder
12/18
- https://gitlab-hybrilit.jinr.ru/cad2gdml/CATIA-GDML_geometry_builder
- S Belogurov et al 2011 J. Phys.: Conf. Ser. 331 032035
- S Belogurov et al 2014 J. Phys.: Conf. Ser. 513 022003
- One prerequisite which stops many potential users: the “Builder” requires CATIA v5 and basic skills of using it.
- However this should should not stop you because:
  - (a) any new software requires some learning time and you really don’t need to learn a lot about CATIA to start working with the “Builder”.
  - (b) JINR has CATIA licenses.
  - (c) we are here to help you.

---
CATIA-GDML geometry builder
13/18
- Create a new product document;
- Give it a name, save it on disk;
- Define volume's shape using Add shape, Poly and Boolean.
- Create volume hierarchy using Inserter, Replica, ArrayMaker;
- Define rotations and positions of the volumes using Point-to-point aligner and Measure;
- Introduce parameterization;
- Use Duplicator if needed;
- Check that the materials are correctly defined using Materials manager;
- Check the model using Checker;
- Export the model using CATIA2GDML;
- If you are using ROOT or ROOT-based package, perform geometry check.

---
Use-cases
14/18
- Over 7 years we have applied “CATIA-GDML geometry builder” in several projects and we are looking forward to find new users:
  - CBM RICH detector – driving use-case.
  - PANDA Muon system.
  - CMS Muon system, CMS beampipe.
  - R3B “GLAD” cryostat.
  - CBM ECAL support structure, CBM beampipe, CBM MVD, CBM vacuum chamber, CBM magnet.
  - Some other small projects.

---
CBM RICH MC-model
15/18

---
CBM RICH MC-model
16/18

---
CBM RICH MC-model
17/18

---
CBM RICH readout module
CAD
Reality
MC