## Slide 1: Status of the GEM tracking system at the BM@N experiment
Andrei Galavanov on behalf of the BM@N Collaboration

## Slide 2
Booster, 3 – 660 MeV/u
Nuclotron,
0.6 – 4.5 GeV/u
NICA complex
Collider,
√S = 4 – 11 GeV/u
Linear accelerators, 3 MeV/u

## Slide 3
BM@N experiment
GEM tracking system
Experimental setup for high intensity heavy ion beams
BM@N provides a unique opportunity to study strange mesons and multi-strange hyperons close to the kinematic threshold. One of the main goals is to measure yields of light hyper-nuclei, which are expected to be produced in coalescence of Λ-hyperons with nucleons.

## Slide 4
Electric field in the region of the holes in a GEM foil.
Electron microscope picture of a section of typical GEM foil: 50 μm thick capton foil, metalized on each side by 5 μm thick copper electrodes . The holes pitch and diameter are 140 and 70 μm, respectively.
Electron avalanche in GEM holes.
The gas electron multiplier (GEM)
DRIFT
Particle
Typical scheme of a triple GEM detector.

## Slide 5
BM@N GEM detectors
0.8
0.68
0.16
0.8
Schematic cross section of the BM@N triple GEM detector
Now we have:
7 detectors 1632 × 450 mm2
7 detectors 1632 × 390 mm2
2 spare detectors will be produced in 2021

## Slide 6
BM@N GEM detectors
Readout board
Cathode plane

## Slide 7
GEM tests on Nuclotron beams
Magnetic field 0.6 T, Ar(80)/Isobutane(20),
Ar beam, Edrift = 1.5 kV/cm
σ = 213 µm
Magnetic field 0.6 T, Ar(90)/Isobutane(10),
d beam, Edrift = 0.8 kV/cm
σ = 670 µm
In Ar and Kr runs, the value of electric field in drift gaps of GEM detectors was increased. The gas mixture was changed to Ar(80)/Isobutane(20). The Lorentz shift of electrons avalanche was decreased.
Magnetic field 0.6 T,
Ar(70)/CO2(30),
C beam, Edrift = 1.2 kV/cm
σ = 309 µm
2016
2017
2018
Fragments of Ar beam in detector
Example of the event reconstruction

## Slide 8
Carbon beam, 4 GeV/n
C + C, Al, Cu → Λ + X minimum bias
Λ signal width 2.4 – 3 MeV
C+C: 4.6M triggers
C+Al: 5.3M triggers
C+Cu: 5.3M triggers
2.5 days of data taking
Λ-hyperon signals

## Slide 9
Scheme of the GEM full planes configuration
Lorentz shifts of an electron avalanche in GEM planes
On top - 7 detectors with active area 1632×450 mm2
On bottom - 7 detectors with active area 1632×390 mm2
top
bottom

## Slide 10
Full planes configuration inside the SP-41 magnet
Active area of the GEM tracking system is around 9.5 m2
Space for the installation and alignment
is limited by the aperture of our magnet
10.2020 – development
of the mechanics design for GEM planes inside the magnet.
2021 – mechanics production, installation of the GEM planes.

## Slide 11
Material budget of the GEM central tracking system
full configuration
D. Baranov

## Slide 12
Assembly of the stand for long-term GEM tests
First stage – tests of 1632*390 mm2 detectors, in progress
Second stage – tests of 1632*450 mm2 detectors
Main goals: to study geometrical efficiency and spatial resolution
DAQ system
Trigger and HV system
GEM detectors
Scintillation detectors

## Slide 13
Gas system
Gas system requirements :
stable flow and mixture parameters;
7 independent channels to each GEM-plane;
reducing and control oxygen and moisture impurities in gas mixture;
Discharge probability on alphas as a function of moisture level in the gas. COMPASS
Multichannel gas mixer
H20 and 02 filter
H20 and 02 analyzer
Distribution panel
GEM plane
Oil gate
For one channel
Gas cylinders
H20 and 02 analyzer
Oxygen analyze - GE oxy.IQ
Moisture analyze - GE dew.IQ+ GE IQ.probe

## Slide 14
Conclusions
7 detectors 1632×450 mm2 and 7 detector 1632×390 mm2 are produced;
7 detectors 1632×450 mm2 was tested at d, C, Ar, Kr ion beams;
2 spare detectors are waiting for the assembly at CERN;
High Voltage and Low Voltage systems are ready;
Gas system is under upgrade;
Mechanics for GEM-planes inside the magnet has been developed;
Assembling the stand for testing the GEM-detectors with cosmic rays has been finished;
Tests of 1632*390 mm2 detectors with cosmic rays are in progress.
Deadline – autumn 2021

## Slide 15
Back up slides

## Slide 17
Material budget of one Gem detector

## Slide 18
GEM HV divider scheme
Mixture | I, mkA | DR, kV/cm | Gem 1, V | TR1, kV/cm | Gem 2, V | TR2, kV/cm | Gem 3, V | IND, kV/cm
Ar (70) + CO2 (30) | 490 | 1.17 | 402 | 2.58 | 382 | 3.68 | 363 | 4.18
Ar (90) + C4H10 (10) | 370 | 0.88 | 303.4 | 1.92 | 288.6 | 2.78 | 273.8 | 3.16
Ar (80) + C4H10 (20) | 430 | 1.5 | 352.6 | 2.24 | 335.4 | 3.23 | 318.2 | 3.67
490 mkA – working point for Ar (70) + CO2 (30) gas mixture
370 mkA – working point for Ar (90) + Isobutane (10) gas mixture
430 mkA – working point for Ar (80) + Isobutane (20) gas mixture
50 kΩ
1.05 MΩ
820 kΩ
1.3 MΩ
780 kΩ
1.5 MΩ
740 kΩ
1.28 MΩ
2000 pF
HV

## Slide 19
GEM efficiency (cosmic tests)
GEM Efficiency

## Slide 20
GEM gas gain measurements
Amplitude distribution, Ar(70)/CO2(30), Fe55
GEM gas gain for Ar(70)/CO2(30) and Ar(90)/Isobutane(10) gas mixtures
cathode
Gem1
Gem2
Gem3
anode
Fe55
Discr.
Trigger
ADC
Experimental
scheme