## Slide 1
Beams formation for the injection into NICA Booster
Levterov K. on behalf of Acceleration Division
1/25

## Slide 2
Area layout
2/25

## Slide 3: HILAC & LILAC – two injectors for NICA
SPI
Nuclotron
ESIS
Booster
Into collider
LIS
RFQ
IH1
IH2
HILАC
Au31+ 3.2 MeV/u
7 MeV/u or 13 MeV for p
p↑, d↑, ions z/A>0.3
Beams of polarized particles p и d and light ions will be accelerated by LILAC (now it is LU-20), then injected into Nuclotron
Heavy ions : HILAC + Booster + Nuclotron
600 Me/u
RF
IH1
IH2
IH3
3/25

## Slide 4: Injection Facility arrangement
p↑, d↑, ions Z/A>0,3
RFQ
Ions Z/A>0,3
LIS
SPI
p↑,d↑
10mA
HILАC
Nuclotron
Booster
RF amplifier for LU-20
LU-20
(to be replaced with LILAC)
Transport channel to booster
Transport channel
to Nuclotron
ESIS
“KRION”
4/25

## Slide 5: TOPICS
Alvarez proton linac LU-20 as an ions injector for Nuclotron
Heavy ion injector based on the KONUS IH-DTL accelerating structure
Ion sources of the NICA injection facility
Formation the beams of ions produced with the Laser Ion Source or plasma ion source with the cold hollow cathode for HILAC and Booster commissioning.
RF beam loading and beam output energy vs RF tuning of IH2
Summary.
5/25

## Slide 6
1974- LU-20 commissioning, 2-2.5×1011 20 MeV protons/pulse, 4×1012 protons/pulse – record achievement
1971- A.M. Baldin paper “Масштабная инвариантность адронных столкновений и возможность получения пучков частиц высоких энергий при релятивистском ускорении многозарядных ионов”
1974 Oct - LU-20 operates in 2ββλ mode as injector of α-particles and deutrons produced by duoplasmotron ion source developed in LHEP
1977 - С6+, N7+, O8+, Ne10+, produced with ESIS “KRION”
1993 – LU-20 reconstruction; proton beam current dropped down from 40 mA to 20 mA, deutron current increased from 10 mA to 14 mA
Alvarez proton linac LU-20 as an ion injector
Only protons were accelerated in βλ mode up to 20 MeV, the other ones species – in 2βλ up to 5 MeV/u
A/Z≤3 due to the reasons of both maximum RF power limitation and vacuum breakdowns in RF cavity
Main features and limitations of LU-20
6/25

## Slide 7
HILAC=RFQ + IH1 + IH2
A/Z 6.25 | Type | Length | RF power | Output energy
RFQ | 4 - rod | 3.16 m | 120 kW | 0.3 MeV/u
MEBT | Two QD + buncher | 1.4 m | 3 kW (buncher) | 0.3 MeV/u
IH1 | DTL + QT | 2.3 m | 296 kW | 2 MeV/u
IH2 | DTL | 2.1 m | 278 kW | 3.2 MeV/u
RFQ
IH-1
IH-2
MEBT
Heavy ion linear Injector based on KONUS DTL structure
7/25

## Slide 8
Main features:
• Main acceleration along a 0° synchronous particle structure with asynchronous beam injection and a surplus in bunch energy compared to the synchronous particle.
• Transverse focusing by a quadrupole triplet or a solenoid lens.
• Longitudinal focusing by a few rebunching gaps operating at φs = -35°
DTL structure IH1 + IH2
Au31+, Ein=300 keV/u Eout=3.2 MeV/u
Accelerating structure «KONUS» (KOmbinierte NUll grad Struktur).
βλ/2 IH-mode, H110.
“KONUS” in the world:
• HSI and HLI in GSI FAIR, Eout=1.4 MeV
• LINAC3- CERN, Eout=4.2 MeV
• Injector for Booster of AGS
· HIAF injector
8/25

## Slide 9
9/25

## Slide 10
10/25

## Slide 11
11/25

## Slide 12
 | HILAC
Species | 197Au31+, 207Bi34
Value А/Z | ≤ 6.25
Input energy | 17 keV/u
Output energy | 3.2 MeV/u
Beam current, mA | ≤10
Pulse spread behind debuncher | 10-3
Emittance normalized, π мм мрад | 0.6/0.4
Repetition rate | ≤ 10 Hz
Frequency, MHz | 100.625
Transmission, % | 98
Main parameters and design features of the HILAC
IH1 cavity with the
internal triplet inside
12/25

## Slide 13
RF power supply system based on the solid state amplifiers
140 kW- RFQ, 340 kW- IH1, 340kW-IH2
4 kW – Buncher, 4 kW - Debuncher
RF pulse duration up to 200 us
13/25

## Slide 14: Ion sources of the NICA injection facility
Electron String Ion Source KRION-6T – project ion source for HILAC
heavy ion production Au31+, Bi+Fe33
Source of Polarized Ions SPI:
project ion source for LILAC
light ion production: p↑, d↑
Laser Ion Source LIS:
wide light ions range:
Traditional species: Li3+, 7Li3+, B4+, C4+, N5+, O6+, F7+, Mg8+, Si11+ The new species: Fe
Helium ion source with the cold hollow cathode
He1+ - for commissioning and transmission estimation
14/25

## Slide 15
Test bench for plasma ion source
Plasma Ion Source is designed to produce the only one species He1+ to estimate HILAC transmission and for the Booster commissioning.
Gas system provides pulsed gas injection into space of magnetron discharge. Pulsed voltage up to 1 kV in the gaps between magnetron anode and magnetron cathode, and between magnetron cathode and anode was provided with the generator of HV pulses. Extraction voltage was supplied with the pulsed transformer and applied to the terminal whereas extraction electrode had a ground potential. Test bench for the TOF studies had three Faraday cups, beam modulation electrode and drift space ~1.8 m (see Fig. 2, 3). The total ion current was estimated with the signal from FC1and the value observed was up to 50 mA. There was the aperture 8 mm diameter in the bottom of the FC1.for the beam passing. About 25 cm behind the extracting electrode Faraday cup 2 and beam modulation electrode mounted together in one assembly could be placed manually on the beam way.
Plasma ion source with a cold magnetron hollow cathode and magnetic plasma compression
15/25

## Slide 16: Test bench for laser plasma research
Note that HILAC was commissioned with the beams of С2+ ions from LIS having mass-to-charge ratio A/Z=6 close to the project one A/Z=6.25 that the ions Au31+ or Bi33+ have.
Laser ion source
Light ions with A/Z≤3: 6Li3+, 7Li3+, B4+, C4+, N5+, O6+, F7+, Mg8+, Si11+. Development of the LIS is focused on the increasing of the radiation flux density on the target for the production of the ions in high charge states to provide as low A/Z ratio as possible. The previous limitation A/Z≤3 was limited by the maximum RF power and RF breakdown in cavity of proton linac LU-20. It seems reasonable to think about new sorts of heavier ions produced with Laser Ion Source that may be accelerated by HILAC in terms of “upgraded” A/Z=6.25.
16/25

## Slide 17
TOF spectra of He1+ ions produced with
Helium Ion Source
Yield of of He1+ ions ̴ 95%
17/25

## Slide 18
TOF spectra of ferrum ions produced with
Laser Ion Source
Fe ions charge states shot by shot evolution, lilac - SEM detector signals, blue - collected signal at the SEM input, yellow - collected signal at the analyzer input, white vertical line is TOF marker for Fe16+. Ionization energy for Fe16+ -489 eV, Fe17+ -1262 eV.
18/25

## Slide 19
TOF spectra of carbon ions produced with
Laser Ion Source
Carbon ions charge states shot by shot evolution (2us/div), green - SEM detector signals, yellow – collected signal at the SEM input, blue - collected signal at the analyzer input. Ionization energy for С6+ 490 eV.
19/56

## Slide 20
Beam diagnostic
Phase probes-3, current transformers-4, shoebox pickups- 5, Faraday cups-4, beam profile monitors - 6
2020-2021 – assembly of the HILAC-Booster channel,
He1+ beams accelerated with HILAC were used in the first run of NICA Booster
LEBT
HEBT
MEBT
20/25

## Slide 21
2015-2018 - HILAC assembly and commissioning
The beams of С2+ С3+ С4+ С5+ С6+ ions with a value A/Z=6 that is closed to the project one 6.25 from Laser Ion Source were accelerated for the HILAC commissioning. The energy of ions accelerated by each cavity step by step was measured.
Acceleration in RFQ, E=300 keV/u
Acceleration in RFQ+IH1, E=1.84 MeV/u
Acceleration in RFQ+IH1+IH2, E=3.2 keV/u
FC signal,
a.u.
FC signal,
a.u.
FC signal,
a.u.
21/25

## Slide 22
Acceleration of the Fe14+ ions produced with a Laser Ion Source
by HILAC and injection into Booster
Fe14+ ions accelerated in LEBT up to 17 keV/u, ion current duration ~2 us, 7.5 mA behind RFQ, 2.5 mA – behind IH2, 1.2 mA at the injection point.
No RF beam loading was observed
22/56

## Slide 23
RF beam loading
Level of RF power inside each cavity was controlled by the pickups signals monitoring. The detected signals of RFQ, IH1 and IH2 pickups were observed synchronously to the beam currents presented. One can see how the part of stored field energy was eaten by the beam passing through. One can also see the reaction of the amplifier – pushing back the cavity to equilibrium level after the extra requirement of beam acceleration has gone.
RF compensation is needed evidently.
RF signals from pickups under beam loading
23/25

## Slide 24
Two energy beams at the output depending on the RF phase in IH2,
phase probe behind IH1 and Faraday cup behind first bending magnet signals
FC1 signal
a.u.
3.2 MeV/u, bunch 1.92 ns, 6mA
IH1 ON
1.84 MeV/u, bunch 2.12 ns, 6.5mA
IH1 OFF
1.84 MeV/u, bunch 2.10 ns, 5/2mA
IH1 ON
Micro bunch duration
3.2 MeV/u ~ 1.9 ns
1.82 MeV/u ~ 2.1 ns
24/25

## Slide 25: Summary
The linear heavy ion injector based on HILAC has been commissioned with the beams of C2+ ions having A/Z ratio close to the project one 6.25
The beams of He1+ and Fe14+ have been accelerated and injected into Booster in its two first runs
Injector should be tuned for the maximum beam transmission
The RF system should upgraded to compensate beam RF loading
Two beam injection energies are available
Range of accelerated ions provided by new injector may be extended due to upgraded LIS based on Nd-YAG laser and “upgraded” ratio A/Z=6.25 available for HILAC.
Thanks
25/25