## Slide 1: Development of the Electron Cooling System for NICA Collider
Bryzgunov Maxim
on behalf of BINP Electron Cooling team

## Slide 2: High voltage electron cooling in the NICA collider
Electron cooling system for NICA booster
(In September of 2021 first cooling was achieved!)
HV electron cooler
In the collider two cooling systems (electron and stochastic) will work both during beam accumulation and during experiment.

## Slide 3: First electron cooling experience in collider
Electron cooler LEReC operated for RHIC physics program using 1.6 MeV kinetic energy electron beam to cool Au ions at 3.85 GeV/nucleon total energy and using 2 MeV electron beam to cool ions at 4.6 GeV/nucleon.
From: A. Fedotov et al., Operational Electron Cooling in RHIC, IPAC’21, Brazil, May 24-28, 2021

## Slide 4
Main problems:
High energy (up to 2.5 MeV);
Small distance between beams (320 mm);
Limited power consumption of the system (not more then 700 kW).
High voltage electron cooling in the NICA collider
Electron energy | 0.2 - 2.5 MeV
Energy stability (ΔU/U) | <10-4
Electron current | 0.1 - 1 A
Cooling section length | 6 m
Magnetic field in cooling section | 0.5 - 2 kG
Vacuum | 10-11 mbar
COSY HV cooler
The construction is based on HV ECS for COSY (Germany)
The HV ECS for NICA consists of two almost independent coolers. Scheme with one electron beam looks very complicated

## Slide 5: High voltage system
bottom flange
HV terminal
gun
HV column
middle section
vessel
collector
Purpose of the high voltage system is production of electron beam in electron gun and acceleration for working energy in electrostatic tube. After interaction with ion beam electrons flies to high voltage again where they are decelerated in another electrostatic tube and dumped in electron collector.
collector
solenoid
gun
solenoid
magnet PS
collector PS
control electronics

## Slide 6: High voltage system production
Collector PS
High voltage section
Electron gun
High voltage column
Middle section
High voltage terminal
Gun-collector control electronics
Wien filters

## Slide 7
Power transfer
Cascade transformer

## Slide 8
Magnetic system
Electrons move on whole trajectory from gun to collector in longitudinal magnetic field. Transport channels consist of set of straight and bend solenoids.

## Slide 9: Electronics
4
4
3
2
1
5
The ECS contains several systems:
Interlock system
PS for cascade transformer
Corrector magnet PS (MPS-6 and MPS-20)
High current magnet PS (IST)
Ethernet-CAN gateway
BPM electronics
6

## Slide 10
Hall for ECS commissioning in the BINP

## Slide 11: Magnetic measurements (Hall)
Hall probe measurement system contains set of straight and bent rails, which can be assembled n different way in order to measure magnetic filed distribution in different parts of the cooler.
Carriage for Hall probe
The rail in 90-degree solenoid
Tape
3-D Hall probe

## Slide 12
Magnetic measurements (compass)
Compass sensor provides high precision measurements of magnetic line straightness.
Scheme of compass measurements

## Slide 13: “Gun-collector” test bench
collector
gun
diagnostic node
Current measurement
Camera measurement
The test bench is assembled to test new electron gun. Its diagnostic node contains BPM and wire profile monitor and provides measurements both profile and temperature of the electron beam.
With the help of the wire profile monitor one can measure both current from the wire with ADC and wire glow (induced by beam) with CCD camera

## Slide 14: Thankyou for your attention!

## Slide 18
Electron cooling
circulating ion beam
“cool” electron beam
Cooling section
solenoid
Electron gun
Electron collector
Uncooled
ion beam
Cooled
ion beam

## Slide 19: High voltage electron cooling in the NICA collider
Electron cooling system for NICA booster
(In September of 2021 first cooling was achieved!)
Parameter | Value |  | 
Number of bunches | 22 |  | 
RMS length of a bunch, m | 0.6 m |  | 
β-function at the IP, m | 0.6 m |  | 
Energy Au79+, GeV / n | 1.0 | 3.3 | 4.5
Number of ions in the bunch | 2·108 | 2.4·109 | 2.3·109
RMS momentum spread, Δp/p | 0.6·10-3 | 1.2·10-3 | 1.6·10-3
RMS emittance, π·mm·mrad | 1.10/1.1 | 1.10/0.9 | 1.10/0.8
Time of growth due IBS, s | 160 | 530 | 1700
Luminosity, cm-2 ·с-1 | 0.6·1025 | 1.0·1027 | 1.0·1027
HV electron cooler
Parameters of the NICA collider
Two cooling systems (electron and stochastic) will work both during beam accumulation and during experiment.