## Slide 1: PECULIARITIES OF PRODUCING 48CA, 48TI, 52CR BEAMS AT THE DC-280 CYCLOTRON
1

## Slide 2: Superheavy Elements (SHE) Factory – the Goals .
Experiments at the extremely low (σ<100 fb) cross sections:
Synthesis of new SHE in reactions with 50Ti, 54Cr ...;
Synthesis of new isotopes of SHE;
Study of decay properties of SHE;
Experiments requiring high statistics:
Nuclear spectroscopy of SHE;
Study of chemical properties of SHE.
To carry out the scientific program, the DC-280 has to provide the following parameters of ion beams:
 | DC-280 | U-400
Ion energies (smooth variation) | 4 - 8 MeV/n | 4 – 20 MeV/n
Ion masses | 10 - 238 | 7 - 209
Intensities (A~50) | >10 pµA | 1 pµA
Efficiency of beam transfer from ion source to physical facility | >50% | ~10%
The first beam of 84Kr14 + ions in the DC-280 cyclotron was obtained on December 26, 2018. and on January 17, 2019, the 84Kr14 + ion beam was extracted from the accelerator
2

## Slide 3
3

## Slide 4
DC-280
Main Parameters
parameters | design | achieved
Injecting beam energy | Up to 80 keV/Z | 38,04 – 72,89 keV/Z
A/Z | 4÷7.5 | 4,4(40Ar+7) ÷6,9(48Ca+7)
Energy | 4÷8 MeV/n | 4,01 – 7 MeV/n
Ion (for DECRIS-PM) | 4-136 | 12 (12C+2) – 84 (84Kr+14)
Intensity (A~50) | >10 pµA | 10,4 pµA (40Ar+7);
Magnetic field level | 0.6÷1.3 T | 0.8÷1.23 T
K factor | 280 | 
Dee voltage | 2x130 kV | 130 kV
Power of RF generator | 2x30 kW | 
Accelerator efficiency | >50% | 51,9 % (48Ca+10 5 pµA)
4

## Slide 5
 | DC280 Parameter | Goals
1. | High injecting beam energy (up to 80 kV) | Shift of space charge limits for factor 30
2. | High gap in the center | Space for long spiral inflector
3. | Low magnetic field | Large starting radius. High turns separation. Low deflector voltage
4. | High acceleration rate | High turns separation.
5. | Flat-top system | High capture. Single orbit extraction. Beam quality.
DC280. Parameters and Goals

## Slide 6
To ensure optimal injection conditions for all range of accelerated ions, two versions of the inflector type A and type B with two magnetic radii of 7.5 and 9.2 cm are used.
Magnetic field Dependence of injection voltage.
The work diagram of DC-280 cyclotron with marks of tested regimes is presented on Fig.2. The cyclotron has shown reliable and highly effective work.
DC-280 description
6

## Slide 7
Magnetic structure of DERIS-PM.
1÷5 – PM rings; 6. 7 – soft iron rings;
8÷11 – soft iron plates;
12÷14 - auxiliary elements;
15 – hexapole; 16 – coil.
DECRIS-PM
(14 GHz)
7

## Slide 8
DECRIS PM Producing of 48Ca
How we can see from the spectrum obtained from the ECR source, ions with charge +7, +10 don’t have impurities. Due to the lower consumption, 48Ca+10 was chosen for experiments on the synthesis of superheavy elements.

## Slide 9
Chart: 
| 9.9999999999999992E-2 | 0.106944444444444 | 0.113888888888889 | 0.120833333333333 | 0.12777777777777799 | 0.13472222222222199 | 0.141666666666666 | 0.148611111111111 | 0.155555555555555 | 0.15625
Beam stability | 1.709 | 1.7396 | 1.709 | 1.6785 | 1.7185 | 1.6748 | 1.709 | 1.7701 | 1.7806 | 1.7701
Beam stability is about 1-3%.
Calcium consumption ~0,2-1,5 mg/h
Producing of 48Ca
I,puA
9

## Slide 10
Producing of 48Ca
Chart: 
| IFC1 | IFC2 | IFC3 | RP2_263 | RP2_300 | RP2_400 | RP2_500 | RP2_600 | RP2_700 | RP2_800 | RP2_900 | RP2_1000 | RP2_1100 | RP2_1200 | RP2_1300 | RP2_1400 | RP2_1500 | RP2_1600 | RP2_1700 | RP2_1770 | T0FC2
70mkA | 1 | 0.96178 | 0.90876 | 0.69284 | 0.6834 | 0.66296 | 0.65067 | 0.65083 | 0.64843 | 0.63897 | 0.63545 | 0.63516 | 0.63644 | 0.63573 | 0.63658 | 0.63447 | 0.63362 | 0.63079 | 0.61487 | 0.60893 | 0.45776
100mkA | 1 | 0.9604 | 0.92673 | 0.71881 | 0.70495 | 0.67822 | 0.66931 | 0.66832 | 0.66535 | 0.65545 | 0.65347 | 0.65248 | 0.65248 | 0.65248 | 0.65248 | 0.65248 | 0.6505 | 0.64752 | 0.63267 | 0.62673 | 0.48317
150mkA | 1 | 0.94604 | 0.89138 | 0.67975 | 0.66854 | 0.64541 | 0.62859 | 0.62789 | 0.62369 | 0.61317 | 0.61317 | 0.61317 | 0.61317 | 0.61317 | 0.61177 | 0.61037 | 0.60827 | 0.60687 | 0.59145 | 0.58444 | 0.42397
240mkA | 1 | 0.95426 | 0.79002 | 0.54137 | 0.53347 | 0.5106 | 0.48815 | 0.48482 | 0.4815 | 0.4657 | 0.4632 | 0.4632 | 0.4632 | 0.4632 | 0.4632 | 0.46195 | 0.46154 | 0.45863 | 0.44782 | 0.43992 | 0.29566
The total efficiency of transporting the ion beam of 48Ca10+ from the vertical part of the injection to the transport channel is about 50%.
10

## Slide 11
On the vertical, with an increase in the intensity from the ion source to 240 μA, we observed a deterioration of the beam transmission through the spherical deflector (Bender) from 94.22% at 150 μA to 79% at 240 µA, and the capture in acceleration decreased from 69% to 67%, respectively. This may be due to an increase in the space charge of the beam or the tuning of the accelerator as a whole.
Ion | Energy (MeV) | Intensity (pµA) |  |  |  | 
 |  | Axial injection |  | cyclotron |  | Transport channel
 |  | after separation | vertical part | R=400 | R=1770 | 
48Ca+7 | 240 | 10,9 | 9,8 | 6,9 | 6,1 | 5,2
48Ca+10 | 240 | 9 | 8,1 | 5,58 | 5,1 | 4,7
48Ca+10 | 240 | 23 | 19 | 12,8 | 10,6 | 7,1
Ion | Energy (MeV) | Efficiency |  |  |  | 
 |  | axial injection | capture | cyclotron | extraction | Total
48Ca+7 | 240 | 90% | 71% | 88% | 85% | 48%
48Ca+10 | 240 | 90% | 69% | 91% | 91% | 51%
48Ca+10 | 240 | 82% | 67% | 83% | 67% | 31%
Producing of 48Ca
11

## Slide 12
Producing of 48Ti
The ions of 48Ti with a charge of +7, +10 do not have impurities and we can use them in experiments on the synthesis of SHE.
Compound (CH3)5Ti(CH3)3.
12

## Slide 13
Chart: 
| IFC1 | IFC2 | IFC3 | RP2_263 | RP2_300 | RP2_400 | RP2_500 | RP2_600 | RP2_700 | RP2_800 | RP2_900 | RP2_1000 | RP2_1100 | RP2_1200 | RP2_1300 | RP2_1400 | RP2_1500 | RP2_1600 | RP2_1700 | RP2_1770 | T0FC2
48Ti10+ | 1 | 0.92738 | 0.85869 | 0.6201 | 0.59348 | 0.56808 | 0.55301 | 0.5518 | 0.55141 | 0.54849 | 0.54544 | 0.55063 | 0.55262 | 0.55739 | 0.54427 | 0.5522 | 0.54111 | 0.54903 | 0.53116 | 0.52679 | 0.39024
48Ti7+ | 1 | 0.9296 | 0.70339 | 0.51738 | 0.50222 | 0.50406 | 0.50044 | 0.49791 | 0.48954 | 0.47806 | 0.47451 | 0.47362 | 0.47178 | 0.46905 | 0.46709 | 0.46569 | 0.46322 | 0.45757 | 0.457 | 0.45148 | 0.43125
Producing of 48Ti
The beam of 48Ti+10 from ECR source with intensity is about 2.5 pµA and 48Ti+7 with intensity is about 3.14 pµA were obtained and accelerated with intensity 1,0 pμA and 0,93 pμA respectively. The total efficiency of transporting the ion beam of 48Ti10+,7+ from the vertical part of the injection to the transport channel is about 40-45%.
13

## Slide 14
Producing of 52Cr
The ions of 52Cr with a charge of +7, +8, +10 do not contain impurities, but we cannot accelerate ions with a charge of +7 and +8 to the energy required for the experiment.
C10H10Cr
14

## Slide 15
Chart: 
| IFC1 | IFC2 | IFC3 | RP2_263 | RP2_300 | RP2_400 | RP2_500 | RP2_600 | RP2_700 | RP2_800 | RP2_900 | RP2_1000 | RP2_1100 | RP2_1200 | RP2_1300 | RP2_1400 | RP2_1500 | RP2_1600 | RP2_1700 | RP2_1770 | T0FC2
Iecr=4,7puA; Pecr=281W; I=1,76 pua | 1 | 0.86526 | 0.79922 | 0.55395 | 0.54366 | 0.52069 | 0.5104 | 0.50932 | 0.50953 | 0.50504 | 0.50567 | 0.50504 | 0.5016 | 0.50118 | 0.48079 | 0.47307 | 0.46642 | 0.46212 | 0.46299 | 0.46278 | 0.37224
Iecr=4,9puA; Pecr=135W; I=1,8 pua | 1 | 0.92441 | 0.8099 | 0.62168 | 0.60098 | 0.56943 | 0.54814 | 0.54814 | 0.52622 | 0.52253 | 0.51905 | 0.51987 | 0.52028 | 0.51885 | 0.51536 | 0.51085 | 0.50697 | 0.50451 | 0.50348 | 0.50328 | 0.35841
Iecr=7,0puA; Pecr=298W; I=2,4 pua | 1 | 0.86306 | 0.72193 | 0.51435 | 0.49819 | 0.48595 | 0.45625 | 0.44644 | 0.44962 | 0.43722 | 0.43635 | 0.43808 | 0.44083 | 0.43348 | 0.41977 | 0.41242 | 0.40926 | 0.413 | 0.4133 | 0.40681 | 0.33906
Iecr=7 puA; Pecr=235W; I=2,33 pua | 1 | 0.828 | 0.73535 | 0.4925 | 0.48441 | 0.47113 | 0.4658 | 0.46638 | 0.46594 | 0.46552 | 0.46479 | 0.4645 | 0.46552 | 0.46162 | 0.41126 | 0.44214 | 0.43796 | 0.44011 | 0.43074 | 0.43866 | 0.33051
Iecr=6,3puA; Pecr=172W; I=2,6 pua | 1 | 0.90665 | 0.82911 | 0.59968 | 0.57437 | 0.56329 | 0.53956 | 0.54589 | 0.54272 | 0.54589 | 0.53956 | 0.5269 | 0.53639 | 0.53956 | 0.53481 | 0.53006 | 0.52848 | 0.52057 | 0.51266 | 0.51108 | 0.41456
Producing of 52Cr
The beam of 52Cr+10 from ECR source with intensity is about 6,3 pµA and accelerated with intensity 2,6 pμA. We can see, that efficiency of acceleration worsen then we increase power input to ECR source.
The total efficiency of transporting the ion beam of 52Cr10+ from the vertical part of the injection to the transport channel is about 50%.
15

## Slide 16
The beams of 48Ca7+,10+,48Ti+7,+10 and 52Cr10+ were accelerated and extracted from the DC-280 to the beam transport channel.
Maximum intensity of accelerated 48Ca ion beam is 10,6 pμA and 7,1 pμA were extracted.
The efficiency of acceleration for 48Ca is about 50 %. The beam is given to the GNS-2 experimental setup for a series of test experiments.
The beams of accelerated 52Cr10+ and 48Ti7+,10+ ions with intensity 2,6 pμA and 1 pμA respectively were extracted from the DC-280 to the beam transport channel.
The efficiency of acceleration for 52Cr10+ and 48Ti7+,10+ is about 40-50 %.
For the the ion beam of 48Ti and 52Cr the intensity is limited by ion current from ECR source. We work to improve of the method of ion production and optimize the ECR source work mode.
CONCLUSION
16

## Slide 17
Flerov Laboratory of Nuclear Reactions , JINR
THANKS
FOR YOUR
ATTENTION !