## Slide 1: Budker Institute of Nuclear Physics, Novosibirsk, Russia
ACCELERATORS OF ELV SERIES: CURRENT STATUS AND FURTHER DEVELOPMENT.
D.S. Vorobev, E.V. Domarov, M.G. Golkovskii, Y.I. Golubenko, A.I. Korchagin, D.A. Kogut. N.K. Kuksanov, A.V. Lavrukhin, R.A. Salimov, A.V. Semenov, S.N. Fadeev. P.I. Nemytov

## Slide 2
The Budker Institute of Nuclear Physics of Russian Academy of Science are developing and manufacturing of electron accelerators of the ELV-type for their use in the industrial and research radiation-technological installations beginning 1970. The ELV-type accelerators were designed with use of the unified systems and units enabling thus to adapt them to the specific requirements of the customer by the main parameters such as the energy range, beam power, length of extraction window, etc.
Due to high power of electron beam in wide energy range, high efficiency of conversation of electricity power to electron beam power and simple procedure of accelerator control by operator ELV accelerators are the most popular Russian accelerator. They are well known in the world, especially in China and South Korea. By now, more than 200 accelerators have been delivered both within Russia and abroad. .
http://www.inp.nsk.su/sites/promusk/eng

## Slide 3: Placements of ELV Accelerators
• 50 accelerators were delivered inside of former USSR
• more then100 accelerators were delivered in China
• 19 accelerators were delivered in South Korea
• 2 accelerators were delivered in Japan
• 2 accelerators were delivered in Poland
• 7 Accelerators were delivered in Germany, Chech Republic, Malaysia, Phillipines, Turkey
• 4 Accelerators were delivered to India.
Cable handling system for ELV accelerator in China
Cable irradiation factory (Kolchugino, Russia)
ELV accelerators are operating at LG cable Korea
2 In & 2 Out wires treatment by one ELV accelerator in JSC "Electrocable Works, Kolchugino" Speed of each line – 400 m/min
http://www.inp.nsk.su/sites/promusk/eng

## Slide 4: Accelerator design
The composition includes: Automated control system, Power supply, Gas system, Water cooling system

## Slide 5: Parameters of the ELV Accelerators
BINP proposes a number of electron accelerators of the ELV-type covering the energy range from 0.4 to 3 MeV with a beam of accelerated electrons of up to 130 mA and maximum power of up to 100 kW. Special case is 1 MeV 400 kW beam power electron accelerator ELV 12. High energy efficiency of accelerator is 60- 80%. All models have similar concept but differ in overall dimensions, length of accelerator tube, and the number of high-voltage rectifying sections. This makes it easy to adapt accelerators to the requirements of technology. Accelerators are continuously modified while saving the modification. So the power of the ELV-4, ELV-6, ELV-8 accelerators was increased to 100 kV. The system of automated control of accelerators and communication with technological lines is constantly developing.
 | Energy range, MeV | Beam power, kW | Maximum beam current, mA
ELV-0.5 | 0.4-0.7 | 25-65 | 50-130
ELV-1 | 0.4-0.8 | 25 | 50
ELV-3 | 0.5-0.7 | 50 | 100
ELV-4-1,5 | 1.0-1.5 | 100 | 67
ELV-4-1 | 0,8-1 | 100 | 100
ELV-6 | 0.8-1.2 | 100 | 100
ELV-6M | 0.75-0.95 | 160 | 200
ELV-8 | 0,8-2.5 | 100 | 50
ELV-12 | 0.6-1.0 | 400 | 500
ELV-15 | 1,5-3,0 | 100 | 50
http://www.inp.nsk.su/sites/promusk/eng
Notes: Надо сказать, что мы можем создать ускоритель под любые требования заказчика. Далее рассмотрим наиболее интересные из последних разработок

## Slide 6: ELV-15 Accelerator
Figure 1 - Rectifiers ELV-8 (left) and ELV-15 (right)
1 - vessel; 2 - primary winding; 3.4 - magnetic circuits; 5 - rectifier sections; 6 - accelerating tube; 7 - injector control unit; 8 - high voltage electrode; 9 - optical channels for injector control; 10 - primary winding terminals.
4500
3800
ELV-8 has an energy range from 0.8 MeV to 2.5 MeV, a beam current of 50 mA, and a power of 100 kW.
ELV-15 has an energy range from 1,5 MeV to 3 MeV, a beam current of 50 mA, and a power of 100 kW.
Notes: ELV-15 is the newest model of ELV. It was developed due to many requests of accelerators users. 80 исправить на 81

## Slide 7: ELV-12 Accelerator
http://www.inp.nsk.su/sites/promusk/eng
The energy range from 0.6 to 1 MeV. Beam current 500 mA. Beam power 400 kW.
Notes: ELV-12 was developed enough time ago. This a good machine that proved their possibilities for ecology. But up to now we nave no orders for these machines.

## Slide 8: Reaction hall ELV-12 accelerator in Dyetec (Taegy)
http://www.inp.nsk.su/sites/promusk/eng

## Slide 9: ELV-12 Accelerator
Irradiation treatment process. luminescence of water during irradiation.
http://www.inp.nsk.su/sites/promusk/eng

## Slide 10: Local shield accelerator ELV-0.5
ELV-0.5 Accelerator, 0.5 MeV x 130 mA, Taiyuan, China.
The radiation shield is open and the extraction device is visible.
http://www.inp.nsk.su/sites/promusk/eng
The window extraction device for ELV-0,5.
The accelerator in local radiation protection is also a new direction. They are especially attractive for the irradiation of films and tape materials, including industrial rubber goods.
Notes: В подписи к рисунку добавить, что радиационная защита открыта и видно выпускное устройство

## Slide 11: Mobile Accelerator (EB-Tech, South Korea)
• 20 kW mobile accelerator
• 30 mA beam current
• 0.7 MeV Energy
• All equipment in two trailers
• Waste water and gas treatment
http://www.inp.nsk.su/sites/promusk/eng
Notes: These accelerators have small amount of orders. Main purpose of them is demonstration af advantage of radiation texchnoligies.

## Slide 12: Additional possibilities
Usually, double-side irradiation of wires and cables is used. However, big size cables required high-energy accelerators. To reduce electron energy and improve the absorbed dose azimuthal inhomogeneity, four-side and ring irradiation systems were developed in BINP.
The calculated distribution of the absorbed dose of the cable in azimuth and depth at 2-sided, 3-sided, 4-sided and circular irradiation.
For four-sided irradiation with a given insulation thickness (depending on the outer diameter of the wire, and especially for wires of large cross section), the required electron penetration depth is 2-4 times less than for bilateral irradiation, which leads to a decrease in the required electron energy by 1.5-2.5 times . This greatly simplifies and reduces the cost of the accelerator used.
http://www.inp.nsk.su/sites/promusk/eng

## Slide 13: 4-side irradiation system
The operation principle relies upon deviation of an electron beam by a magnetic field. The electron beam being accelerated pass thru scanning system results to forming rectangular raster. Further being effected by constant transversal field of turn magnets electron beam deviated on some angle (see Fig. 1 ). Shape of magnet's poles and a magnetic field force are selected so that the electrons deviated on an angle of 45° symmetrically of the extraction device axis, with irrespective of a place of an entrance. Being transported through an irradiation zone a cable orientation is changed for 180° on each pass, thus four-sided irradiation is occur (see Fig.2).
Fig.1. Schematic diagram of the four-sided irradiation system: 1 - scanner system together with shift magnet; 2 - extraction chamber; 3 - electron trajectories; 4 - turned magnet; 5 - extraction window; 6 - irradiation area.
Fig.2. Principle of fore sides irradiation
http://www.inp.nsk.su/sites/promusk/eng

## Slide 14: Ring irradiation system
Treatment of large cables (up to 60 mm in diameter) can be done by using the ring irradiation system. Cable is passing only 1 time through irradiation area
http://www.inp.nsk.su/sites/promusk/eng
Notes: Cable is passing only 1 time through irradiation area. Это устройство является дополнительным к стандартному ускориелю. Так на рисунке показано не только система кольцевогооблучения, но и магниты 4-х сторонней системы, котроая в данном случае не используется.

## Slide 15: Main application of ELV Accelerators
• Modification of polymer products
• Modification of the polyethylene insulation for the production of thermoresistant wires and cables 0.5-120 mm2 with the capacity of up to 200 m/min
•The production of heat shrinkable pipes, films and bands with the capacity of up to 1000 kg/h
•The production of prepregand gel
•The production of artificial leather and rubber-technical products with the capacity of up to 1000 m/h
•Curing lacquer-paint coatings on different bases for the building industry of up to 500 m2/h
http://www.inp.nsk.su/sites/promusk/eng

## Slide 16: Concentrated beam extraction to atmosphere
Accelerator parameters: Energy 1.4 MeV, Beam current 50 mA, Beam power 70 kW. The beam diameter at the exit from the extraction device is 2,5 mm.
http://www.inp.nsk.su/sites/promusk/eng
Notes: There is special modified design of extraction device for focused beam/ Вообще говоря рисунки непонятны.

## Slide 17: Producing of SiO2 nano-powder
Evaporation of quartz sand
Productivity – tens killograms per hour
http://www.inp.nsk.su/sites/promusk/eng
Notes: Результаты экспериментов по производству. Не натуральный, кварцевый

## Slide 18: HECToR (Helmholtz-Zentrum Dresden, Germany)
ELV accelerators are widely used for scientific purposes. For example High Energy Computed Tomography Scanner In Helmholtz-Zentrum Dresden-Rossendorf (Germany, Dresden)
http://www.inp.nsk.su/sites/promusk/eng
Notes: Надо найти правильное название центра и статью. Где про это написано

## Slide 19: Collaboration with Shanxi Yitaike Electrical Equipment
Taiyuan, China
27 accelerators are installed in China
Full set (Shield design, Accelerator, Technology line)
http://www.inp.nsk.su/sites/promusk/eng

## Slide 20: Collaboration with EB-Tech
20 accelerators are delivered to customers in South Korea, China, Turkey, Malaysia
http://www.inp.nsk.su/sites/promusk/eng

## Slide 21
We are ready for collaboration.
Thank you for attention!
http://www.inp.nsk.su/sites/promusk/eng