## Slide 1: Status of Forward Hadron Calorimeter (FHCal)
A.Ivashkin
Institute for Nuclear Research RAS, Moscow
on behalf of the FHCal group
7th MPD collaboration meeting, Apr., 2021.
FHCal structure;
FHCal modules;
Front-End-Electronics and readout;
Detector Control System;
Energy calibration;
FHCal in trigger;
Integration to MPD;
Summary.

## Slide 2
FHCal
Two arms of hadron calorimeter at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules.
~1x1 m2 each part.
Beam hole 15x15 cm2.
Lead/scintillator sampling calorimeter.
Longitudinal segmentation;
Light readout- WLS-fibers;
7 sections/photodetectors in each module.
Structure of FHCal
FHCal modules

## Slide 3
The centrality of the collision;
The reaction plane orientation;
Physics in forward rapidity;
Minimum bias trigger.
Tasks: detection of spectators to measure:
X
Centrality:
2D-Fit of energy distributions in FHCal modules
E_max [a.u]
Edep [a.u]
central events
peripheral events

## Slide 4
All (90+spare) FHCal modules are assembled and are used for the tests.
100 Front-End-Electronics (FEE) boards are produced and tested.
The activities with modules:
Tests with cosmic muons;
Tests of Front-End-Electronics (FEE);
Study of FEE electronic noises;
Development of FHCal trigger;
Development of Detector Control System.
Status of FHCal modules

## Slide 5
Energy calibration with cosmic nuons and light yield of FHCal modules
Light yield depends on WLS-fiber length.
Average light yield for MIP’s in longitudinal sections.
New MPPC type
Clear amplitude spectra from cosmic muons allow the energy calibration in self-triggering mode (without external muon trigger).
This is due to high light yield in the longitudinal sections in modules.
~5 MeV
Light drops for ~40% for 1m fiber.
Corrected to pass length in scintillators.
Raw spectrum

## Slide 6
Front-End-Electronics
Two PCBs in each module with:
7 photodetectors ;
Photodetectors – MPPCs;
two-stage amplifiers;
HV channels;
LED calibration source.
100 units of FEE were produced and tested. A few units were repaired.
MPPC: S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
MPPC: new type
S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
Similar FFE is tested in FHCal at BM@N.

## Slide 7
Detector Control System for FHCal
DCS Tasks:
Control of HV at photodetectors (MPPC’s);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
Software:
Test version (full functionality) is ready.
New (advanced) python version is almost ready.
  Provide TANGO bindings
  Faster operation with multiple System Modules
LAN
FEE
Database
FHCal New Slow Control (proxy)
General Slow Control
System Module
System Module
FEE
FEE
FEE
FEE
FEE
RS485
Connection diagram

## Slide 8
noise
signal
Readout of FHCal
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
To minimize the length of signal cables, ADC’s will be placed around FHCal.
Shape of digitized signal.
muon signal
Noise signal
Fit function:
Prony method of fit
Fit of waveforms and suppression of noises allow the identification of low (~MeV) signals.

## Slide 9: ADC positions around FHCal
Variant-I
Variant-II
ADC boxes are placed at the rear side of FHCal modules
ADC boxes are placed at the lateral sides of FHCal support
Two halves of FHCal.

## Slide 10: Diagram of FHCal readout
FEE
FEE
FEE
1
2
44
…
on detector
ADC64 (1)
(9 modules)
ADC64 (2)
(9 modules)
ADC64 (5)
(8 modules)
…
near detector
Left (Right) FHCal arm
HVsys
DCS Control box
Wiener MPOD power supply
signal cables
General Control System (Tango)
- Ethernet
DAQ
5 Ethernet
5 lemo (trigger)
5 lemo (XOR)
5 lemo (WR)
~20m cables
Both FHCal arms have the same readout scheme.

## Slide 11: FHCal in trigger
Dependence of trigger efficiency on the energy threshold and on the number of modules.
Events with energy deposition in each central module > 5 MeV.
Total trigger efficiency ~97.7%.
Can we measure total cross-section?
In peripheral collision the energies are mainly deposited in central modules.
In the simplest case only the central modules can be used in trigger.

## Slide 12: Main FHCal construction elements
Распорка
Пластина
Support frame in magnet pole
Наружный фланец
Каркас
Basket of FHCal modules
Outer table

## Slide 13: FHCal installation into magnet pole
Main problem: beam pipe between two FHCal halves
Table with FHCal near pole
FHCal shifted into pole
Two FHCal halves compressed together
Design of FHCal support is in progress!

## Slide 14
Summary
All FHCal modules are assembled.
Each module was characterized with cosmic muons.
FEE was produced and tested.
Detector Control System is in final stage of development.
Energy calibration procedure is well developed.
The FHCal readout (ADC64 and mechanics) are in preparation.
The mechanical platform is under design now.
FHCal trigger is to be simulated and tested more accurately.

## Slide 15
Thank you!

## Slide 16: Hadronic showers in FHCal modules (beam tests).
Selection of beam muons for calibration.
Longitudinal shower profile.
Dependence of energy resolution on number of longitudinal sections.
Only stochastic term in resolution.
No constant term.