## Slide 1: Upgrade of the CMS Detector Project for 2022-2026
1
JINR Topic 02-0-1083-2009/2023
“CMS. Compact Muon Solenoid at the LHC”
21 June 2021. 55th Meeting of the Programme Advisory Committee for Particle Physics
Project leader: V.Yu. Karjavin
Scientific leader: I.A. Golutvin

## Slide 2
2
44 participants from JINR
23 participants from JINR member-states
Participants of Projects
Authors:
from JINR: 16 paid and 5 unpaid (4 PhD and 1 emeritus)
from JINR member-states: 6 paid

## Slide 3
3
JINR in CMS Collaboration
94 publications with contribution of JINR physicist's (since 2017):
13 CMS public paper in scientific journals (of more than 510 CMS papers in total)
18 CMS notes with physics analysis
6 CMS operation and upgrade notes
22 papers in peer-reviewed journals
35 articles with reviews of CMS results and on future physics
More than 70 reports at international conferences on the CMS project
Over 25 years JINR has been participated in the CMS experiment at the LHC, starting the very beginning of the detector concept development
Within the RDMS Collaboration JINR bears responsibility for the design, construction, commissioning, operation and upgrade of the Endcap Hadron Calorimeters (HE) and
Forward Muon Stations (ME1/1)
JINR scientists play active role in the CMS Physics programme. They contribute actively to the data taking and processing, data analysis for the purpose of obtaining new physics results

## Slide 4
4
LHC Schedule
LHC proton-proton collisions started in 2009
In Run 1 ﬁrst 2 years 2010–2012 LHC operated at 7 TeV, delivering integrated luminosity ≈6 fb−1, in 2012 energy was increased to 8 TeV, delivering ≈ 23 fb−1. Higgs boson discovery
Run 2 started in 2015 at 13 TeV with instantaneous luminosity 1.7×1034cm−2 s−1 (exceeded the design value). Physics tasks: detailed studies of the Higgs boson, standard model (SM) processes and searches for physics beyond the SM
During LHC Long Stop periods LS1 (2013−2015) and LS2 (2018−2021) the CMS detector is upgraded to facilitate an effective operation of all subsystems at high luminosity of 12×1034 сm-2 s-1 in pp−collisions at the LHC energy 14 TeV
After long shutdown LS3 in 2027 LHC start with HL-LHC operational mode with instantaneous luminosity (5-7.5)×1034cm−2 s-1. By 2030 LHC will deliver integrated luminosity ~3000 fb−1
we are here…
project
completion

## Slide 5
5
HL-LHC Physics Goals (1)
The main goal of the HL-LHC is to make New Discoveries
Detailed study of the Higgs boson (width, branchings, couplings, rare decays)
Looking for new scalar states of extended Higgs sector
Wide searches for physics beyond the SM (dark matter candidates, supersymmetry, TeV-scale gravity, extended gauge sector, etc.)
Precision tests of the SM, including rare processes
Higgs Projections for 300 fb-1 and 3000 fb-1
Higgs boson, the coupling constants to the SM particles will be measured with a precision of 5–14% and 2–10% given the integrated luminosities of 300 and 3000 fb–1 , respectively
New resonances in Hi-mass Dilepton States
Dark photons decaying to displaced muons
HL-LHC will provide the enough statistic for extending physics scenarios
which can be tested with CMS:
for new resonances up to mZ’ ~ 6.2-7 TeV (~ 4.56-5.15 TeV with RUN2 data)
dark photon masses (1−30 GeV) and lifetimes cτ = (0.01−10) m in the context of Dark Supersymmetry models.

## Slide 6
6
HL-LHC Physics Goals (2)
LHC produces many Long Lives Particles (LLP) with MeV - TeV masses with signatures involving displaced vertexes. Such states can not be discovered with existing CMS detectors configuration, they have to be reconstructed from outside the tracker volume in calorimeters and in muon system
The capability of the upgraded detectors give possibility of
a dedicated Level-1 triggering for displaced objects
HL-LHC physics aims to study reactions initiated by Vector Boson Fusion (VBF) and reactions with boosted objects giving narrow or merged jets (possible results of hadronic decays of the W and Z bosons, the Higgs boson, new Higgs states, and other new particles in the same mass range).

## Slide 7
7
HGCal Impact on Physics
Vector Boson Fusion (VBF) jet reconstruction and tagging efﬁciency comparing Run 2 (pileup 25) simulation to the upgraded Phase-2 detector with 0 and 200 pileup events.
Higgs VBF Production
Electron Selection Efficiency (~100%)
Jet response resolution
Primary vertex (PV) reconstruction efﬁciency
At the HL-LHC conditions with high pile-up (~200) HGCal will provide high effective registration of physics objects (electrons, jets) and primary vertexes

## Slide 8
8
HL-LHC Requirements for Calorimeter Systems
At HL-LHC Integrated luminosity will became 3000 fb-1, posing signiﬁcant challenges to radiation tolerance of detectors and pileup
- Fluence ~1016 n/cm2
- Integrated dose ~2 MGy
Dose of ionizing radiation
Fluence (1 MeV equivalent neutrons)
The existing endcap electromagnetic calorimeter (EE) - based on the lead tungstate crystals (PbWO4) and the hadron calorimeter (HE) - based on plastic scintillator- were designed for integrated luminosity of 500 fb−1
The High Granularity Calorimeter (HGCal) is
designed to replace the existing endcap calorimeters
Main design requirements for HGCal :
radiation tolerance
dense calorimeter structure in order to simplify two shower separation and the observation of narrow jets
longitudinal granularity to provide a good electromagnetic energy resolution, pattern recognition and discrimination against pileup
time precision measurement of high energy showers

## Slide 9
9
Structure of the HGCal
Key Parameters (from TDR):
HGCal covers 1.5 < h < 3.0
(~640 m2 of silicon sensors, ~370 m2 of scintillators)
  6.1M Si channels, cell size: 0.5 or 1.1 cm2
  240k scintillator tile channels
  ~31000 Si modules (incl. spares)
  Full system maintained at -30oC
Electromagnetic calorimeter (CE-E):
Si, Cu/CuW/Pb absorbers, 28 layers, 25.5 X0 & ~1.7 l
Hadronic calorimeter (CE-H):
Si & scintillator, steel absorbers, 22 layers, ~9.5 l (including CE-E)
Longitudinal structure of the HGCAL
consists of 3 types of cassettes:
CE-E cassetts,
CE-H silicon sensor cassettes
CE-H mixed silicon/scintillator cassettes.
Active Elements:
Si sensors are used in high-radiation region CE-E and inner region of CE-H
SiPM-on-Scintillating tiles in low-radiation region of CE-H

## Slide 10
10
HGCal Composition
Silicon sensors in CE-E and CE-H
Front-end electronics on the modules
Readout and control through motherboards
The active detector consists of cassettes (300 or 600 sectors) with scintillators and silicon modules assembled on cooling plates
cooling plate
silicon modules
scintillator tile modules
CE-H Mixed layer with silicon
wafers and scintillation tiles
Mixed silicon-scintillator cassette
Layout of the silicon cassette
CE-H Cooling Plates
Material: Oxygen-free copper 6 mm sheets
1300x900 to 2300x1300
Stainless steel tube ⌀4 mm
Mass production in 2022–2024
  Total 546 plates to be delivered at CERN

## Slide 11
11
Cold-room facility
Insertion of the tray
Testing and diagnostic of multi-cassettes CE-E and CE-H
Up to 7 cassettes testing in cold environment simultaneously ( room cooled to -350 C)
The duration of tests of one cassettes batch is ~2 weeks including test with cosmic muons
Multi-cassette cold-room facility
Design, construction and assembly at CERN in 2021-2022
- Services and cables installation
- Development of cosmic test setup, DAQ, trigger and detector control
Operation in 2022-2025
µ
Test with cosmic muons
Cassettes
Monitor
Cold room

## Slide 12
12
JINR Responsibility in the HGCal Project
According to the Addendum 14 to the CERN-MoU-2019-009 JINR contribution:
production of CE-H cooling plates
(1210 kCHF)
purchase of silicon sensors
(700 kCHF)
purchase of SiPM photosensors
(200 kCHF)
According to the MoU CMS-2010-010 JINR contribution:
production of multi-cassette cold-room facility (90 kCHF)
testing and diagnostic of CE-H cassette in 2022-2025
assembly and commission of HGCal in 2023-2026
JINR has committed to participated in the HGCal project with total contribution of 2.2 MCHF in CORE
The Full Cost of the CMS HGCal Project is 67.127 MCHF

## Slide 13
13
Motivations for Endcap Muon system Upgrade
During LS2 period
MEx/1 stations:
ME1/1, ME2/1, ME3/1,ME4/1
Total 180 CSCs
HL-LHC conditions
Instantaneous luminosity х 5
Integrated luminosity х 10
Pileup х 5
HL-LHC at detectors level
L1 trigger rate х 7.5
L1 trigger latency х 10
DAQ bandtwidth х 10
Additional requirements to sustain work at high rates
to detectors, readout, DAQ
and trigger electronics
The main task of the Endcap Muon system Cathode Strip Chambers ( ME CSC) Phase 2 upgrade: modernization of CSC electronics on the inner rings Muon stations (MEx/1), where the rates is higher with respect to the outer stations

## Slide 14
14
JINR team participation in LS2 CSC upgrade
ME1/1 installation with Loading Machine
LS2 CSC cosmic test data for both Endcaps
are in good agreement
CSC upgrade infrastructure
Upgrade of the Endcap Muon system was performed in LS2 shutdown
Instead of initially planned LS3 because it will be extremely busy
Contribution of JINR in Muon System upgrade
during LS2 period :
Design and construction of 120 new Low Voltage
Distribution boards (LVDB-5)
Refurbishing with new electronics, installation and
commissioning of 180 cathode strip chambers (CSC)
Modernization of the ME1/1 CSC cooling system
Endcap Muon System upgrade infrastructure

## Slide 15
JINR Responsibility in the Muon Upgrade
The Full Cost of the CMS Muon Upgrade is 21.437 MCHF
JINR group participates in Muon CSC
R&D programme:
CMS CSC ageing study at GIF++
study of CSC characteristics in HL-LHC conditions with uncorrelated background.
study of methods for eliminating the Malter current in a cathode strip chamber
participation in the new gas mixture studies
development and test of an algorithms for track segments reconstruction in the CSC chambers
See details of Muon CSC R&D in backup slides
According to the Addendum №13 to the MoU CERN-MoU-2019-008 JINR contribute to CORE:
upgrade of the CSC electronics (76 kCHF)
RPC Upgrade Project (75 kCHF paid by Georgia Institutions)
15

## Slide 16
16
Upgrade Cost Summary
The CMS Phase II Upgrade Cost is 285 MCHF in terms of CORE value
The Phase II Upgrade Common Fund is established at the level of
25’000’000 CHF (twenty-five million Swiss Francs)
According to the Addendums to the Memorandum of Understanding for Collaboration in the Construction of the CMS Detector, JINR has following commitments in CORE (2020-2026):
participation in the Highly Granularity Calorimeter (HGCal) Project with total contribution of 2.2 MCHF
upgrade of the Endcap Muon system Cathode Strip Chambers (CSC) with total contribution of 76 kCHF (these obligations is nearly fulfilled)
Additional contributions:
contribution to Upgrade Common Funds of 289,855 kCHF in 2022-2026 (468.855 kCHF is in a total, 144.928 kCHF is already accounted for 2020-2021)
179 kCHF of operation expenses on technical maintenance of HGCal in 2022-2026 according to М&O_B

## Slide 17
17
Funding Requested for 2022–2026

## Slide 18
We are asking PAC
to give recommendation to open a new project “Upgrade of the CMS Detector”
for the period of 2022-2026.
Thank you for your attention!!!
18

## Slide 19
BACKUP SLIDES
19

## Slide 20
20
CSC ageing study R&D at GIF++
Equivalent to 3ˣHL-LHC periods of L=3ˣ3000 fb-1
the integrated charge to be:
ME1/1 - 0.33 C/cm
ME2/1(sect.1) - 0.24 C/cm
ME2/1
ME1/1
Main goal - to study will CSCs survive at HL-LHC of Lint=3000 fb-1?
14 TBq Cs137 source (Eγ = 662 keV)
D2: Total flux ~1.7*107 γ/(s*cm2)
2.4 m
3.3 m
beam
GIF++ Radiation field map
Tests at Gamma Irradiation Facility GiF++ :
1. CSC Ageing study.
2. Study of background rates influence on CSC performance
3. Study of methods for Malter current eliminating.
Longevity tests- monitoring CSC performance:
Dark rate/currents
Relative currents
Strip-strip resistance
Test beam measurements:
Efficiency
Spatial resolution
Gas gain

## Slide 21
21
Recent CSC ageing study results
ME1/1 Relative current Ilayer/Iref.
ME1/1 accumulated charge in time
CSC spatial resolution vs GIF++ Source intensity
for different values of accumulated charge
ME1/1 with the accumulated charge
ME2/1
ME1/1
With the HL LHC conditions
at L= 5x1034 Hz/cm2 the spatial resolution degradation:
10% for ME1/1
16% for ME2/1
No degradation observed

## Slide 22
22
Malter currents at CMS and GIF++
CMS p-p collisions:
One of the 6 CSC ME1/1 layers shows a current spike exceeding 30 µA followed by a long-time discharge. The current persists even after the LHC beams are dumped. The other layers show stable currents around 3 μA
HV training of the Spare ME1/1 layer 2 (blue) at GIF++
The current is produced by Cs-137 gamma source. As soon as the current disappeared, the voltage is raised manually by 5-10V. At some point Malter current disappears and no seen even at HV=3.0kV
Beam dump
Run2

## Slide 23
23
Track-segment reconstruction algorithm development
An example of the reconstruction of four overlapping signals on a single CSC layer
Green - simulated muon coordinate
Yellow - initial distribution of the signal
Blue - coordinate done with standard algorithm
Red – 4 overlapping cathode signals
recognized by the proposed algorithm
Development of a new
wavelet-based RecHits reconstruction algorithm
New CSC segment builder algorithm
Spatial residuals for muon track reconstruction
Red - new algorithm, Blue – standard algorithm showing 2.5 times bigger standard deviation than the new one
New algorithm customized
for ME1/1 geometry
Red- eliminated inefficiency in narrow part of the chamber (R=115 cm) and the area of ​​the strip cut (R = 150 cm) between the two parts of the CSC.
ADC
Strip number