## Slide 1
Development of high resolution TOF system
  Wang Yi
Department of Engineering Physics, Tsinghua University

## Slide 3
Main requirements for SoLID-TOF
The MRPC is developed for the TOF of SoLID
Main Requirements for TOF:
  /k separation up to 7GeV/c & 3 
  Time resolution < 20ps
  Rate capability : 20kHz/cm²
20ps

## Slide 4
4
Time requirement for MRPC and electronics
TOF <20 ps， the intrinsic resolution of narrow gaps MRPC is around 15ps，so the time jitter of readout electronics <13~15 ps。

## Slide 5
Intrinsic time resolution of standard MRPC
Electron multiplication
Time resolution:

## Slide 6
Intrinsic time resolution vs. gap number
When avalanche strength~28
The thinner gas gap, the better time resolution
The time will not be improved when gap number > 20
For time resolution <10ps. The width of gas gap should less than 160 m

## Slide 7
 | 1st MRPC | 2nd MRPC | 3nd MRPC
Width of gas gap (m) | 250 | 104 | 128
Number of gap | 6 | 4 x 8 = 32 | 4 x 8 =32
Electrode | Float glass | Float glass | Low resistive glass
Glass thickness (m) | 700 | 500 | 400
Readout strip | 7 mm +3 mm | 7 mm + 3mm | 5mm + 2mm
Close to real prototype !
Prototype design

## Slide 8
~ 35.6ps
Cosmic rays
E: 121 kV/cm
1st MRPC + TI amplifier + Lecroy Oscilloscope
Cosmic ray test

## Slide 9
3rd MRPC
2nd MRPC
Amplitude
3rd > 2rd
Base line noise
Comparison of 2nd and 3nd MRPC

## Slide 10
2nd MRPC + USTC FEE + Lecroy Oscilloscope
Voltage: ，Eff，Time resolution
Electric field：150 kV/cm
Performance of 2nd MRPC

## Slide 11
Analyisis with Neural network
ComLSTM (Combined LSTM)：FC combined with LSTM，
Network training：60k simulated data，Input is 10 points of leading edge,
=16.8ps

## Slide 12
Electric field：
140 kV/cm
3rd MRPC + USTC FEE + Lecroy Oscilloscope
Time resolution：20.8ps
Performance of 3nd MRPC

## Slide 13
Test at high rate environment

High rate test system
Working current and counting rate .vs. X-ray strength

## Slide 14
X-rays
55kV/0.55uA
Rate ~ 15 kHz/cm2
Time resolution
28.74 ps / √2
~ 20.32 ps
Performance at high rate environment

## Slide 15
Gas pollution at high rate environment
The MRPC3a (8 gas gaps, 250 μm gap width, active area 33*27.6cm2) was irradiated widely under X-ray in the lab. The operating current increased with a slope about 40 nA/h.
Box size: 60cm*60cm*20cm, flow rate: 100 mL/min
Reason: Gas pollution in gas gap
Read by TDC moniter

## Slide 16
Parameter | Value
N of gas gap | 2×5
Detector volume | 约350×350×50mm3
Width of gas gap | 0.25mm
Readout channel | 24 channels, 10mm strip width + 3mm gap，32 cm length
Signal readout | Differential, double-ended
Gas volume | ~170 ml
Strip impedance | ~42 Ω
The sealed MRPC has shown excellent air-tightness under low gas flow.
  4 ml/min “standard gas”： Freon/iC4H10/SF6 90/5/5
  1 ml/min pure Freon
  Bubble stably
  Serial chambers
Development of a sealed-MRPC

## Slide 17
10 mL/min individual gas supply for sealed prototype.
Standard gas mixture: Freon/iC4H10/SF6 90/5/5
300 mV PADI threshold.
Dark current: < 20 nA, Noise rate: < 1 Hz/cm2
Reasonable ToT, position resolution comparable to reference counters
Cosmic ray test

## Slide 18
Chart: I-counter (μA)
| 0.27083333333333331 | 0.29166666666666669 | 0.29167824074074072 | 0.30141203703703706 | 0.3014236111111111 | 0.30143518518518519 | 0.30144675925925929 | 0.30145833333333333 | 0.30146990740740742 | 0.30155092592592592 | 0.30157407407407405 | 0.3021064814814815 | 0.30453703703703705 | 0.30693287037037037 | 0.30694444444444441 | 0.3125 | 0.33333333333333331 | 0.35416666666666669 | 0.375 | 0.3908564814814815 | 0.39086805555555554 | 0.39087962962962958 | 0.39089120370370373 | 0.39090277777777777 | 0.39091435185185186 | 0.39099537037037035 | 0.3910763888888889 | 0.39152777777777775 | 0.39488425925925924 | 0.39489583333333328 | 0.39490740740740743 | 0.39491898148148147 | 0.3949421296296296 | 0.39523148148148146 | 0.3972222222222222 | 0.39811342592592597 | 0.39812500000000001 | 0.3981365740740741 | 0.39814814814814814 | 0.39815972222222223 | 0.39817129629629627 | 0.39818287037037042 | 0.39861111111111108 | 0.39905092592592589 | 0.4069444444444445
 | 4.99 | 4.985 | 7.08 | 7.08 | 5.71 | 1.08 | 0.15 | 0.07 | 0.05 | 0.04 | 0.035 | 0.03 | 0.03 | 0.03 | 8.57 | 8.58 | 8.58 | 8.59 | 8.585 | 8.585 | 6.38 | 0.3 | 0.1 | 0.06 | 0.045 | 0.04 | 0.035 | 0.03 | 0.03 | 8.45 | 8.61 | 8.63 | 8.62 | 8.61 | 8.615 | 8.61 | 5.6 | 0.82 | 0.18 | 0.07 | 0.055 | 0.045 | 0.035 | 0.03 | 0.03
X-ray started since 0:28:00
3.4K
(Hz/cm2)
4.3k
5k
OFF
OFF
OFF
Stable current for over 6h: 5->5.02->4.99μA
Performance of sealed-MRPC under X-ray
We did not observe obvious gas pollution effect!

## Slide 19
    Gain：26 dB~40 dB
    Band width：1.4 GHz
    Time jitter：4 ps
Nucl. Instrum. Meth. A 925 (2019) 53.
    SCA (DRS4)：1024 sampling capacitor
    Max sampling rate：5.12 GHz
    Noise：0.5 mV
    Time jitter：3 ps
Time digitizer (not ready)
Fast FEE by USTC
Fast amplifier and SCA digitizer

## Slide 20
FPGA-TDC
Time precision is about 10ps !

## Slide 22
Layout of MRPC-TOF
12 module for
one circle
Each module consists of
10 sealed MRPC

## Slide 23
End-cap MRPC-TOF
eTOF consists of 16 modules and each module consists of 3 sealed MRPC.

## Slide 24
MRPC description
Fast amplifier+ SCA
NINOs + FPGA TDC

## Slide 25
TOF system

## Slide 26
Advantage of sealed MRPC
Performance: fast gas exchange
Economy: save gas
Environmental protection

## Slide 27
Thanks for your attention !