## Slide 1: Барионная материя на Нуклотроне (BM@N)
Дмитрий Дементьев для коллаборации BM@N
ЛФВЭ ОИЯИ

## Slide 2: Outline
BM@N experiment at NICA;
Heavy ion program at BM@N;
Upgrade of the BM@N experiment;
Summary

## Slide 3: NICA Heavy Ion Complex
BM@N: beams from p to Au, heavy ion energy 1-3.8 AGeV, Au intensity up to 2 MHz
BM@N

## Slide 4: Baryonic Matter at Nuclotron Experiment
Dipole magnet with 6 (half) GEM tracking chambers and 3 Silicon stations inside
Drift chambers for tracking
mRPC Time-of-flight detectors
Forward hadron calorimeter
Neutron detector
Beam direction

## Slide 5: Heavy Ion program at BM@N
The research program of BM@N includes:
Scouting the location of transition between hadronic and partonic dominated matter;
Onset of deconfinement and chiral symmetry restoration;
Searching the critical endpoint of a possible 1st order phase transition at Nuclotron energies;
Exploring the high net-baryon density EoS for symmetric nuclear matter ;
Study of the ΛN, ΛNN, and ΛΛN interactions
4

## Slide 6: Study of the EOS of nuclear matter
Study of the EOS at densities above 2 may provide insight for the mass/density relation of neutron stars
T. Klaehn et al., Phys. Rev. C74: 035802, 2006. Update by D. Blaschke, priv. comm.
Observables sensitive to EoS:
  Collective flow (,
  Subthreshold particle production ( - ,- )
Ch. Fuchs and H.H. Wolter, EPJA 30 (2006) 5
Mass-density relation of neutron stars for different EOS

## Slide 7: Hypernuclei production in heavy-ion collisions
Maximum yield predicted for √s=3-5 GeV
Precision measurements of lifetime and mass of hypernuclei will shed light on the ΛN, ΛNN, and ΛΛN interactions
A. Andronic et al., Phys. Lett. B697 (2011) 203
BM@N

## Slide 8: BM@N upgrade for heavy ion collisions
New hybrid tracking system:
  4x stations of Silicon Tracking System (STS) with double-sided silicon microstrip sensors;
  7x planes of Gas-Electron-Multiplier chambers (GEM)
Vacuum beam pipe
Upgrade of the outer tracking system based on Cathode Strip Chambers
New Forward Hardron Calorimeter (FHCal) instead of ZDC
New hybrid tracker (STS +GEM)
Fall 2021 - start new experiments with Kr beams
2022+ -start experiments with heavy ion beams up to Au, Bi, Pb
FHCal

## Slide 9: GEM central tracker
7 upper GEM 163x45 cm2 chambers produced at CERN were integrated into BM@N
7 lower GEM 163x39 cm2 chambers were assembled, delivered to BM@N and tested
Photo of assembled GEM chamber
Material budget of GEM tracker
Two-coordinate GEM planes;
Stereo angle between strips: 15°;
Pitch: 0.8 mm
Setup of GEM detectors for cosmic tests
GEM team

## Slide 10: ʌ decay reconstruction in carbon beams with GEM tracker
experimental limitations of the first setup:
  low granularity of tracking systems (small S/B ratio);
  no vacuum beam pipe in BM@N (large background)
ʌ⇾p decay reconstruction in GEM + Si tracker in C+C interaction,
March 2017

## Slide 11: Silicon Tracking System
Technical solutions:
double-sided silicon microstrip sensors
  hit spatial resolution  25 µm
  material budget per tracking station:  0.3% – 2% X0
  radiation tolerance up to 1 × 1014 n/cm2 (1 MeV equivalent)
self-triggering front-end electronics, time-stamp resolution  12,5 ns
low-mass detector modules/ladders
The project is being implemented as a joint effort of CBM and BM@N STS teams under the GSI-JINR Roadmap Agreement
4 x STS stations
34 x Ladders
292 x Modules
STS Material budget
STS team
2022 – installation of the first two stations
2024 - commissioning of the full STS

## Slide 12: STS modules
N-side read-out
P-side read-out
cable stack: thickness ~ 800 µm / 0.23% X0
Performance:
noise: 1090 150 e (N-side); 1350 200 e (P-side);
r/o threshold: 7000 e;
signal-to-noise: 153 ;
hit detection eff.: > 95%;
STS module
Cable stack
Sensor
FEE
Module assembly at JINR
STS XYTER ASIC Tab-bonded
with micro-cables
STS team

## Slide 13: STS ladders
Mockup of the ladder
Measured deviations of X coordinates of the fiducial
marks on the sensors from the mean value.
Fiducial marks on sensors
Ladder assembly device
CF-truss with bearings
STS team

## Slide 14: Forward Hardon Calorimetr
Determination of:
Orientation of the reaction plane
Collision centrality
20 PSD CBM modules - transverse size
20x20 cm2, length 5.6 λint.
34 MPD/NICA like modules - transverse size 15x15cm2, length 4 λint.
FHCal is completely assembled and installed at the BM@N
Team of INR RAS, Troitsk
CBM modules MPD modules

## Slide 15: Beam pipe downstream the target
1 meter prototype of the BM@N carbon
beam pipe (DD “Arkhipov”)
Beam pipe is made of 1 mm thick carbon fiber;
Consists of four parts with a non-flange connectors;
FLUKA simulations have shown that the proposed beam pipe is well suited to guide the high intensity beam;
First vacuum tests have shown an insignificant leakage level of side surfaces of the sample, vacuum up to 10-5 Torr.
A. Senger, P. Senger, S. Piyadin,V. Spaskov, A.Kubankin

## Slide 16: Physics performance simulations of the tracking system
Ξ- and ΛH3 reconstruction in central Au+Au at 4A GeV
Generator: PHQMD (V. Kireyeu), 500k events, Au+Au at 4A GeV, b = 0-5 fm
Statistics:  2106 Λ ,  2104 Ξ-,  8.4104 ΛH3
Detectors: STS + GEMs + TOF
A.Zinchenko, M.Kapishin, I.Rufanov, V.Vasendina

## Slide 17: Short-Range Correlations (SRC) at BM@N
12C + p  2p + 105B + n (np SRC)
12C + p  2p + 104Be + p (pp SRC)
First fully exclusive measurement in inverse kinematics probing the residual A-2 nuclear system!
Experiment at BM@N with a 4A GeV C-beam:
k<kF Mean field region: Single nucleons
k>kF High momentum region: Correlated pairs of nucleons, which are close together in space with a high relative momentum, but a low c.m. momentum compared to the Fermi momentum kF. SRC probe nucleonic and partonic degrees-of-freedom in nuclear systems.

## Slide 18: Summary
Nuclotron energy range is well suited for the study of high density baryonic matter
BM@N is being upgraded in order to start experiments with heavy ion beams up to Au in 2022
Stages of BM@N experiment:
2021: beams of Kr and Xe;
2022: Au beams with max. intensity 0.5 MHz and trigger rate 10 kHz, installation of 2 stations of STS;
2023: Au beams with max. intensity 2 MHz and trigger rate 50 kHz;
2024: Installation of the full STS.

## Slide 19: СПАСИБО ЗА ВНИМАНИЕ!