## Slide 1: MRPC of SPD-TOF
Yi Wang
Tsinghua University

## Slide 2: Outline
Multigap Resistive Plate Chamber (MRPC)
MRPC: at the R&D frontier: high rate + high time resolution
MRPC for SPD-TOF
Conclusions

## Slide 3: Multigap Resistive Plate Chamber
First proposed by E. C. Zeballos
The multigap structure brings:
Narrow gap thus high time precision
Necessary gap thickness for good efficiency
MRPC has been broadly adopted to construct the Time of Flight (TOF) systems in HEP experiments.
 | ALICE | STAR | FOPI | BESIII | CBM | SoLID
Active area per detector (cm) | 120 x 13 | 22 x 8.4 | 90 x 4.6 | 0.5x(9.2+14.8)x32.8 | 33 x 27.6 | --
Total active area (m2) | 141 | 50 | 5 | 1.33 | 120 | 10
Pad size (cm) | 3.7 x 2.5 | 6.3 x 3.1 | 90 x 0.3 | (9.1~14.1) x 2.4 | 27 x 1.0 | (16~28) x 2.5
Gap×thickness(mm) | 10 x 0.25 | 6 x 0.22 | 6 x 0.3 | 12 x 0.22 | 10 x 0.25 | 10 x 0.25
Gas mixtures (C2H2F4/ C4H10/SF6) | 90/5/5 | 95/5/0 | 85/5/10 | 90/5/5 | 90/5/5 | 90/5/5
Operating field (kV/cm) | 96 | 107 | 110 | 109 | 110 | 106
Efficiency | 99.9% | 95-97% | 97±3% | 99% | 97% | 98%
Time resolution(ps) | 40 | 60 | 73±5 | 60 | 60 | 20 ps
Max rate (Hz/cm2) | 50 | 10 | 50 | 50 | 30k | 20k
In construction
Proposed
The next generation MRPC applications mark the higher counting rate and time precision.

## Slide 4: Expanding the MRPC rate capability
One must control the voltage drop (efficiency loss) when incident flux goes up.
Decrease the resistivity of the electrodes
With the low-resistive glass developed in Tsinghua, resistivity has decreased by 2 orders of magnitude.
(common float glass: 1012 Ωcm, low-resistive: 1010 Ωcm)
MRPC2 with low-resistive glass will be applied in CBM-TOF wall, and has been operating at FAIR-Phase 0 programs like STAR-eTOF and mCBM
Rate capability verified through beam test: 93%, 80ps@70kHz/cm2

## Slide 5: Towards a time precision < 20 ps
Simulation indicates proper ways to design the gap thickness and arrange the stacks
Besides the ‘intrinsic’ time resolution of the detector, it is also crucial to develop an advanced readout technique.
Time over Threshold (ToT) method
– Leading and trailing time
Waveform sampling technology
Nucl. Instrum. Meth. A 925 (2019) 53.
Fast-End Electronics:
Bandwidth: 1.4 GHz
Gain: 26-40 dB
Noise (NSD): < 1.5 nV/√Hz
Waveform Digitization:
Sampling freq.: 5 GS/s
Noise ampl.: 0.5 mV
Waveform provides detailed information of avalanche that allows more calibration methods.
An MLP neural network for position calibration
An LSTM model for signal leading edge recognition and time calibration
Narrower gap thickness required

## Slide 6: The high-rate high-resolution prototype
Parameter | Value
Gap thickness (mm) | 0.128
N of gaps | 4 x 8
glass | Low-resistive
Glass thickness(mm) | 0.4
Strip interval (cm) | 0.5 width + 0.2 gap
S0
S1
X ray source
Top MRPC
Bot MRPC
Two prototypes has been assembled and tested.
The high rate test is carried out by discriminating cosmic event in X-ray irradiation.
Counting rate
Current
Counting rate
Operating current
Current of X-ray source
Efficiency
Time resolution
Counting rate
Efficiency
Time resolution
~ 20 ps achieved at high rate!

## Slide 7: Gas-related challenges of MRPC
Regulations against greenhouse gases causes uncertainty:
availability, cost, eco-impact, …
Application with large area:
gas flow, cost, leakage, …
STAR-TOF (left) and CBM-TOF (right) detectors in gas boxes forming a module
Motivation: A wise design of the gas volume shall promote the gas exchange and decrease the gas consume.
Gas pollution effect in high rate conditions
Narrow gap of MRPC and large gas volume ---
ionization products exchanged slowly by diffusion
Pollution caused noise and current rise
…observed in HEP experiments and lab tests.
Constant rate condition of 1kHz/cm2

## Slide 8: Sealed MRPC
Gas tube
Inlet/outlet
Fishline hook
3D printed sealing frame with Good strength, insulation and radiation persistency
With the lateral side mostly enclosed, the counter itself becomes a gas box. The sealed design brings the features of:
1. Gas saving: 20 sccm/m2 gas flow with common practice
With cosmic ray test of a counter, 1 mL/min flow is examined with stable operation for the tested 24 days!

## Slide 9: Sealed MRPC
2. Promoted gas exchange
Excellent current behavior under high rate irradiation:
Stable current with constant rate condition.
Fast decay of dark current since when X-ray is off
Decrease the wait time of gas purging:
Reach the working HV in 2h since flowing the gas

## Slide 10: The real prototype for CEE-eTOF
Structure of sealed MRPC prototype
2 stack * 5 gas gap * 0.25mm
Float glass plates of 0.7mm width
32 channels, differential signal
2-end readout
Strip length 27cm, 7mm width+3mm gap
Sealed design, total gas volume ~170ml
Frame edge

## Slide 11: The super module with 4 MRPC
Noise level <0.5 Hz/cm2
Become better after long time training
Four MRPCs, total detection area  1m2
Working gas: Freon, 20sccm
HV: 6.5kV
Total dark current: 70nA

## Slide 12: Layout of SPD
Requirement for TOF system
PID : e few GeV at distance of 108cm
Time resolution: 70ps
Particle rate: 100Hz/cm2
Total area: 27m2

## Slide 13: Structure of barrel TOF
12 module for
one circle
Each module consists of
10 sealed MRPC

## Slide 14: Structure of end-cap TOF
eTOF consists of 16 modules and each module consists of 3 sealed MRPC.

## Slide 15: Fast amplifier+Pulse shape digitizer
    Gain：26 dB~40 dB
    Band width：1.4 GHz
    Time jitter：4 ps
Nucl. Instrum. Meth. A 925 (2019) 53.
    SCA (DRS4)：1024 sampling capacitor
    Max sampling rate：5.12 GHz
    Noise：0.5 mV
    Time jitter：3 ps
Time digitizer
Fast FEE by USTC

## Slide 16: Ninos + FPGA-TDC
Time precision is about 10ps !
Ninos Asic specifications

## Slide 17: Summary
Future HEP experiments calls for MRPCs with high rate capability and excellent time resolution.
Low-resistive electrodes help expand the rate capability.
Narrow gap width and advanced readout chain help improve the timing performance.
Prototype has been examined its 96% efficiency and 20 ps resolution at 20 kHz/cm2 rate condition.
MRPC faces gas related challenges which motivates an enhanced gas exchange.
Sealed MRPC with low gas volume can be used in SPD-TOF.
Thank you !