## Slide 1
Producing high intensity beams ions 48Ca, 48Ti, 52Cr, 54Cr at the DC-280 cyclotron
Andrey Protasov, Head of the Cyclotron DC-280

## Slide 2: Report concert:
Obtaining high ion intensities 48Са10+
Obtaining ions 48Ti10+
Obtaining ions 52Сr10+ and 54Cr10+
Plans for the first half of 2022

## Slide 3: Cyclotron DC-280

## Slide 4
Superheavy Elements (SHE) Factory – the Goals
Experiments at the extremely low (σ<100 fb) cross sections:
Synthesis of new SHE in reactions with 50Ti, 54Cr ...;
Synthesis of new isotopes of SHE;
Study of decay properties of SHE;
Experiments requiring high statistics:
Nuclear spectroscopy of SHE;
Study of chemical properties of SHE.
To carry out the scientific program, the DC-280 has to provide the following parameters of ion beams:
Ion energies (smooth variation) | 4 - 8 MeV/n
Ion masses | 10 - 238
Intensities (A~50) | >10 pµA
Efficiency of beam transfer from ion source to physical facility | >50%

## Slide 5
Ion | Energy (MeV) | Intensity (pmkA) |  |  |  |  | Efficiency (%) |  |  |  | 
 |  | Axial injection |  | Cyclotron |  | Transport channel |  |  |  |  | 
 |  | After separation | vertical part | R=400 mm | R= 1770 mm |  | Axial injection | Capture | Cyclotron | Extraction | Total
40Ar7+ | 195 | 28,7 | 24,7 | 17,1 | 14,2 | 10,4 | 86% | 69% | 83% | 73% | 36%
48Ca7+ | 240 | 10,9 | 9,8 | 6,9 | 6,1 | 5,2 | 90% | 71% | 88% | 85% | 48%
48Ca10+ (2021) | 240 | 24 | 19 | 12,8 | 10,6 | 7,1 | 82% | 67% | 83% | 67% | 31%
48Ti10+ | 244 | 2 | 1,9 | 1,4 | 1,25 | 1 | 92% | 72% | 92% | 83% | 50%
52Cr10+ | 250 | 6,3 | 5,2 | 3,56 | 3,23 | 2,62 | 83% | 69% | 91% | 81% | 42%
84Kr14+ | 496 | 3,1 | 2,8 | 1,7 | 1,6 | 1,4 | 91% | 60% | 93% | 92% | 47%
54Cr10+ | 270 | 5,9 | 5 | 3,7 | 3,2 | 2,54 | 85% | 73% | 87% | 79% | 43%
48Ca10+ (2022) | 240 | 20 | 17,6 | 12,4 | 11 | 7,7 | 87% | 70% | 88% | 71% | 38%
Efficiency of acceleration in cyclotron DC-280

## Slide 6: Obtaining high ion intensities 48Сa10+ in 2021
48Сa7+ | 5.17 pmkA
48Сa10+ | 7.11 pmkA
Efficiency of beam transmission 48Ca10+ at different initial currents from the DECRIS-PM ion source
The 48Ca iThe 48Ca ion spectrum, optimized for Ca10+
on spectrum, optimized for Ca10+

## Slide 7
Obtaining high ions intensities 48Сa10+ in 2022
iThe 48Ca ion spectrum, optimized for Ca10+
48Сa10+ | 7.73 pmkA

## Slide 8: Obtaining ions 48Ti10+
iThe 48Ti ion spectrum, optimized for Ti10+
Beam profile in the transport channel

## Slide 10
Obtaining ions 52Сr10+
iThe 52Cr ion spectrum, optimized for Cr10+

## Slide 12: Obtaining high ions intensities 54Сr10+
Axial injection |  | Accelerator |  | Transport channel | 
Beam current from the ECR source, µA | Beam current after the high voltage platform, µA | Beam current in the vertical part of the injection, µA | Beam current at a radius of 400 mm, µA | Beam current at the output radius of 1770 mm, µA | Current on the Faraday Сup T0FC2, µA
59,277 | 54,903 | 50,193 | 36,734 | 31,912 | 25,366
84,68 % |  |  |  |  | 
 |  | 71,19 % |  |  | 
 |  |  | 86,87 % |  | 
 |  |  |  | 79,49% | 
42,79 % |  |  |  |  | 
The 54Cr ion spectrum, optimized for 54Cr10+
beam profile in the transport channel

## Slide 13: Plans for the first half of 2022
January: obtaining maximum intensities of 48Ca ions
March: obtaining high intensities of 50Ti, 52Cr and 54Cr ions