## Slide 1
BM&N STS ladders assembly in VLHEP
Structure of the stations
Number and types of ladders & modules
Components, jigs & assembly procedures
Status of ladders assembly at LHEP.
Vladimir Elsha
JINR, LHEP
22.05.2017

## Slide 2
1. Supposed structure of the BM&N STS stations
Supposed four BM&N STS stations
Structure of stations based on Jochen Kunkel paper (1)
Stations 1 and 2 are assumed like “Station 0” by Kunkel
Stations 3 and 4 are assumed like “Station 1”
Number of ladders may be reduced for stations 1,2,3
But Station 4 supposed like full size “Station 1” by Kunkel
“Station 0” (2 pc)
“Station 1” (2 pc)
Anyway number of modules and ladders which is necessary for two “Station 0” and two “Station 1” should be produced and assembled.
Ladders which not included in the stations initially can be used as a spare.

## Slide 3
There are 3 pin to pin lengths of ladders which used in both types of Stations. These are 294.6 mm (294), 414.6 mm (414), 454.6 mm (454). Type 414 and 454 are the same for “Station 0” and “Station 1”, (except central ladders). Type 294 used in “Station 1” only.
The “Station 0” consist of ladders 2x414 normal
4x454 normal
2x454 central
The “Station 1” consist of ladders 2x294 normal
4x414 normal
4x454 normal
2x454 central
8 Ladders
12 Ladders
Total number of ladders should be produced is 40 for 2- “Station 0” and 2-“Station 1”
Ladder type 294n consist of 4-6x6 modules
type 414n 2-6x6 4-4x6 4-2x6
type 454n 4-6х6 2-4х6 4-2х6
type 454c 4-6х6 2-4х6
Sensors are necessary: 6x6-88 pc 4x6-96 pc 2x6-112pc
All ladders initially are without double 6x6 sensor modules. But type 294 ladders are possibly to do with double 6x6 sensor modules.
2. Number and types of ladders & modules

## Slide 4
3. Available components
We got a sufficient number of:
HPC sensors S13847 62x62 with specification from producer
CIS sensors CBM08 42x62 with specification from producer
HPC sensors S13847 22x62 single metal without specification
CF-ladders by Igolkin drawings (with smooth edges) and installation parts

## Slide 5
4. Components that must be obtained
STS-XYTER Chips
FEBs
Module cables kit

## Slide 6
5. Assembly device
Design and production of Ladder assembly device are in collaboration with “Planar” Minsk. As result of this work we hope to obtain device which suitable for assembling ladders with any pin to pin distances till 1 m and possibly wider. The main trouble is time limitation. 2 years is too long for us but “Planar” requires a 2 year for design and production.
Device consist of
Base table
Optical system
XYZ coordinate system for optics
XYϕ coordinate units for modules
CF-frame holder
CF-frame lift unit
Base for modules preliminary adjustment
Module carrying tool
Ladder removing tool
Storage containers
PC
Application program
Points 1-4 will be ready in December 2017

## Slide 7
Specification of the Assembly device
The precision of the sensor orientation
X coordinate ±50 mkm
Y coordinate ±15 mkm on 1200 mm base
±12 mkm on 180 mm base
Z coordinate ±50 mkm
The precision of the recognition system ±2 mkm
Move the optical system X coordinate 1200 mm
Sensors sizes 22x62 mm; 42x62 mm; 62x62 mm
The thickness of sensors 320±15 mkm
A number of XYϕ coordinate units for modules 20
A number of vacuum clamps for sens. 22x62 mm 6
42x62 mm 8
62x62 mm 20
Vacuum channels 20
Power AC220V, 50Hz, 500Wt
Dimensions (no more) 1500х900х1400 mm
Weight (no more) 900 kg

## Slide 8
Assembly device concept
Optical alignment of alignment marks for each sensor through modules mounting
Optical checking of sensors position before gluing
Gluing of all modules L-legs to CF-frame in one process
HPC alignment mark

## Slide 9
6. Assembly procedure
The preliminary operation before ladder assembly is L-Legs gluing. L-legs should be glued on longitudinal edges of the sensor (see picture below)
L-legs
Cables
Interstrip cable (for 2x6 only) on p-side
Assembly starts from periphery to the center of the ladder.
Each ladder may contain from 4 till 10 modules placed on 6 levels.
Following pictures shown ladder assembly procedure with 4 pair of modules

## Slide 10
Base for modules preliminary adjustment

## Slide 11
Step 1. Edge to edge adjustment of the module in preliminary position before assembling
Sensor fixed with vacuum clamp
Cables and FEBs are on support freely.
Module with single sensor 22x62 mm and interstrip cable for example

## Slide 12
Step 2. Mounting carrying tool on the base above module
Carrying tool is fixed on base (with screws).
Upper cable fixed on carrying tool (with vacuum)

## Slide 13
Cables and FEBs lifted up above support

## Slide 14
Step 3. Cables & FEBs holder placed under them and fixed to carrying tool (with screws)

## Slide 15
the screws are not shown

## Slide 16
Module is ready to carrying to assembly position (after unfixing from base)
Interstrip cable on p-side

## Slide 17
Possibly to prepare a few modules for assembly (like variant)

## Slide 18
Or even to prepare all modules of ladder
For example

## Slide 19
Step 4. Mounting vacuum clamps for sensors and Cable holders onto assembly position
side view
Each vacuum clamp equipped with independent XYϕ adjustment screws and vacuum channel. (not shown)
Height of working surface adjusted with 1 mm calibrated plates. (not shown)

## Slide 20
Sensor fixed with vacuum and adjusted with optical system and alignment marks. Sensors, cables, FEBs moving as one.
Step 5. Carrying, mounting and adjustment 1st pair of modules start from periphery
Double sensor module for example

## Slide 21
Removing of carrying tool and straighten cables in plan on cable holder for 1st pair
Adjusted sensors fixed with vacuum. Cables and FEBs are on support freely

## Slide 22
Step 6. Carrying, mounting and adjustment 2nd pair of modules
The optical system should be driven by the PC program and give the position for each point of alignment.

## Slide 23
Removing of carrying tool and straighten cables in plan on cable holder for 2nd pair
The cables are stacked on cable holders

## Slide 24
Step 7. Carrying, mounting and adjustment 3rd pair of modules
The position of the each alignment mark may be illuminated by the laser on sensor surface, or to be shown as the cross on the video cam picture.

## Slide 25
Removing of carrying tool and straighten cables in plan on cable holder for 3rd pair

## Slide 26
Step 8. Carrying, mounting and adjustment modules of central part

## Slide 27
Removing of carrying tool and straighten cables in plan on cable holder for modules of central part

## Slide 28
Step 9. Mounting of the cable clamps
Cables are held together
Cable clamps

## Slide 29
Step 10. Mounting of the CF-frame above modules
Cable holders are removed

## Slide 30
Step 11. Mounting CF-frame. Gluing L-legs and cable clamps to CF-frame in one process
After check of positions of all alignment mark with optical system.

## Slide 31
Step 12. Mounting of the cooling boxes and FEBs

## Slide 32
Step 13. Transfer of the cooling boxes in the operating position

## Slide 33
Step 14. Joining CF-frame and cooling boxes with 1st half of storage container

## Slide 34
Step 15. Removing of the complete ladder from device
All clamps are released

## Slide 35
Step 16. Mounting of the 2nd half of storage container
Ladder ready to be stored

## Slide 36
8.References
Jochen Kunkel “Pin-to-Pin distances of CBM STS ladders, documentation and so on …” 2015-03-30

## Slide 37
Thank you for your attention!
BM&N STS = 4 stations = 40 ladders of 3 types = 300 simple one sensor modules