## Slide 1: Results of obtaining 48Ca, 48Ti and 52Cr ion beams at the DC-280 cyclotron
Pugachev D.K., Bogomolov S.L., Mironov V.E., Efremov A.A., Loginov V.N., Lebedev A.N., Bondarchenko A.E., Kuzmenkov K.I.

## Slide 2: Superheavy Elements (SHE) Factory – the Goals
Experiments at the extremely low (σ<100 fb) cross sections:
Synthesis of new SHE in reactions with 50Ti, 54Cr ...;
Synthesis of new isotopes of SHE;
Study of decay properties of SHE;
Experiments requiring high statistics:
Nuclear spectroscopy of SHE;
Study of chemical properties of SHE.
To carry out the scientific program, the DC-280 has to provide the following parameters of ion beams:
Ion energies (smooth variation) | 4 - 8 MeV/n
Ion masses | 10 - 238
Intensities (A~50) | >10 pµA
Efficiency of beam transfer from ion source to physical facility | >50%

## Slide 3: Main Parameters
Ion sources | Permanent magnet ECR DECRIS-PM - 14 GHz
Injection energy | Up to 80 keV/Z
A/Z range | 4÷7.5
Energy | 4÷8 MeV/n
Magnetic field level | 0.6÷1.3 T
K factor | 280
Magnet weight | 1000 t
Magnet power | 300 kW
Dee voltage | 2x130 kV
RF power consumption | 2x30 kW
Flat-top dee voltage | 2x14 kV
Deflector voltage | Up to 90 kV

## Slide 4
Parameters of DECRIS-PM | 
UHF frequency | 14 GHz
Binj | ≥ 1.3 T
Bmin | 0.4 T
Bextr | 1.0 ÷1.1 T
Br | 1.05÷1.15 T
Plasma chamber internal diameter | 70 mm
Ion source

## Slide 5
Magnetic structure of DERIS-PM.
1÷5 – PM rings; 6, 7 – soft iron rings;
8÷11 – soft iron plates;
12÷14 - auxiliary elements;
15 – hexapole; 16 – coil.
Axial magnetic field distribution
DECRIS-PM magnet system

## Slide 6
3 48CaO + 2 Al
3 48Ca + Al2O3
Production of 48Ca beam
Oven 1
1300 °C
Oven 2
500 °C
Helium
Helium + Ca
Helium + Ca +
UHF Power>300
The 48Ca ion spectrum, optimized for Ca10+
Reduction of calcium from
calcium oxide

## Slide 7
Production of 48Ca beam
Faraday Cup | Current, emkA | Efficiency of beam transfer
Iinj1 | 240.5 | 100.00%
Iinj2 | 229.5 | 95.43%
Iinj3 | 190 | 79.00%
IRP2-1 | 130.2 | 54.14%
IRP2-2 | 105.8 | 43.99%
IFCI | 71.106 | 29.57%
61 events of 115Mc
94 events of 114Fl
16 events of 112Cn

## Slide 8
Production of 50Ti and 54Cr beams

## Slide 9
Production of 48Ti and 52Cr beams
(CH3)5C5Ti(CH3)3
C10H10Cr
Compound Properties | (CH3)5C5Ti(CH3)3 | C10H10Cr
Molar mass, g·mol−1 | 228.291 | 182.186
Appearance | yellow crystals | dark red crystals
Density, g/cm3 | 1.081 | 1.43
Vapor Pressure, mmHg at 25°C | - | 418
Sensitive | Light, Air & Moisture Sensitive | Air & Moisture Sensitive

## Slide 10
Production of 48Ti and 52Cr beams
The 52Cr ion spectrum. optimized for Cr10+
The 48Ti ion spectrum. optimized for Ti10+
48Ti + UHF Power 350 W

## Slide 11
Production of 48Ti and 52Cr beams
Faraday Cup | Current, emkA | Efficiency of beam transfer | Current, emkA | Efficiency of beam transfer
Iinj1 | 22.746 | 100.00% | 70.498 | 100.00%
Iinj2 | 20.346 | 89.45% | 58.372 | 82.80%
Iinj3 | 15.849 | 69.68% | 51.841 | 73.54%
IRP2-1 | 11.556 | 50.80% | 34.72 | 49.25%
IRP2-2 | 9.949 | 43.74% | 30.925 | 43.87%
IFCI | 7.27 | 31.96% | 25.5 | 36.17%
48Ti7+
52Cr10+

## Slide 12
Resonator
Inductive oven
Power supply:
EA-PSI 9080-60
0÷80 V, 0÷60 A, 0÷1500 W
Screen
Waveguide
Pre-pumping volume
water cooling of the inductor
Inductor
IPHC Strasbourg / FLNR Dubna collaboration

## Slide 13
The first test of the inductive oven gave a good result. We have reached the required temperature for evaporation of Ti (1700 degC) and Cr (1300 degC).
Tmax=1860 degC in a crucible with room temperature on the outer surface of the plug.
First results
IPHC Strasbourg / FLNR Dubna collaboration

## Slide 14: Results and future plans
Calcium consumption was 1.2 mg/h for a high-intensity ion beam (14 pµA 48Ca10+) and 0.3 mg/h for a low-intensity beam (4 pµA 48Ca10+). Average consumption of calcium 0.67 mg/h. Total working time with a calcium beam for the last year around 3200 h.
Titanium and chromium beams were obtained on the DC-280 cyclotron. The issues of modernization of the design of some elements of the ion source, contributing to an increase in the intensity of the ion beam using the MIVOC method, are being solved.
The successful first test of the inductive oven in an isolated vacuum chamber allows us to start real tests with the ion source DECRIS-2M (Test-bench).

## Slide 15: Thank you for your attention