## Slide 1
The new Inner Tracking System of the ALICE experiment
Paolo Martinengo – CERN
A Large Ion Collider Experiment

## Slide 2
OUTLINE
  Motivations and Experimental Strategy
  Design Objectives and Layout
  Selected topics from the R&D
  Construction and Integration Schedule
  Conclusions
The new ALICE Inner Tracking System

## Slide 3
ALICE Upgrade – From observation to precision measurement
In March 2013 a new physics program for ALICE was approved
Physics Goal  high-precision measurements of QGP properties
Open HF ( charm & beauty, mesons & baryons ), Quarkonia down to zero pT
  thermalisation, hadronization, recombination, temperature evolution of the QGP
Vector mesons and low-mass di-leptons
  chiral symmetry restoration, virtual thermal photons
High-precision measurement of light (anti-)nuclei and hyper-nuclei
  nucleosynthesis, exotics
ALICE Upgrade LoI
March 2013
and more

## Slide 4
ALICE Upgrade – From observation to precision measurement
Main requirements for the new Inner Tracking System:
High tracking efficiency and resolution at low pT (60% @ 100 MeV/c)
Increase granularity, reduce material thickness
Excellent secondary vertex resolution (Lc ct ~60 mm)
Move closer to Interaction Point (IP), new beam pipe, smaller diameter
High-statistics, un-triggered data sample ( >10 nb-1 Pb-Pb)
Increase readout rate, reduce data size (online data reduction)
ITS Upgrade TDR
March 2014

## Slide 5
3. Exploit LHC luminosity increase  fast readout
readout Pb-Pb interactions up to 100 kHz, i.e. 2 x expected peak luminosity after LS2 (currently limited at 1kHz)
4. Withstand radiation load (10 years operation):
TID: ~ 270 krad, NIEL: ~1.7x1012 1MeV neq / cm2
5. Reliability  fast insertion/removal for yearly maintenance
possibility to access faulty components during yearly shutdown
 Services (power, cooling, R/O) connected only on one side
New ITS Design Objectives
1. Improve impact parameter resolution by a factor of 3 (5) in rj (z) @ pT = 500 MeV/c
Get closer to IP (position of first layer): 39 mm 23 mm
Reduce x/X0 /layer: ~1.14%  ~ 0.3% (for the 3 innermost layers)
Spatial resolution: currently 12 mm x 100 mm (SPD)  5 mm x 5 mm
2. Improve tracking efficiency and pT resolution at low pT
Increase granularity:
  6 layers  7 layers
  silicon pixel, drift and strip  all-pixels

## Slide 6
12.5 G-pixel camera
(~10 m2 active Si)
Binary read-out
7-layer barrel geometry,
fully equipped (~24000 chips) with dedicated MAPS:
ALice PIxel DEtector (ALPIDE)
r-coverage: 23 – 400 mm
coverage: |h| ≤ 1.3
Material /layer : 0.3% X0 (IB), 1% X0 (OB)
Layout of the new ITS
Monolithic Active Pixel Sensors

## Slide 7
Performance of new ITS (MC simulations)
Total weight
1.4 grams
40 μm at pT = 500 MeV/c
Impact parameter resolution
Tracking efficiency (ITS standalone)
~60% at pT = 100 MeV/c
Cellular automaton, i.e. online tracking & vertexing
mandatory in Run3, 1.1 TB/s of data (ITS 40 GB/s)

## Slide 8
Physics performance with the new ITS (MonteCarlo)
B± not accessible with the present ITS
Low pT , clean signal
Measure energy loss for b,
quantitative verification of DEc > DEb vs. pT

## Slide 9
Physics performance with the new ITS (MonteCarlo)
Large improvement also for D0 & DS signals,
possibility to discriminate between
thermal and coalescence hadronization models
LC not accessible (in Pb-Pb) with the present ITS
v2 measurement possible with the new one
pT (GeV/c)

## Slide 10
R&D
Huge R&D effort started 6 years ago
Simulation
Pixel sensor, connectivity
Cooling, power distribution
Read-out chain
Assembly tools & procedure
Construction database
Mechanical support (carbon fiber)
Integration in ALICE
and more
First prototype usually does not
meet all requirements

## Slide 11
ALPIDE – Technology and Pixel Layout
Pixel Sensor using TowerJazz 0.18 mm CMOS Imaging Process
NA ~ 1018
Small n-well diode (2 mm diameter), ~100 times smaller than pixel => low capacitance (~fF)
High-resistivity (> 1 kW cm) p-type epitaxial layer (25 mm)
on p-type substrate
Reverse bias voltage (-6 V < VBB < 0 V) to substrate (contact from the top) to increase depletion zone around NWELL collection diode
Deep PWELL shields NWELL of PMOS transistors (full CMOS circuitry within pixel active area)
In-pixel:
Amplification
Discrimination
3-hit storage register (MEB)
In-matrix sparsification
MFT based on the same chip

## Slide 12
Key features:
Dimensions: 30 mm x 15 mm
Pixel pitch: 29 mm x 27 mm
Ultra-low power (entire chip): ~40 mW/cm2 , (requirement < 100 mW/cm2) 140 mW full chip
Triggered acquisition (200 kHz Pb-Pb, 1 MHz pp) or continuous (progr. integration time: 1ms - ∞)
ALPIDE – Final Version
High speed serial data output (HSO)
OB: 400 Mbit/s
IB: 600 Mbit/s or 1.2 Gbit/s
Inner Barrel: 50 mm thick
Outer Barrel: 100 mm thick
Production started Dec 2016, to be completed by Dec 2017
Pad-over-matrix

## Slide 13
ALPIDE floorplan
Sensitive area / Si area ~0.92

## Slide 14
ALPIDE carrier card and DAQ board

## Slide 15
~400 mm

## Slide 18
ALPIDE telescopes

## Slide 19
ALPIDE telescopes

## Slide 20
Position-resolved results

## Slide 21
Position-resolved results

## Slide 22
Big operational margin with only 10 masked pixels (0.002%), fake-hit rate < 10-10 pixel/event (requirement < 10-6)
Chip-to-chip fluctuations negligible
Non-irradiated and NIEL/TID chips show similar performance
Sufficient operational margin after 10x lifetime NIEL dose
VBB=-3V
NIEL/TID
non-irradiated
10x lifetime NIEL
ALPIDE – Detection Efficiency and Fake-Hit Rate
99%
Test beam at facilities all around the world:
BTF Frascati, CERN, DESY, Pohang/Korea, SLRI/Thailand –
JINR will be next
6 GeV/c p-

## Slide 23
Chip-to-chip fluctuations negligible
Non-irradiated and TID/NIEL chips show similar performance
Resolution of about 5µm at a threshold of 200 electrons
Sufficient operational margin even after 10x lifetime NIEL dose
ALPIDE – Resolution and cluster size
VBB=-3V
5 mm
6 GeV/c p-

## Slide 24
Detector Barrel Staves
Si
1500 mm length
80 gr weight
cooling integrated in C fiber support
H20
C
glue

## Slide 25
Flexible PCB
9 sensors
Cold Plate
Space Frame
Outer Barrel
Inner Barrel
Stave Layout
sensors thinned to 50mm
x-cables for connection to power bus
9 chips, stave length ~450 mm
2x7 chips
length 245 mm

## Slide 28
X-ray (55Fe) image of IB HIC (radiography of 3 sensors)
Prototype series of Inner Barrel and Outer Barrel HICs Staves with pALPIDE-3
Characterization with different modes of operation, readout rates and environmental conditions (power supply and temperature)
Sensor performance comparable to standalone chip
Pre-series production with ALPIDE chips starting now
Hybrid Integrated Circuits (HIC) and Stave Prototypes
INNER BARREL
OUTER BARREL
Outer Barrel HIC – threshold measurements

## Slide 29
ALPIDE in NA61, Dec. 2016, Pb-Pb

## Slide 30
ALPIDE in NA61

## Slide 31
ALPIDE in NA61

## Slide 32
ALPIDE in NA61

## Slide 33
Muon Forward Tracker (MFT)

## Slide 35
MFT
ITS OB
ITS IB
TPC
Beam Pipe
FIT
ALICE ITS Upgrade
ITS & MFT Interfaces
Interaction point

## Slide 36
BERYLLIUM
RB 26
RB 24
OD 38 mm
ID 36.4 mm
New Beam Pipe, diameter reduction from 60 to 38 mm
Beryllium
UNDER PRODUCTION

## Slide 37
CERN-LHCC-2015-001
ALICE-TDR-018

## Slide 40
Two points/track for 50% of tracks, overlap included

## Slide 41
Chip series test and Hybrid Integrated Circuit (HIC) assembly
ALICIA (IBS)
6 machines (+1 MFT)
(Chip probe testing & HIC assembly)
Korea-YS01 (C-On)
1 machine
(mass chip probe testing )
24000 chips needed
+
MFT & spares
ALICIA = ALice Integrated Circuit Inspection and Assembly
Machines installed at production sites, training started
Chip tray
Probe card
Assembly table

## Slide 42
Layout – staves and modules data/control connections
Inner layers stave, 9 master sensors (each read/drives its own control and data lines)
Control (trigger)
Clock
Mid/Outer layers module: 2 symmetric group of 1 master and 6 slave chips. Only the master accesses the data/control lines toward/from the outer world.
Clock
Data
Control (trigger)
Clock
Data
Control (trigger)
…
…
Data
Data

## Slide 43
Communication between detector (ALPIDE) and off-detector electronics via SAMTEC firefly cables
Distribution of CLK and slow-control at 40MHz
Data readout at 1.2Gb/s (IB) & 0.4Gb/s (OB)
RUv0
sensor
GBT loopback
RUv0 – Readout chain with final ALPIDE verified
Eye diagram of signal propagated over 5m-long cable
Measured BER (no errors over 14 h) < 1.6 10-14
RUv0
“CRU”
ALPIDE
FireFly Cable
ALPIDE will be the only electronics
component around the Interaction Point,
the off-detector electronics will sit 5 m away

## Slide 44
Sensor Series Production
Stave Develop
2016
2017
2018
2019
2020
Commissioning @ Surface
Installation
Commissioning in ALICE
Stave Mechanics
HIC Production
CMOS processing, thinning & dicing, test
HIC and Stave
Stave Production
Mechanical Support Structures
Design & Prototyping
Design & Prototyping
Production & Test
PRR
PRR
Global Assembly
EDR
PRR
Development
Production
2016
2017
2018
2019
2020
EDR
PRR
Readout Electronics
Commissioning
11 months
Dry Assembly Test
Overall ITS Planning (Simplified Global View)
Sensor: Production started
HIC: EDR ok, PRR in March
Mechanics: PRR passed
R/O: EDR ok, PRR end ’17
Cooling: PRR passed
EDR = Engineering Design Review
PRR = Production Readiness Review

## Slide 45
Conclusions
The new ALICE Inner Tracking System project has successfully completed the R&D phase
All requirements have been met or even exceeded
With the start of the production of the ALPIDE sensor a major milestone was achieved
Production sites are equipped with custom machines for test &assembly
Detector production will enter full swing during 2017
The project is well on track for installation starting middle 2020

## Slide 46
SPARES

## Slide 47
TPC
EMCAL
HMPID
TRD
TOF
ZDC
PMD
T0, V0A
SOLENOID
ABSORBER
DIPOLE
PHOS
ZDC
MCH
MTR
Si PIXEL
Si DRIFT
Si STRIPS
Central Barrel Tracking
Silicon: 39 – 430 mm
Gas (TPC, TRD): 88 – 368 cm
New ITS
Readout rate is currently limited by TPC and ITS (SDD)
~ 1kHz for Pb-Pb
ACORDE
ALICE ITS Upgrade – entirely new, all-pixel detector, after LS2
ADC
ADA
DCAL
Current ITS

## Slide 48
VBB=-3V
All chips show the same correlation
Neither irradiation nor settings influence the correlation
At low cluster size, the loss of detection efficiency leads to a deterioration
Cluster size can be used to infer position resolution
ALPIDE – Resolution vs. cluster size

## Slide 49
ALPIDE – Technology and Pixel Layout
pALPIDE-1
Full-scale prototype: 1024 x 512
4 sectors with pixels variants
pixel pitch: 28mm x 28mm
1 register/pixel, no final interface
pALPIDE-2
4 sectors with pixels variants
Optimization of in-pixel and peripheral circuits
NO high-speed output link (1.2 Gbit/sec replaced by a 40Mb/s)
May-2015
May-2014
30mm
15mm
pALPIDE-3
8 sectors with pixel variants, 3 registers / pixel
All final features, including 1.2 Gbit/s data serial output
Aug - 2016
Chip Final Version
Main changes wrt pALPIDE-3
Full matrix with same pixel type
time skew of global signals
Improved protection against SEUs
Improvement of PLL  High-speed Serial Output
Oct-2015
ALPIDE
ALICE ITS Upgrade

## Slide 50
2 Layers, Vacuum deposition
20 µm
25 µm
75 µm
25 µm
20 µm
50 µm
200 µm
Laser soldering: connection of Pixel chip to flexible printed circuit
Laser soldering machine
Selective laser soldering
R&D on Pixel Chip to FPC Interconnection – Selective Laser Soldering
All process main issues were solved
More time needed to bring the process to a steady single interconnection yield of ~99.99%
Remains a very promising interconnection technology for future applications
R&D addressed:
Geometry of the interconnection
soldering ball, interface pad and VIA
laser beam profile and power time profile
….

## Slide 51
STRIP
DVDD
AVDD
AVDD
DVDD
STRIP
STRIP
STRIP
STRIP
STRIP
STRIP
STRIP
BIAS
DVSS
AVSS
DVSS
solder mask
aluminum (IB) / copper (OB)
polyimide
solder mask
aluminum (IB) / copper (OB)
30mm
25mm/18 mm
75mm
25mm/18 mm
30mm
Flexible Printed Circuit (FPC) cross section
FPC to Chip interconnection – Wire Bonding
Droplets of glue (epoxy resin) dispensed on the FPC
chip pads aligned to FPC VIAs
FPC to Chip interconnection (Al wire bonding)
solder mask
aluminum (IB) / copper (OB)
polyimide
solder mask
aluminum (IB) / copper (OB)
30mm
25mm/18 mm
75mm
25mm/18 mm
30mm
pixel chip
pad
glue
glue
Al bonding
wire
PCB conductor
aluminum Inner Layers
copper outer layers

## Slide 52
Hybrid Integrated Circuits (HIC) and Stave Prototypes
ALICE ITS Upgrade
Stave temperature measurements while powering on stave in two steps
Power on (with CLK): ~ 80 mW digital + 20 mW analogue / chip
Activation of high-speed serial output (DTU): ~ 160 mW digital + 20 mW analogue / chip
Power On
DTU Configuration

## Slide 53
Inner Barrel Stave Mechanics & Cooling
ALICE ITS Upgrade
Coolant: H2O, leak-less
Sensor temperature < 30°C
Temperature non-uniformity < 5°C
Tout=16.6 °C
Tin=15.8° C
Max T periph=18.5° C
Min T pixel =16.5° C
290mm length
W = 100 mW / cm2 (> x2 nominal) , H2O flow rate = 3 Lh-1
Si

## Slide 54
Space Frame
Cold Plates
~1500mm length
~ 80gram weight
Power bus
Space Frame
Cold Plate
2x7 sensors
FPC
single-phase H2O leak-less
- temperature < 30°C
- non-uniformity < 5°C
- dissipation < 100mW/cm2
Outer Barrel Stave Mechanics & Cooling
ALICE ITS Upgrade

## Slide 55
Stave
Half Layer
Detector Half Barrel
End wheel
End wheel
The end-wheels, ensure precise positioning of staves in a layer
3 half-layers are connected together to form half-barrel
An outer Cylindrical Structural Shell (CYSS) connects the opposite end-wheels of and avoids external loads are transferred to Staves
Each barrel is divided into two halves, which are mounted separately around the beam pipe
CYSS
290 mm
Inner Detector Barrel
ALICE ITS Upgrade

## Slide 56
Outer Detector Barrel
ALICE ITS Upgrade
3310mm
Stave
Outer Detector Half Barrel
Conical Structural Shell
Service Barrel

## Slide 57
MFT
ITS OB
ITS IB
CAGE
Beam Pipe
FIT
ALICE ITS Upgrade
Detector Interfaces

## Slide 58
Clock
FPGA
FPGA
GBTx
GBTx
GBTx
SCA
2 × 16 channel FPGA
Control
Data (960 Mb/s max)
Trigger
Central Trigger Processor
One way, passive optical splitting, no busy back
GBT optical
GBT optical
Common Readout Unit & O2
Data (9.6 Gb/s max)
Inner layer (0,1,2)
0.6 (1.2) Gb/s high speed data,
80 Mb/s clock and control
FPGA
FPGA
GBTx
GBTx
GBTx
SCA
2 × 16 channel FPGA
…
× 192
Control
Data (9.6 Gb/s max)
Clock
Control
Data (320 Mb/s max)
Each Readout Unit is connected to one stave both for Inner and Outer Barrels
GBT optical
Control
Identical Readout Units (RU) cover the full ITS
Outer layers (3,4,5,6)
400 Mb/s high speed data,
80 Mb/s clock and control
Readout Electronics - Architecture
ALICE ITS Upgrade
Detector Readout  192 READOUT UNIT

## Slide 59
Readout Unit - Prototype
ALICE ITS Upgrade
Prototype Readout Unit – 2015
Based on SRAM FPGA (Xilinx Kintex7) + GBTx FMC (daughter board)
Extensive use of radiation mitigation techniques
Communication with Trigger and DAQ via GBT link validated
Communication with sensors via high-speed copper serial links validated
Radiation induced fault rates
Intensive SEU test campaigns :
MTBF/device: ~2400 hours (109 h/cm2)
MTBF/entire system: ~12 beam hours
System downtime ~ 10-5
READOUT UNIT v0 – October 2015
Mother Board
FPGA Mezzanine Card (FMC)
Mother Board
Hadron Flux
~ 1kHz/cm2