## Slide 1: Progress on the Magnet Yoke assembling October 2021
N.Topilin, E.Belyaeva, E.Gerasimov, O.Khilinova, A.Shunko
JINR, Dubna

## Slide 2
28 plates
16 t each
2 support rings
42.5 t each
2 poles
44 t each
Total weight: 621 t
Material:
Steel 10 (AISI 1010)
forging
MPD Yoke (L=8970 mm, Ø6625 mm)
Lodgement (Yoke support) – 70 tons, ordinary steel St.3 (Fe 360)
Pole transport supports 15 tons each without ballast

## Slide 3
MPD yoke preassembly at VHM, June-August 2018

## Slide 4
MPD pre assembly at JINR
(13 July – 12 August 2020)
1-st stand
1-st plate: 8.5 m length, 16 tons
42 t Pole installation
Support ring lifting, Ø 6.7 m, 44 tons
13 plates and 2 rings as 1 piece
370 tons in total
Leading engineer N.Topilin VBLHEP
JINR-Pelcom plant team
JINR-Pelcom plant team

## Slide 5: Measurements by “Industrial Measurements” LLC (ООО “Промышленные измерения”) , S.Peterburg
Rails planarity (top and side surfaces) – 0.4 mm on length 30 m
12 stands height deviations – 0.1 mm max
Stands shape deviation – 0.2 mm max
7 plates in assembly – nonplanarity 0.5 mm
13 plates in assembly - nonplanarity 0.58 mm max
13-th plate installation

## Slide 6
Geometry of 13 plates in the assembly
Nonflatness of plates
## 12-13 per faces
Nonflatness of plates
## 12-13 per faces
relative to the
horizontal plane
Nonflatness of plates
##4-5 and ##8-9

## Slide 7
Capturing the position of the plate with micron accuracy
Поимка положения плиты с микронной точностью

## Slide 8
Installation top (last) plate #28

## Slide 9: December 25, 2020

## Slide 10
28 plates in assembly

## Slide 11
Poles installation technology
This operation was elaborated by DD of VBLHEP and performed only in JINR
The accuracy of the installation of the pole axis relative to the axis
of the support ring is 0.25 mm (provided technologically).

## Slide 14
Movement system assembly and test

## Slide 15
The movement system allows you to move an object weighing
up to 1000 tons with a positioning accuracy of 0.01 mm across
the beam and install it with an accuracy of 0.1 mm in height.
The speed of movement of all rods is from 0 to 3 mm/s.

## Slide 16
1 - Assembly zone position
Rails shape during Yoke moving
2 - Central position
(poles installation)
3 - Beam position

## Slide 17
Power frame brackets

## Slide 18
July 16, 2021

## Slide 19
Technology beam 8470 mm length

## Slide 20
Magnet installation: July 30, 2021
August 2020
Traverse 75 t capacity and
80 t Crane test together

## Slide 21
The position of the magnet axis relative to the axis of the Yoke

## Slide 22: Related tasks
Assembling and modification
the mobile platform
Evacuation of the ASG magnet transport container

## Slide 23
Pole transport support modification
O-Ring, 3935 mm in diameter,
Overall thickness: 300 mm
Weight: 2.7 t , 2 ps
Modification reason: Cable space increasing
by “Lider” Company, St-Peterburg
Installation: end of October 2021

## Slide 24: Thanks for your attention !
Conclusion
Next steps:
Pole transport support modification
Yoke assembly finishing
Top platform assembly
Cryogenic equipment installation on the top platform
Worm coils installation in the poles
AOB for magnetic test preparation
All of these operations will be done as soon as it will be possible