## Slide 1: Experiments on the short x-ray pulse generation at the NovoFEL facility
presented by
Getmanov Yaroslav
& Borin V, Ma X, Maltseva Y,
Meshkov O, Shevchenko O, Vinokurov N
Budker INP
XIV МЕЖДУНАРОДНЫЙ СЕМИНАР
ПО ПРОБЛЕМАМ УСКОРИТЕЛЕЙ ЗАРЯЖЕННЫХ ЧАСТИЦ
∙ Крым, Россия, Sept 20-25 2022 ∙

## Slide 2
1. Introduction
2. Novosibirsk FEL facility
3. Energy Recovery Linacs
4. Layout of the experiment
4. Bremsstrahlung from a thin foil
5. Optimization of the used beam transport
6. The beam parameter measurements
7. Results
8. Conclusion
Content
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия
2

## Slide 3
An r. m. s. bunch duration at the fourth track of the ERL of the Novosibirsk FEL facility could be less than 10 picoseconds. Installing graphite foil, one can obtain the source of picosecond x-ray pulses with high (few MHz) repetition rate.
All other contemporary x-ray sources (storage rings, x-ray tubes, laser wake-field accelerators, x-ray FELs, etc.) have no such capability.
Sources of picosecond bremsstrahlung x-ray pulses could be an interesting application for low-energy (few tens of MeV) ERLs.
What for?
3
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 4
NovoFEL Accelerator Design
Gun
Injector
Main linac
The first THz FEL
undulator sections
The second FEL
undulator
The third IR FEL
undulator sections
Dump
NovoFEL
The most attractive ranges for FELs are at very short and at very long wavelength, where there are no other lasers
Three FELs working in terahertz and far infrared regions
The most powerful source of coherent terahertz radiation
The first in the world multi-turn Energy Recovery Linac
The world record beam average current for ERLs
4
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 5
NovoFEL Parameters
5
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия
FEL | 1 | 2 | 3
Energy, MeV | 12 | 22 | 42
Av. current, mA | 30 | 10 | 3
Wavelength, mkm | 90-240 | 37-80 | 8-11
Max. Av. Power, kW | 0.5 | 0.5 | 0.1
Electron efficiency кпд, % | 0.6 | 0.3 | 0.2
Bunch frequency, MHz | 5.64 | 7.52 | 3.76
Bunch duration, ps | 100 | 50 | 10
Accelerator tracks | 1 | 2 | 4
Launched | 2003 | 2009 | 2015
optical discharge
plexiglass
EPR station

## Slide 6
NovoFEL Radiation
6
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия
radiation structure of the 1st FEL
beam image at station
Radiation with and without electron modulation
macropulse of radiation

## Slide 7
Accelerator is the most important part of
the high power radiation source
Energy Recovery Linear Accelerator
1 – injector, 2 – linac, 3 – bending magnets, 4 – undulator, 5 –dump
7
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 8
Energy recovery
decreases radiation hazard and
makes possible operation at high average current.
Energy Recovery Linear Accelerator
1 – injector, 2 – linac, 3 – bending magnets, 4 – undulator, 5 –dump
8
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 9
area of generation
Four-Pass NovoFEL Energy Recovery Linear Accelerator
Parameters | 3rd
Energy, MeV | 38-42
Avg. current, mA | 3
Beam freq, MHz | 3.76
Bunch Charge, nC | 0.5-1
Bunch length, ps (estimation) | 10
Norm. Emittance Hor., mm*mrad (measured) | 80
Norm. Emittance Ver., mm*mrad (measured) | 30
PEA
ФЭУ
electron bunch
bremsstrahlung
thin foil
foil input
undulator
diagnostic
9
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 10
Low-frequency bremsstrahlung from a thin foil
The low-frequency ( ) intensity of radiation from the length L is
This expression is valid if the corresponding r. m. s. multiple-scattering angle
does not exceed the angular divergence of radiation, which is about 1/ γ, or
where n is the density of atoms, a is atomic radius, γ, e and re are Lorentz factor, electric charge and classical radius of electron, Z is atomic number.
10
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 11
The NovoFEL advantages and comparison with others sources
The main problem is a beam transport after scattering.
As already mentioned, the bremsstrahlung on the foil makes it possible to obtain 10 ps radiation pulses with a frequency of several MHz. The photon flux can be estimated as 1010/pulse. Moreover, the frequency can be smoothly adjusted (the maximum achieved FEL lasing bunch frequency is 22 MHz at the one-pass ERL).
For comparison:
at the SASE FEL (record peak brightness) pulse frequency is about 10Hz– 10kHz with pulse duration 0.1 ps, photon/pulse 1012;
at the storage rings frequency is about 100 MHz and pulse duration 40-100 ps;
with femtoslicing technique the pulse duration is about 0.1 ps with frequency 1-2 kHz and photon flux 103/pulse.
In addition, those experiments do not require the installation of additional radiation output channels, since X-rays freely exit the vacuum chamber. And does not limit the other experiments at the facility, as the foil is easily removed from the orbit of the electron beam.
11
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 12
The beam transverse sizes does not change.
R. m. s. multiple-scattering angle
Beam parameters after the foil
In the case of bremsstrahlung, the losses increase due to an angular spread and emittance grows of the beam after foil.
ФЭУ
electron bunch
3 MHz
thin foil
bremsstrahlung
25μm
20 m
3x1x1 mm
Twiss parameters after foil
Emittance
E=38.8 MeV
target
There are two options of foil input.
At the FEL lasing the main beam losses arise due to an increase in the energy spread by an order of magnitude due to microbunching.
The main problem of radiation sources based on ERL is a beam transport after generation
The difference is in the geometry of the apertures and the distance to the lenses
12
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 13
Electron beam propagation
The reason for the beam loss at bremsstrahlung differs from it of FEL lasing. Therefore, probably, the electron-optical structure should be reconfigured. To do this, it is useful to recalculate the regime and use it as initial conditions for tune.
To set the boundary conditions for the beta-functions, it is necessary to estimate the admissible beam losses.
At the FEL laing the maximum beam losses is 10–15%. Assuming the losses are uniform distributed over the tracks and equality of the loss powers at the tracks, the distribution of losses is 1.5, 2, 3, 5.5)% at the deceleration. It determines the fraction of the beam that must be passed through the system.
The beam emittance depends on how strongly the beam can be focused on the foil and on the angular divergence determined by the thickness and composition of the foil.
There are two options of foil input:
The first is in front of the undulators with rather narrow vertical aperture. But a camera is installed in this place and the beam size can be observed and adjusted.
The Second is after undulators, but without diagnostic and beam parameters can be only estimated.
foil
free
vert
hor
13
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 14
Electron optic optimization
Achromatic bends
Symmetric quad lenses
Symmetrical lattice functions at the input and output of the 4th track
Minimum emittance at the foil
Energy changes form 2 to 40 MeV
80 quadrupole lenses
8 bends with 16 dipoles
4 accelerating and decelerating RF sections
Total orbit length is about 350 m
Common optics at the intermediate tracks
lattice parameters
conditions
example of the beam transport in ordinary mode
14
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 15
Foil Regimes
full deceleration
15
beam transport after the foil-5
the main problem – optic matching after bend
smaller beam size at the foil is required
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 16
bunch before FEL lasing
bunch after FEL lasing
optical diagnostic of the bean sizes
Beam parameters diagnostic system
emittance measurement
scheme
16
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 17
Experiments at the NovoFEL facility
Spectroscopy
(20.25%, 328 h)
EPR
(21.76%, 352 h)
3d Stage
(12.03%, 195 h)
2d Stage (4.27%, 69 h)
Biology (2.32%, 38 h)
Other (0.75%, 12 h)
Photonics
(38.61%, 625 h)
NovoFEL worktime at 2021-2022
Posters:
Commissioning Of The First Fel With Variable-period Undulator
Permanent Magnets For The Novofel Variable Period Undulator
Design And Simulation Results Of Helical Undulator With Variable Period
Development Of A 540-degree Magnetic Buncher Based On Permanent Magnets
Spontaneous Emission From Distributed Optical Klystron
17
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 18: Experiments with graphite foil before undulators
Iin
Ifoil
Ifoil / Iin
rel. beam propagation
with foil
withot foil
rel. beam propagation
18
signal from PEA
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 19
I foil-5-graphite
I foil-4-aluminum
I initial
без фольги
с фольгой
I foil-graphite
The bunch frequency 100 kHz is achieved with corresponds to 100 mkA beam current
rel. beam propagation
Aluminum foil before and graphite foil after undulators
19
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 20
signal from PEA
1 – foil input and camera
PEA
Short X-Ray Pulses Generation
graphite and aluminum foils
1 – without lasing
2 – FEL lasing
3-5 – graphite foil-4
6-8 – aluminum foil-4
9 – graphite foil-5
beam image
beam propagation
20
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия
graphite and aluminum foils
with and without plumbum shield

## Slide 21
signal from PEA
Experiment results
beam propagation
21
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 22
The possibility of generating short X-ray pulses has been experimentally shown
Registered radiation bunch duration is about 1 ns, which is determined by photo electronic amplifier resolution
Beam repetition rate reached 100 kHz and beam current reached 100 mkA.
The beam propagation rate was obtained at the level of 70-80% depending on the regime.
A further increase in frequency is associated with beam losses, which will be eliminated using
  experimental adjusting of the optic, based on the calculated regime
  decreasing the emittance on the foil using the optical diagnostic station
  additional installation of a quadrupole lens closer to the foil
  replacing the foil with a thinner one
The generation of short X-ray pulses at the NovoFEL looks promising
Conclusion
22
XIV Международный Семинар по Проблемам Ускорителей Заряженных Частиц, 20-25 Сент. 2022, Крым, Россия

## Slide 23: Спасибо за внимание!