## Slide 1
NICA BEAMLINES AND STATIONS FOR APPLIED RESEARCH
Presenter:
Georgii Filatov
on behalf of team
INTRODUCTION
General information about the NICA accelerator areas for applied research.
Stations requirements and equipment for applied research
Beam lines for stations based on ion Nuclotron beams
The first commissioning of the beam line and Station of CHip Irradiation (SOCHI).
Conclusion/plans
*SOCHI, SIMBO, ISCRA beam lines and station are discussed in this report

## Slide 2
RADIATION DAMAGES IN MICROELECTRONIC
Dependence of the latch-up effect cross section in microchip from ions LET range
For example: Single Event Lаtchup
Chart: Au in Si
| 0.30463038180341184 | 0.33001624695369619 | 0.35540211210398048 | 0.40617384240454912 | 0.45694557270511776 | 0.5077173030056864 | 0.5584890333062551 | 0.60926076360682369 | 0.66003249390739238 | 0.71080422420796097 | 0.76157595450852966 | 0.81234768480909825 | 0.86311941510966694 | 0.91389114541023553 | 1.0154346060113728 | 1.1423639317627945 | 1.269293257514216 | 1.3962225832656376 | 1.5231519090170593 | 1.6500812347684808 | 1.7770105605199025 | 1.9039398862713242 | 2.0308692120227456 | 2.284727863525589 | 2.5385865150284319 | 2.7924451665312753 | 3.0463038180341186 | 3.1999898456539397
 | 36.39 | 38.51 | 40.52 | 44.21 | 47.52 | 50.51 | 53.24 | 55.74 | 58.05 | 60.18 | 62.17 | 64.03 | 65.77 | 67.4 | 70.39 | 73.68 | 76.56 | 79.09 | 81.34 | 83.34 | 85.11 | 86.7 | 88.16 | 90.11 | 91.12 | 92.19 | 92.97 | 93.31
 | 93.52 | 93.88 | 94.17 | 94.05 | 93.64 | 93.05 | 92.33 | 91.53 | 90.68 | 89.8 | 88.9 | 88.01 | 87.12 | 85.64
GCR spectra for several ions [1]
Galactic Cosmic Rays: protons and ions Z=2 to 92, E up to 1011 GeV
not all modern microchips allow the process of decapsulation
Dependence LET VS Ion energy
NICA accelerator: HILAC (рус. ЛУТИ) CAN BE USED
[1] M.A. Xapsos, P.M. O'Neill, and T.P. O'Brien, “Near-Earth space radiation models,” , IEEE Trans. Nucl. Sci., vol. 60, no. 3, pp. 1681-1705, 2013

## Slide 3
Spectrum of LET in Si microchip for 197Au79+ ions at initial
energy 250 MeV/n after their deceleration in the
degrader system (set of polyethylene plates of different
thickness)
Modern microchips irradiation without decapsulation
The ions like 131Xe54+ and 197Au79+ at energy of 150-200 MeV/n are decelerated in microchip package to energy of 5 -10 MeV/n corresponded to the Bragg peak.
Peculiarities: long pulse duration and very good uniform extracted beam distribution in time
Spill of Kr ion beam extracted from Nuclotron
New Nuclotron beamlines applied for radiobiological researches and chip irradiations
IRRADIATION BY HIGH ENERGY IONS
The lower energy,
the greater energy and LET spread.
Radiobiological experiments
with dose 1-2 Gy
Intermediate energy of 0.5 – 1 GeV/n
Investigation:
  interactions of ions and bio objects
  genetic mutations
  morphological changes

## Slide 5
Special area-1 (SIMBO, ISCRA) | Special area-2 (SOCHI)
NuclotronIon Ion beams of intermediate energies | HILAC Ion beams of low energy
Radiation damages in microelectronic: Irdiation Station of Components of Radioelectronic Apparatuses (ISСRA) Radiobiological Researches: Station of Investigation of Medico-Biological Objects (SIMBO) | Radiation damages at microelectronic Station Of Chip Irradiation (SOCHI).
Shorted NICA’s scheme

## Slide 6
STATIONS
Parameter | SIMBO | ISCRA | SOCHI
Ion type | 40Ar18+, 56Fe26+, 84Kr36+ |  | 12C4+, 40Ar10+, 131Xe22+, 84Kr14+, 169Tm21+, 197Au31+, 209Bi34+
 | 12C6+ | 131Xe54+, 197Au79+ | 
Ion energy, MeV/n | 400-1100 | 150-425 | 3,2
Beam intensity, particles per pulse | 106-3×109 | 3×104-108 | 108-6×109
Beam emittances (95%), x/y (mmmrad) | 3-10/ 8-15 | 5-17/ 13-25 | 10/10
Mean particles flux density, particles/(cm2.s) at the target | 103-105 | 102-3×105 | 103-105
Pulse time | 2-20 s |  | 0.5-8 μs
Ionization chamber № 2 based on the IC64-16 (Pyramid Technical Consultants, Inc) strip ionization chamber is a duplicating of detector № 1 is used to measure ion flux density and beam profiles in the non-scanning mode during beam adjustment before the experiment.
The equipment for the SIMBO station is being developed as part of the JINR-VST collaboration. Some detectors:
Ionization chamber № 3 a slanted multi-section dosimetric ionization chamber with column recombination suppression is used to determine the absorbed dose.
precision linear movement
longitudinal axis ±100 mm,
transverse axis ±100 mm,
vertical axis +600 mm,
angular movement 10 degrees/sec.
The primate's fixation chair
JINR- Ostec-EC Enterprise collaborations
Positioning device for irradiated objects

## Slide 7
ISCRA station
The equipment for the ISCRA station is being developed as part of the JINR-NRC Kurchatov Institute, ITEP-SPELS/MEPhI-GIRO-PROM collaboration.
The station includes the following components:
Energy degrader;
Test object positioning system;
Six-channel stepper motor controller;
System of ion beam profile projection and video control;
System of positive temperature setting for test objects (+25°C … +125°C, ±5°C, 10 min);
System of negative temperature setting of test objects (minus 60 ºС … 0 ºС, ±5ºС, 15 min);
Chamber with drained atmosphere for testing at negative temperatures;
Universal test board for device under test (DUT)
Scintillation-fiber detector;
Ionization chamber 1;
Proportional wire ionization chamber 2 (128-channel);
Miniature gas-filled ionization chamber 3;
Silicon detector;
A particle flux density meter;
Workplace in the Measurement Hall of Building 1
DUT: device under test

## Slide 8
SOCHI STATION (AND DETECTORS)
positioning system for DUT,
universal test board for connecting test equipment with DUT,
DUT,
a heating module,
a phosphor detector of full absorption, a gas analyzer.
main vacuum chamber
DUT: device under test
5/ fast phosphor detector
to measure beam profiles
3/ A Faraday cup
to control the ion flux density during beam adjustment
2/ MCP-based detector
used for nondestructive control of the intensity and spatial distribution of the ion beam in the horizontal plane during irradiation
4/ fast scintillation
detector
1/ online diagnostics and control of peripheral ion flux density and fluence
(system comprised of four scintillation-fiber detectors based on multichannel photomultipliers).
developed as part of JINR-NRC KURCHATOV INSTITUTE collaboration with the participation of SPELS/MEPhI—GIRO-PROM—VST.

## Slide 9
ISCRA ― Irradiation Setup for Components of Radioelectronic Apparature, technical station is applied for irradiation by ions at energy of 150..500 MeV/n
Measurement Pavilion Infrastructure
SIMBO ― Setup for Investigation of Medical Biological Objects, biological station is applied for irradiation by ions at energy of 400..1100 MeV/n

## Slide 10
type 2,
bore 160
type 1,
bore 108
beam line equipment
 | Scanning | Quadrupole |  | 8-pole
Parameter | SMX/SMY | Type 1 | Type 2 | 
# magnets | 2+2 | 6 | 2 | 2
Gap/bore Ø (mm) | 140 | 108 | 160 | 105
Field/Gradient (T, T/m, T/m3) | ± 0.8 | 0.6 - 5.4 | 0.2 - 1.4 | 1098
Leff (mm) | 356 ± 4 | 492 ± 2 | 480 ± 2 | 505 ± 3
Good Field Region (mm) | H×V 60x60 | Ø 100 | Ø 128 | Ø 90
Rel. integrated field error x10-3 | < ±5 | < ±5 | < ±5 | < ±5
Operating mode | Scanning f=0.5-3Hz | DC | DC | DC
Mechanical layout of the quadrupoles

## Slide 11
Octupole irradiation mode
Mechanical layout of
the octupole magnet
Chart: X, m
large target area up to
  200×200 𝑚𝑚2 (ISCRA)
  100×100 𝑚𝑚2 (SIMBO)
For the 3-Hz repetition frequency homogeneity at the targets is better than 5%
Spiral and string scanning mode
Mechanical layout of the SMX scanning magnets
50000 Particles
To reach Beam homogeneity on the target better than 10%.
In ISCRA channel, two octupole magnets required
Scanning irradiation mode
spiral mode at the target

## Slide 12
For the magnets | octupoles | Type 1-2 (108, 160) | Sp94 | SM
PS type | SM 18-50 | SM 45-140 | ИП 635-230 | PA-400-350
Output voltage/Output current, (V/A) | 10/ 0.5 ÷ 20 | 50/3 ÷ 120 | 230/ 120÷635 | ±350 V/ ±400 A
Output signal relative uniformity | +/- 0.1% | +/- 0.1% | +/- 0.01% | N/A
Operating mode | DC |  |  | Scanning
Cooling | Air | Air | Water | Air
Manufacturer | DELTA ELEKTRONIKA |  | LM Inventor | IECO
The power supplies were delivered at JINR in the end of 2021, except for scanning magnets.
The control of power supplies will be realized via Profibus and integrated into the NICA’s control system.
measurements irradiation parameters:
  the ion beam profiles,
  the primary ion fluence
  and the primary ion density flux.
1 - Ionization chamber,
2 - Scintillating Fiber-based beam position Monitor,
3 - Online Detector (ion hallo)
Beam line detectors
SIMBO Collimator
A 500 mm length
beam limiting
movable collimator
with set of inserts
of various inner diameters
for formation of a sharp boundary irradiation field
PS for magnets

## Slide 13
SOCHI BEAM DESIGN
high beam current of few mA coming from the HILAC-Booster channel
HILAC (рус. ЛУТИ)
12C4+ to 197Au31+ (3.2 MeV/n)
decapsulated chip irradiation
CAN BE USED
by means of collimator
20 mm × 20 mm
homogeneity 10%
beam size is needed to be huge (more 70 mm In diam.)
beam currents of nA
the dose rate should not exceed 1 rad/µs to not distort test results
AT THE TARGET
Dispersion function to get beam in diameter at the station > 70 mm
Leads to small beam size (30 µm)
foil target:
20 holes
⌀ 30 μm
Step: 700 μm
50 μm stainless
collimator
movement system VAb Vacuum-Anlagenbau GmbH
the positioning accuracy is ±100 μm
controlled by a linear potentiometer
way of movement is 100 mm
13

## Slide 14
dipole
5 quadrupole magnets (3 HILAC-Booster +2 SOCHI )
the air-cooling of the magnet coils
the magnets operated in the pulsed mode (except steerer)
pair of two-coordinate steerers
(DS, 1 HILAC-Booster + 1 SOCHI )
magnet similar to those in the HILAC-Booster transfer line
Dipole magnet | 
Type of power source | Pulse
Effective length, m | 0.65
Max. magnetic field, T | 1
Gap, mm | 45
Parameter/magnet type | DS | QS | CS
PS/ Magnet quantity | 1/1 | 2/2 | 1/1
Beam line | SOCHI |  | 
PS type/ mode | Pulse (1 Hz) |  | DC
Max. voltage /current, V/A | 900/ 450 | 800/ 230 | 20/ 10
Stability × (±1·10-3) | 0.15 | 1 | 0.2
Half sin pulse length, ms | 90 | 30 | -
Manufacturer | JINR |  | 
Quadrupole lenses | 
Type of power sources | Pulse
Effective length, m | 0.29
Max. gradient, T/m | 10
Gap (diameter), mm | 95
Steerers | 
Type of power sources | DC
Effective length, m | 0.25
Max field, T | 0.05
Gap, mm | 125 × 110
SOCHI MAGNETS AND PS
SOCHI PS
14

## Slide 15
1 - dipole magnet,
2 - third vacuum post,
3 - corrector,
4 - first quadrupole lens,
5 - second vacuum post,
6 - second quadrupole lens,
7 - first vacuum post,
8 - SOCHI station.
SOCHI VACUUM TESTS
The mass spectrum of the residual gas
The volume with microchips samples have a high level of gas flow and low vacuum level
Vacuum system in the SOCHI station and(or) beam lines
-cryogenic traps,
-a pulsed diaphragm (butterfly valves),
-pumps
will be prevent spoiling the vacuum condition in the HILAC-Booster beam line
the residual gas pressure is lower than the pressure in the HILAc-Booster channel (10-6 Pa)

## Slide 16
SOCHI PHYSICAL START-UP (December 2021)
The photo shows the beam spot on a phosphor detector. Shadows from the system for online.
The beam spot at the target
nonuniform structure of the striped character
To provide good dose uniformity on the target when using a small ion beam, the collimator was modified
several slits
260 μm35 mm,
30 μm×35 mm,
234 holes 30×15 μm with a step of 150 μm
An experiment on a target with a new collimator configuration will be carried out in further sessions on the SOCHI equipment.
Beam from HILAc:
Energy: 3.2 MeV/n
Ions: 12C4+
current 3.5 mA,
pulse duration 3 μs,
repetition frequency 4 s.

## Slide 17
http://science-tv.jinr.ru/videonews/ https://www.youtube.com/watch?v=1sPX0y0I-T8
Collider NICA
The physical start-up of the SOCHI equipment was carried out in December 2021.
Further commissioning work will continue in 2022 on argon ion beams.
The works related to the installation of the SIMBO and ISCRA stations equipment are planned for late 2022/2023.
Conclusion
SIMBO, ISCRA
SOCHI