## Slide 1
Raman Spectroscopy
in Life Sciences
Grigory Arzumanyan
Sector of Raman Spectroscopy, FLNP
Centre “Nanobiophotonics”

## Slide 2
2
2
OUTLINE
Introduction in brief: Raman effect
  2. Enhanced Raman microspectroscopy:
    CARS – Coherent antiStokes Raman Spectroscopy
  SERS – Surface-Enhanced Raman Spectroscopy
  TERS – Tip-Enhanced Raman Spectroscopy
  …
3. “CARS” microspectrometer at FLNP – description and
operating modalities
  4. Examples of applications in Life Science

## Slide 3
Raman effect is a vibrational molecular spectroscopy which derives from an inelastic light scattering process – a laser photon is scattered by a sample molecule and loses (or gains) energy during the process.
3
Diagram of the Rayleigh and Raman Scattering Processes
The amount of energy lost is seen as a change in energy (wavelength) of the irradiating photon. This energy loss is characteristic for a particular bond in the molecule.

## Slide 4
4
Classical Raman Physics
Polarizability induced dipole equation
The shift in frequency corresponds to the energy of the vibrational motion of the molecules – they are unique for each molecular spices.

## Slide 5
The effect was predicted theoretically by Adolf Smekal in 1923
Discovered by Prof. C.V. Raman and K.S. Krishnan (student of C.V. Raman) in liquids (Calcutta, 28 Feb., 1928),
and independently by
Academicians G.S. Landsberg and L.I. Mandelstam in crystals (Moscow, MSU, 21 Feb., 1928)
C.V. Raman
G.S. Landsberg
L.I. Mandelstam
A.G. Smekal
The Nobel Prize in Physics in 1930 was awarded to Sir C. V. Raman "for his work on the scattering of light and for the discovery of the effect named after him."
2023 – 95th anniversary of the Raman effect
K.S. Krishnan
5

## Slide 6
Historical photos of the discovery
Raman - Krishnan
scattering spectrum,
benzene
incident light
scattering spectrum,
quarts seal (rhinestone)
Landsberg - Mandelstam

## Slide 7
What can Raman spectra tell us?
Vibrational frequencies are characteristic of chemical bonds in a specific molecule.
Peak intensity is proportional to the concentration of a substance.
Shifts of vibrational frequencies are sensitive to local environment of a molecule, such as crystal phase, local strain, and degree of crystallinity.
The frequencies of vibration depend on the masses of the atoms involved and the strength of the bonds between them. Heavy atoms and weak bonds have low Raman shifts. Light atoms and strong bonds have high Raman shifts.
7
Raman spectroscopy produces chemical and structural information.
Raman effect is also known as a “fingerprint spectroscopy” as each molecular species has its own unique fingerprint.
Raman spectroscopy can be used to study solid, liquid and gaseous samples.

## Slide 8
Region - I : (below 1500 cm-1) – “fingerprint region” – individual characteristic of each substance.
Region - II : (1900 – 1500 cm-1) – “double bonds” – valent stretching modes: СС, СO, CN, ...
Region - III : (2500 – 1900 cm-1) – «triple bonds» СС, CN, …
Region - IV: (3700 – 2500 cm-1) – “hydrogen region”: H-X, where Х: С, O, N, S
Interpretation of Raman spectrum
8
Raman effect is also known as a “fingerprint spectroscopy” as each molecular species has its own unique fingerprint.

## Slide 9
Raman and IR spectroscopy are complementary techniques.
The main specificity distinguishing Raman/IR spectroscopy from other spectroscopic methods – both of them are molecular vibrational spectroscopy
9
Although the spectral features of Raman and infrared spectra can be interpreted in a similar way the selection rules are different.
Infrared absorption is sensitive to the change of the dipole moment µ during the vibration.
A Raman active vibration is sensitive to the change of polarizability ɑ during the vibration.

## Slide 10
Raman microscopy (imaging) –
a powerful tool for generating selective chemical images based on analyte molecules Raman spectrum
Raman peak intensity yields images of analyte concentration and distribution.
Raman peak position yields images of molecular structure, conformation, etc.
Raman microscopy is a good alternative to fluorescence microscopy, and Raman has a remarkable advantage over it: no photobleaching of the fluorophore, stable work with live cells.
10

## Slide 11
Raman applications
Key applications
Other applications – any application where non-destructive, microscopic, chemical analysis and imaging is required: pharmaceutics, forensics, art, etc., etc.
Raman spectroscopy is one of most versatile analytical techniques.
11

## Slide 12
12
ADVANTAGES & LIMITATIONS of RAMAN MICROSPECTROSCOPY
Main advantages
very high sensitivity (enhanced Raman, SERS, CARS, …)
non-invasive probing (controlled by laser power & λ)
short-term analysis (a few seconds, enhanced Raman)
compatibility with water solutions (not the case for IR)
non-photobleaching signal for live cells studies
chemical imaging without exogenous tags
single excitation wavelength
a small sample volume and simplicity of preparation
Major limitation of spontaneous Raman:
weak signal which limits its practical application – 1 in 106 incident photons are Raman scattered

## Slide 13
13
OUTLINE
Introduction in brief: Raman effect
  2. Enhanced Raman microspectroscopy:
    CARS – Coherent antiStokes Raman Spectroscopy
  SERS – Surface-Enhanced Raman Spectroscopy
  TERS – Tip-Enhanced Raman Spectroscopy
  …
3. “CARS” microspectrometer at FLNP – description and
operating modalities
  4. Examples of applications in Life Science
13

## Slide 14
10-30
10-26
10-22
10-18
10-14
RS – Raman Scattering (spontaneous) – weak!
RRS – Resonance Raman Scattering – strong!
CARS – Coherent Anti-Stokes Raman Scattering – strong!
SERS – Surface Enhanced Raman Scattering – very strong!
SECARS – Surface Enhanced CARS
TERS – Tip-Enhanced Raman Spectroscopy – moderate!
SMD – single molecule detection level ~ (10-15)
Modern modalities of enhanced Raman microspectroscopy
14

## Slide 15
CARS is a third-order nonlinear process that involves a pump beam at a frequency ωp and a Stokes beam at a frequency of ωs. The signal at the anti-Stokes frequency is generated in the phase-matching direction.
The sample is stimulated through a four-wave mixing parametric process.
The vibrational contrast in CARS is created when the pump-Stokes frequency difference matches molecular vibration of a particular chemical bond  = ωvib and the oscillations of molecules with that bond are driven coherently. Thus, CARS provides a chemically specific signature of various molecules.
Physical background of CARS in brief
ICARS(ω) ~ |CARS(3)|2 x Ip2 IS x N2
(3) – third-order nonlinear susceptibility
AS = 2pump - Stokes

## Slide 16
HOW it WORKS ?
3078 cm-1
3078 cm-1 corresponds to the pump beam at 803 nm

## Slide 17
Raman resonance CARS-image of polysterene beads
λ (nm)
804
803
802
801
798
799
800
797
CARS
resonance
Transmitted light
F-CARS channel
17
805
weak and
fuzzy image
3078 cm-1
3101 cm-1

## Slide 18
Surface Enhanced Raman Scattering (SERS) –
SERS involves inelastic light scattering by molecules adsorbed onto Ag or Au NPs with nanoscale roughness.
Enhancement factors under suitable conditions can be as high as 108-12, in some specific cases even higher which allow a few molecule detection level.
18
Two main mechanisms of SERS enhancement:
1. Electromagnetic (dominant):
- collective oscillations of free electrons (plasmons) in the metallic nanostuctures upon a laser excitation. Enhancement by local optical fields close to surface of metallic NPs at resonance conditions – surface plasmon resonance (SPR).
2. Chemical (much weaker than 1):
- charge-transfer (electrons) process in the ground and excited states of the adsorbed molecule-metal system (metal-molecule bonds).
SERS is a plasmonic-based technique developed to detect extremely small quantities of molecules by determining their characteristic Raman signal.

## Slide 19
19

## Slide 20
SERS-active substrates:
existing commercial products
20
At present the main challenge in SERS is a fabrication of the novel effective and inexpensive plasmon nanostructures with well-defined nanoscale geometry demonstrating strong, reproducible and stable Raman signal.

## Slide 21
SERS-active substrates based on porous silicon
Plasmonic nanostructure design (developed in BSUIR, Minsk, Belarus):
Template: porous silicon (PSi) formed by an electrochemical anodization in a solution of HF (45%)
Ag nanoparticles: immersion plating in 1mM AgNO3 aqueous solution with an ethanol additive during 5-25 min.
Reflectance spectra of the samples:
for (a) 5 and (b) 25 min immersion.
The formed PS layer has the thickness of 5 µm and the porosity of 75 %.
SEM images of the samples formed by the immersion deposition of silver on PS for (a) 5 and (b) 25 min
The packing density of the silver particles is estimated to be 60 % after 5 min immersion and 75 % after 25 min immersion.
21

## Slide 22
Tip Enhanced Raman Scattering (TERS) or nano-Raman –
brings Raman spectroscopy into nanoscale resolution imaging
TERS imaging is performed with an AFM-Raman spectrometer, a SPM integrated with an optical micro-spectrometer.
TERS combines the chemical sensitivity of surface-enhanced Raman spectroscopy (SERS) with high spatial resolution of scanning probe microscopy (SPM) and enables chemical imaging of surfaces at the nanometer length-scale.
TERS image of single wall carbon nanotubes with spatial resolution of ~ 30 nm
22
TERS signals are not strong enough because
there is only one tip working as a signal amplifier.

## Slide 23
“CARS” microspectrometer
Laser scanning confocal luminescent microscope –
developed and fabricated at “SOLAR” / “SOL Instruments”, Minsk, Belarus
23

## Slide 24
Raman
Multimodal optical platform at FLNP
24
Second harmonic &
sum frequency
generation
F-CARS, E-CARS, P-CARS
SERS
SECARS
SHG, SONICC
Transmitted and reflected channels
Up-conversion luminescence
“CARS” microscope

## Slide 25
Optical layout of the “CARS” microspectrometer
25

## Slide 26: Picosecond CARS laser, “EKSPLA” (Lithuania)
1 – picosecond Nd:YVO4 laser; 2 – picosecond SOPO (LBO); 3 – module for formation and combination of the pump (SOPO) and Stokes (Nd:YVO4) beams; 4 – HeNe laser
1
2
4
3
Nd:YVO4 laser parameters:
Master oscillator – diode pumped mode-locked ND:YVO4 laser:
- wavelength – 1064 nm
- pulse duration – 7 ps
- output power – 6 W @ 1064 nm and 2.5 W @ 532 nm
- repetition rate – 85 MHz
Synchronously pumped optical parametric oscillator (SOPO)
- pump wavelength: 532 nm
- tuning range: (690 – 990) nm
- pulse duration: 6 ps
- output power ̴ (150-350) mW
- spatial mode – TEM00
- linewidth: < 7 cm-1
- scanning step: 0.1 nm
26

## Slide 27
27
OUTLINE
Introduction in brief: Raman effect
  2. Enhanced Raman microspectroscopy:
    CARS – Coherent antiStokes Raman Spectroscopy
  SERS – Surface-Enhanced Raman Spectroscopy
  TERS – Tip-Enhanced Raman Spectroscopy
  …
3. “CARS” microspectrometer at FLNP – description and
operating modalities
  4. Examples of applications in Life Science
27

## Slide 28: Raman, CARS and SHG (SONICC) imaging of bacteriorhodopsin (BR) crystals as a model of membrane proteins (MP)
MOTIVATION
Membrane proteins (MPs) are responsible for vital functions of the cells and their studies are of great importance for both science and practical medicine.
Structural study of MPs is a major challenge due to dramatic difficulties with growing, detection and imaging of the crystals suitable for X-ray crystallography.
28
1
MPs represent roughly one-third of the proteins encoded in the human genome.
They are also extremely important drug targets (up to 60% of all existing drugs target MPs).

## Slide 29
1529cm-1
1529cm-1
1529cm-1
P-CARS resolves tiny features of BR morphology and displays several defects visible as dark parts of the crystal, the edges of the crystal are not smooth.
Stair-like morphology of the surface of the crystal is well defined (useful in crystal growth).
Optical microscope image gives an impression that the crystal is perfect with the only visible edge defect.
The same conclusion can be made with the Raman image.
29

## Slide 30
3D-sectioning
Imaging of twinned BR crystals –
one of the most common crystal-growth defects in protein crystallography.
Scan area 48x48um, resolution: 2pl/1µm,
data accumulation time ~ 2s
P-CARS, 1529сm-1
Raman spectra in the central part
of the BR crystal is similar to that of in the boundary rim.
The boundary rim is not well ordered part of the crystal
and SONICC fails to display any signs of the rim.
30

## Slide 31
Identifying the smallest sized BR crystals (~4 µm down to submicron)
by P-CARS vs SONICC (SHG)
P-CARS, 8x8um
P-CARS, 8x8µm
SONICC, 8x8µm
Scan area 8x8um
Resolution: 2pl/1µm
Data acquisition time ~2s
P-CARS image at ~ 1529cm-1
SONICC image at SHG (532nm)
P-CARS, 8x8µm
31
JACS, 2016, 138(41))

## Slide 32
32
Raman detection of a few/single molecule(s)
for ultrasensitive biosensing
2

## Slide 33
Ultrasensitive detection of lactoferrin molecules covered by graphene at attomolar concentration by Raman spectroscopy
SERS spectra of lactoferrin at 10-6 to 10-18 M concentrations obtained by the collection of the SERS spectra maps (10 х 10 µm)
Most of the lactoferrin Raman bands are presented in the spectrum at the 10-18 M concentration:
1002 cm-1 (Phe), 1290 cm-1 (Amide III), 1340 cm-1 (Trp), 1440 cm-1 (CH2), 1605 cm-1 (Tyr) and 1642 cm-1 (Amide I).
Biosensors, 2019, 9, 34
Graphene heat sink –
overcoming the limitation
10-18M
33
Lactoferrin is a multifunctional glycoprotein that is widely represented in various secretory fluids, such as milk, salvia, tears, etc.
Lactoferrin is one of the components of the immune system of the body and is part of the innate defense.

## Slide 34
34
Silver 3D dendrites in SERS
Advantages for SERS spectroscopy
Excitation upon a wide range of laser wavelengths (including IR) due to the wider spectral SPR (surface plasmon resonance) band due to the longitudinal and transverse modes.
Use of low laser powers and portable instrumentation for biosensing due to richly-developed dendrites’ morphology that possesses much more hot spots compared to the 2D nanostructures.

## Slide 35
35
Average SERS spectra for three maps of the Ag dendrites/macro-PS kept in the DTNB solutions with different concentrations. The excitation wavelength 785 nm.
Distribution maps of 1338 cm-1 band (intensity in the SERS spectra of DTNB molecules from solutions at concentrations: (a) 10-6 M ; (b) 10-18 M
-------------------------------------------------------------------------
1338 cm-1 – symmetric nitro stretching mode s(NO2)
1558 cm-1 – aromatic ring stretching mode
Raman reporter: DTNB
Dithionitrobenzoic acid
1338 сm-1
1558 сm-1
J. Appl. Phys, 2019, 126
Silver 3D dendrites for attomolar limit of analyte
molecules detection by SERS

## Slide 36
Addition of various molecules to the membrane can change its physical properties and alter its structure, which in turn may affect its functionality.
36
Raman sturdy of conformational changes in model lipid membranes with additives: cholesterol and melatonin
Lipids are one of the most important classes of biomolecules involved in cell vitality – cellular signaling, energy storage and building of cellular membranes.
3

## Slide 37
Ternary system – Lipid / Cholesterol / Melatonin
Cholesterol and melatonin incorporate into
the lipid bilayer at different positions
37
Cholesterol is located mainly in lipid tails region
Melatonin resides in the head-group region

## Slide 38
The spectral range of 1030 cm-1 – 1150 cm−1
is sensitive to trans/gauche conformations, has the three dominant Raman bands (1062 cm −1, 1096 cm −1, 1127 cm −1 ) and can serve as an spectroscopic markers indicating phospholipids’ hydrocarbon chains ordering and disoredering.
Raman spectrum of pure DPPC
trans conformer
gauche conformer
1062
1096
1127
38

## Slide 39
Area of impact of melatonin
Schematic illustration of the preferential areas of influence of melatonin and cholesterol
Raman band 1127 cm-1 is most sensitive to changes resulting from the addition of Cholesterol
Raman bands 1062 cm-1 and 1096 cm-1 are most sensitive to changes resulting from the addition of Melatonin
1062
1096
1127
Area of impact of cholesterol
The dynamics of hydrocarbon chains represented by the ratio of trans/gauche conformers (S1062/S1096 , S1127/S1096) serves as an index of the strength of the lattice order/disorder effects in lipid bilayer

## Slide 40
DPPC+Cholesterol
DPPC+Melatonin
Сondensing effect of cholesterol and the fluidizing effect of melatonin
The dynamics of hydrocarbon chains represented by the ratio of trans/gauche conformers (S1062/S1096 , S1127/S1096) serves as an index of the strength of the lattice order/disorder effects in lipid bilayer

## Slide 41
41
MAIN RESULTS
Raman spectroscopy demonstrates high sensitivity to the
trans/gauche conformers alterations with additives.
With cholesterol lipid molecules become more ordered and membrane became stiffer and thicker (condensing effect).
Melatonin decrease order of lipid molecules and membrane became more fluidic and thinner (fluidizing effect).

## Slide 42
42
Raman biomarkers as a diagnostic tool
of various diseases
4.

## Slide 43
Comparison of Raman "fingerprint" bands of C6 glioma tumor cells and mesenchymal stem cells (MSC)
The revealed spectral differences in the Amide-I (1600 – 1700 cm-1) line of tumor and healthy cells are related to tumor C6 glial cells.
An area where there are no glioma tumor cells
tumor focus
A horizontal section of a rat brain
artificial holes
Right hemisphere, C6
Left hemisphere, no C6
JSCRT, 1(1), 2016
Stem cells – the earliest type of cell in a cell lineage

## Slide 44
CARS microscopy for tissue imaging
Cancer tissue,
CARS imaging at 2850 cm-1
Healthy tissue,
CARS imaging at 2850 cm-1
N. Vogler, Y. Popp, et al. @ 4th Int. Graduate Summer School: Biophotonics '09
CARS images of physiological and pathological tissue of the colon
44

## Slide 45
NETosis – a special form of programmed cell death
Classic or suicidal NETosis
Vital NETosis
Neutrophils are the largest population of myeloid leukocytes, which normally comprise 50-70% of all white blood cells
5.

## Slide 46: Neutrophils and NETosis NETs – Neutrophil Extracellular Traps
Neutrophil cells are the immune system's first line of defense against bacterial, fungal and in viral infections
In the cytoplasm of neutrophil cells there are granules with antimicrobial agents
NET has an electrostatic charge which holds pathogens
Raman spectroscopy as an early diagnostic tool
Protective capabilities of neutrophils
Phagocytosis
Chromatine decondensation
Formation of NETs
46

## Slide 47
Raman spectrum: low-frequency range of citrulline line evolution indicating the pre-activation of NETosis
Raman Marker of NETosis
Since NETosis is a process of programmed neutrophil cell death, the growth of the “citrulline” peak in Raman spectrum indicates that cell death will occur soon.
J. of Raman spectroscopy, 2020, https://doi.org/10.1002/jrs.5844
NETs preformation: citrullination of histones (nuclear proteins)
The averaged Raman spectrum of neutrophils chemically activated (30 min)
The averaged Raman spectrum of neutrophils activated with bacteria (40 min)
Raman spectroscopy serves as an early diagnostic tool

## Slide 48
Light (UV and visible) induced NETosis
(the article is currently under publication)
Every day, the human skin is exposed to the wide spectrum of electromagnetic radiation of sunlight, including ultraviolet radiation (UV). The whole spectrum of UV covers the wavelengths between 200 and 400 nm and is divided into three ranges: UVA (400–315 nm), UVB (315–280 nm) and UVC (280–200 nm).
UVC is completely absorbed by gases in the Earth atmosphere, but 10% of UVB and almost 100% of UVA reach the Earth surface.

## Slide 49
49
SUMMARY
Raman microspectroscopy is a powerful and sensitive tool for Life Science.
Nonlinear CARS microscopy is an efficient and fast technique for imaging with much stronger signal and chemical contrast without using tags.
SERS is a technique to detect extremely small quantities of molecules (single molecule level) by determining their characteristic Raman signal.

## Slide 50
Thank you!
50