## Slide 1
«Разработка и создание газонаполненных детекторов на основе строу-трубок нового типа для работы в вакууме в трековом спектрометре установки NA62»
K+  π+νν
Глонти Л.Н.
Даниелссон Х. (H.Danielsson)
Еник Т.Л.
Кекелидзе В.Д.,
Колесников А.О.
Мадигожин Д.Т.,
Мовчан С.А.,
Потребеников Ю.К.
Самсонов В.А.,
Шкаровский С.Н.
Тема 1096

## Slide 2
NA62 Project
NA62 Collaboration:
- 13 countries
- 32 institutions
- 238 participants
Spokesmen – A.Ceccucci
K+  π+νν
P326:
- 16 institutions
- 95 peoples

## Slide 3
K→πνν in New Physics
Searches for NP in K→πνν:
Complementary to LHC
Several scenarios possible
Measurements of charged and neutral mode will allow to discriminate between New Physics scenarios
D. Straub @ CKM-2010 arXiv: 1012.3893
Grey: ruled out
SM: Standard Model
SM4: SM with 4th generation
RSc: custodial Randall-Sundrum
LHT: littlest Higgs with T-parity
MFV: minimal flavor violation
Theory:
BR(K0→π0νν) = (2.43 ± 0.39 ± 0.06 ) x 10-11
BR(K+→π+νν) = (7.81 ± 0.75 ± 0.29 ) x 10-11
E787/E949 experiment @ BNL
E391 experiment @ KEK

## Slide 4
NA62 goals
Main goal:
Collect O(100) signal events in 2-3 years
(1013 kaon decays, 100 times more than in the NA48/2 experiment)
Measure BR(K+→π+νν) with 10% precision
Further goals:
Measure |Vtd| with ~10% accuracy
Probe several New Physics scenarios in K+→π+νν
Probe New Physics in similar processes (e.g. K+→π+X)
Beyond the baseline:
LFV/LNV decays with 3 tracks in the final state
Heavy neutrino searches (K+  m+nH)
π0 decays
Dark photon searches (π0  gA’; A’  e+e-, A’  m+m-)
K+p+p0P (pseudoscalar sGoldstino, should exists in model with
spontaneous symmetry braking, V.Rubakov)

## Slide 5
Signal vs background
Main kinematical variable for the signal:
m2miss = (PK – Pπ)2 is measured in two regions (I and II)
Background:
Kaon decays
Accidental tracks in time with kaon tracks
Beam-gas and upstream interactions
Region I: 0 < m2miss < 0.01 GeV2/c4
Region II: 0.026 < m2miss < 0.068 GeV2/c4

## Slide 6
SPS to NA62 detector
SPS primary beam: 400 GeV/c, ~1.1∙1012 protons/s on target
Secondary hadron beam: 75 GeV/c, ~780 M particles/s, ~6% of K+
~4.8∙1012 kaon decays per year (~10 MHz event rate downstream)
~10% signal efficiency
~50 signal events per year

## Slide 7
Straw spectrometer
4 straw chambers in vacuum + spectrometer magnet
Straw chamber:
4 views x 4 planes/view
Mylar straw tubes: R=9.8 mm, L=2.32 m
112 Mylar tubes per plane, 7168 in total
X/X0 ~0.1% per view
Magnet:
B ~ 0.36 T
pT = 270 MeV/c
Performance:
Spatial resolution < 130 μm per straw
Momentum resolution dp/p ~ 0.32% + 0.008%*p

## Slide 8: Design and assembling of the first straw prototype
48 straws:
36 - Al
12 - Cu+Au

## Slide 9: Test run 2007
Main goal: estimation of a straw spatial resolution
Statistics:
Muon beam - 160M
Pion beam - 60M
Kaon beam - 550M
-----------------
Total - 770M
~127 m from
a beam target
~90 m to DCH
Trigger condition:
Q1 x 1-track
~105 triggers/burst
(burst - 16.8/4.8 s)
TDC resolution – 97.66 ps
ASD-8 chip in FEE

## Slide 10
Test run 2008
Non-inflammable gas mixture:
CO2+isoC4H10+CF4 (82%:5%:13%)
Burst - 43.0/4.8 s
TDC resolution – 195.3 ps
CARIOCA and ASDQ chips in FEE
Statistics:
HV | Threshold | Run number |  | Statistics in M
2400 V | 4 - 6 fC | from 21146 | till 21156 | 48.4
2500 V | 4 - 6 fC | from 21157 | till 21161 | 46.5
2600 V | 4 - 6 fC | from 21162 | till 21167 | 41.1
2600 V | 15 - 15 fC | 21168 | 21173 | 22.2
2700 V | 4 - 6 fC | from 21169 | till 21172 | 40.2

## Slide 11
Spatial resolution estimation – 2 algorithm
Th=6 fC
Th=12 fC
Efficiency
R=4.7 mm
99.98%
2400V
2600V
2500V
2400V
2600V
2500V

## Slide 12
Straw view design
p +

## Slide 13
2.1m
x
y
u,v
4 views: x,y,u,v
The straws are mounted individually in “views”
The effective region in Ø = 9.8 mm – 9.4 mm
A hall for beam – by geometry
The detector layout

## Slide 14
Other technology of the straw detector
Ring chamber
Hexagonal bushes and twisters for wire centering;
O-rings for sealing
Stand for testing of the Prototype with 3 straws
Straw drift spectrum
Ch. unit
Optical bunch for straw assembling
Δstraw = 0.15 mm
P - up to 10-6 torr

## Slide 15: Straw mass production
Microscope pictures of a straw cross- section for quality control of the weld
Humidity and temperature
Control at clean room
Common view of
the Clean room
ISO clean room standard 6
600 mm
On-line control of a weld seam by the digital microscope (zoom x20 on a PC monitor)
Unique welding machine

## Slide 16
Off-line tests
Stand for tensile strength
measurement
Optical check of seam quality
Straw long term overpressure test (> 1 month as min)
Straw end-plugs
(bottom with nipple)
Straw storage after 3 bar overpressure test with 1,5 bar overpressure inside
Stand for straw gas leak measurement

## Slide 17
Summary of straw mass production
7032 2.7 m straws have been produced in 3 years
Length of a roll: 300 m 250 m

## Slide 18
Straw data base and its design
NA62 straw label: NA62TASTDU003525
NA62 – NA62 experiment
TA or TR – Tracker
ST - straw
DU–Dubna, JINR, Russia
CE – CERN (Sefar, Swiss)
003525 – straw serial # (000001-999999)
Barcode and the NA62 Data Base

## Slide 19
Detector production at CERN:
Module 1,2,5,6
Mechanical elements are designed together with CERN and are produced on the EUROMEC factory (Italy) with a precision 0.1 mm
Sealing of the Module elements connections by a two-component epoxy resin
Vacuum test of the Module after sealing
The CERN assembling area:
the Module at the designed at Dubna rotation jig for straw-module assembling

## Slide 20
Detector production:
Straw insertion and preparation for tests
Designed assembling tooling allows to glue a half of one layer of straws per day

## Slide 21
Detector production:
straw straightness test and final view
The Module at the stand for straw straightness measurement. This stand based on a laser right finder ILD 1700-50
Each layer is measured after full assembling to check straightness of all straws.
The Modules with fully assembled straws
05.2012

## Slide 22
Detector production at JINR:
Modules 3,4,7,8
Sealing of the Module elements in a special “Dry room”
Vacuum test of the Module after sealing
The JINR assembling area
with 2 assembling jigs
A Module assembly rotation jig

## Slide 23
Detector production at JINR:
straw assembling and wiring
Straw insertion and fixing in a horizontal position of a module frame
Straw gluing from the top and bottom in a vertical position of a module frame
Wiring in vertical position of a module frame
Top side
Bottom side

## Slide 24
Detector production at JINR:
straw positioning test
Laser
Optical ruler
Optical sensor
Optical ruler:
Handenhain
measurement - up to L=4500 mm
accuracy - (1-2) mkm
Stepping motor with raster pattern:
1 step = 10,4 mkm
“Micro Epsilon” Laser sensor:
measurement distance -
L=(30-50) mm
accuracy - 3 mkm
beam diameter – 0.3 mm
INFN
commands
visualization
saving data
Scan indicator
User interface
Example: measurement of a straw shape
and distances between straws in a module view

## Slide 25
Detector production at JINR:
straw pretention test
1500 G
Requirement: F > 1.5 KG  Fr >=65 Hz)
Opto-coupler
Oscilloscope with the FFT function

## Slide 26
Detector production at JINR:
HV and gas leakage test
Requirement:
I < 4 nA at HV = +2200 V
Temp T=(23-25) degree
Humidity H=(35-40) %
Chamber CH2 M1 U-V - HV – OK, L = 0.5 cm3/min
Chamber CH2 M2 X-Y - HV – OK, L = 0.5 cm3/min
Chamber CH4 M1 U-V - HV – OK, L = 0.1 cm3/min
Chamber CH4 M1 U-V - HV – OK, L = 0.1 cm3/min
These tests have been done for last 2 modules simultaneously!

## Slide 27
High-intensity light source
Digital microscope
Wire image in a straw
in reflected lite
The same optical ruler
as was used for straw
position measurement
Two high-intensity
light sources
Detector production at JINR:
straw position measurement

## Slide 28
Module 8 (X-Y):
measurement of distances between wires inside straws
X-plane, layer 1:
Chart: 
| -200 | -160 | -120 | -80 | -40 | 0 | 40 | 80 | 120 | 160 | 200
Bottom, -90 cm 0 | 0 | 1 | 1 | 6 | 6 | 8 | 2 | 0 | 0 | 0 | 0
Middle, 0 cm 0 | 1 | 1 | 3 | 13 | 32 | 25 | 0 | 0 | 0 | 0 | 0
Top, 85 cm 0 | 1 | 0 | 5 | 11 | 6 | 12 | 2 | 0 | 0 | 0 | 0
Chart: 
Bottom, -90 cm | -28 | 1 | -59 | 35 | 37 | -13 | -101 | 77 | -64 | 73 | -6 | -50 | 26 | 44 | -120 | 76 | 17 | -1 | 58 | -64 | -56 | 3 | 71 | 6 | -9 | 35 | -65 | 75 | 102 | 43 | 64 | -29 | 41
Chart: 
Chart: 
Top, 85 cm | -10 | 20 | -18 | 29 | -41 | 75 | -3 | -103 | 110 | 7 | -65 | 33 | -46 | 29 | -50 | 78 | 36 | 19 | -191 | 145 | -13 | -59 | 76 | -84 | 10 | 28 | -43 | 65 | -118 | 122 | -107 | 58 | -57 | 98 | -75 | 75 | -53 | 57 | -59 | 31 | -16 | -15 | 16 | 72 | -105 | 72 | -48 | 50 | 9
49 wires
97 wires
33 wires
RMS for wire positions – 40 ÷ 50 mm
Detector production at JINR:

## Slide 29
Transport from JINR to CERN
Summary
End of assembling

## Slide 30
Integration into the NA62 set-up:
deformations calculation
Interface flange deformation is up to 240 μm, max stud stress – 41 MPa. A straw shift from it nominal position along axial axis is up to 60 μm

## Slide 31
Integration into the NA62 set-up:
tooling, assembling
Table for straw detector assembly
(designed at Dubna)
Stacking tooling
at CERN
Intermediate flanges
Insertion of the straw detector into NA62 experimental set-up

## Slide 32: Electronics schematic view

## Slide 33: Front-end and Read-out electronics

## Slide 34: One of the four chambers during the 2014 run
MPOD with high
and low voltage
modules
(from Wiener)

## Slide 35: DCS panels
Mixer and gas distribution
10 mbar above atmospheric pressure at all times!
Low Voltage
High Voltage
Temperature

## Slide 36: Online monitoring plots
Hit rates in the straws

## Slide 37: Detector performance: three track events run 2014
Selection of K+  π+π+π-
2 positive and 1 negative charge. 3-track vertex (analytical). 4 chamber tracks.
Invariant mass resolution: 0.9 MeV/c2
Invariant mass average: 493.657 MeV/c2 (PDG - 493,667 MeV/c2)
Total momentum [MeV/c]
Invariant mass [MeV/c2]
Invariant mass [MeV/c2]
493.657 MeV/c2

## Slide 38: Run 2017 (2.3*1012 kaon decays)

## Slide 39
Получены следующие результаты:
Разработана и реализована технология изготовления методом ультразвуковой сварки вдоль образующий длинных (до 5,5 м) тонкостенных дрейфовых трубок – строу – нового типа из полиэтилентерафтолата (майлара), а также технология контроля качества при их использовании в качестве элементов изолированного газового объема в детекторах, работающих в вакууме. Изготовленные таким способом строу использованы не только в эксперименте NA62, но и в прототипах детекторов экспериментов COMET (J-PARC, Япония) и SHIP (CERN).
Предложена конструкция детектора заряженных частиц большой площади (около 3,5 м2) для работы в вакууме, построенного на основе нового типа строу-трубок, обеспечивающая регистрацию заряженных частиц с высокой (более 99%) эффективностью в телесном угле до 3о при приемлемом (порядка 0,1 ХО на координату) количестве вещества в объеме камеры на пути регистрируемых частиц и безфланцевым вакуумным объемом на пути частиц пучка.
Характеристики предложенного детектора детально исследованы на разработанном и реализованном в ОИЯИ прототипе, с использованием которого в трех сеансах экспозиции 2007 – 2009 годов накоплено несколько сотен миллионов событий с треками заряженных частиц в его регистрирующей части. Эти исследования позволили оценить достижимое разрешение строу (на «медленном» газе Фреоне-14 было достигнуто разрешение лучше 60 мкм), определить оптимальное геометрическое размещение строу-трубок в рабочем объеме детектора так, чтобы минимум 2 хита от трека в одной координатной плоскости детектора регистрировались в так называемом «эффективном объеме» строу с эффективностью больше 99,98%, выбрать оптимальное преднатяжение строу-трубок для обеспечения их прямолинейности в вакууме.

## Slide 40
На основе изготовленных из покрытого с внутренней стороны 50 нм меди и 20 нм золота 36 микронного майлара 7168-и строу-трубок нового типа диаметром 9,8 мм созданы 8 двухкоординатных (4 слоя трубок на координату) модулей строу-детекторов большой площади регистрации частиц (x 2,1 м) для работы в качестве детекторов трекового спектрометра эксперимента NA62 на SPS в CERN. С этой целью в ОИЯИ и в ЦЕРН были созданы два технологических участка с оснасткой для производства и контроля качества указанных детекторов, включая вакуумные тесты, тесты на натяжение проволок, тесты на измерение расположения трубок и проволок внутри трубок. На каждом из этих участков были собраны и сертифицированы по 4 строу-модуля.
Созданные модули объединены попарно в 4 четырехкоординатных детектора, для чего в ОИЯИ разработана и спроектирована соответствующая оснастка и поддерживающие элементы. Детекторы интегрированы в 2014 году в экспериментальную установку NA62. С 2014 года эти уникальные детекторы успешно эксплуатируются в течение 4-х сеансов экспозиции установки NA62 в качестве детекторов спектрометра заряженных частиц. Характеристики, демонстрируемые детекторами, полностью удовлетворяют требованиям эксперимента по импульсному и угловому разрешениям и по эффективности регистрации частиц.
Исследованы возможности создания подобных детекторов круглой формы, применения плавающих торцевых заглушек строу для равномерного преднатяжения трубок, применения специальных шестигранных конструкций для использования в детекторах трубок с небольшими различиями в диаметрах. Детально изучен вопрос устойчивости строу-трубок в вакууме.
Полученные результаты опубликованы в ведущих научных журналах [1-8] и в виде препринтов ОИЯИ [9-10], доложены на крупных международных научных конференциях [4-8]. По результатам исследований получены 3 патента РФ на изобретения [11-13] .

## Slide 41
1. N.I. Azorskiy et.al Design and test results of the first prototype detector based on thin-walled drift tubes for the NA62 experiment. Instrum.Exp.Tech. 58 (2015) no.5, 593-601, Prib.Tekh.Eksp. 2015 (2015) no.5, 11-19.
2. E. Cortina Gil et.al. The beam and detector of the NA62 experiment at CERN (the NA62 collaboration). JINST 12 (2017) no.05, P05025, 2017, 121 pp. (chapter 7).
3. N. I. Azorskii et.al. New Type of Drift Tubes for Gas-Discharge Detectors Operating in Vacuum: Production Technology and Quality Control. Physics of Particles and Nuclei Letters, 2017, Vol. 14, No. 1, pp. 144–149.
4. N. Azorskiy et.al The NA62 spectrometer acquisition system. JINST 11 (2016) no.02, C02064, 11 pp.
5. N. Azorskiy et.al. A drift chamber with a new type of straws for operation in vacuum. Nucl. Instrum. Meth. A824 (2016) 569–570.
6. Yu.Potrebenikov (for CERN-DUBNA Straw group) A new system of STRAW chambers operating in vacuum for the NA62 experiment. J.Phys.Conf.Ser. 800 (2017) no.1, 012047, 2017, 3 pp.
7. L. Glonti et.al Determination of the anode wire position by visible light in a new type straw for NA62 experiment tracker. Nucl. Instrum. Meth. A824 (2016) 532–534.
8. S. Shkarovskiy. NA62 spectrometer to search for K+→π+νν. JINST 12 (2017) no.02, C02027, 7 pp.

## Slide 42
9. Л.Н. Глонти et.al Определение местоположения анодных проволок в тонкостенных дрейфовых трубках (строу) нового типа в видимом свете для дрейфовых камер эксперимента NA62. 1. Измерени в проходящем свете. Препринт ОИЯИ Д13-201-82. ОИЯИ, Дубна, 2016, 11 с.
10. L. Glonti, T. Enik, V. Kekelidze, A. Kolesnikov, D. Madigozhin, N&Molokanova, S. Movchan, Yu. Potrebenikov, Longitudinal tension and mechanical stability of a pressurized straw tube. Preprint JINR E1-2017-20. JINR, Dubna, 2017,12 pp.
11. Глонти Л.Н., Кекелидзе В.Д., Потребеников Ю.К. Дрейфовая камера для работы в вакууме. Патент на изобретение № 2465620. ФСИС РФ, Бюлл. №30, 2012.
12. Н.И. Азорский, В.В. Елша, Т.Л. Еник, Ю.В. Ершов, В.Д. Кекелидзе, Е.М. Кислов, А.О. Колесников, С.А. Мовчан, Ю.К. Потребеников, С.Н. Шкаровский. Устройство для изготовления цилиндрических трубок для газонаполненных дрейфовых детекторов ионизирующего излучения. Патент на изобретение № 2555693. ФСИС РФ, Бюлл. №19, 2015.
13. Глонти Л., Кекелидзе В.Д., Потребеников Ю.К., Самсонов В.А., Еник Т.Л., Колесников А.О., Мовчан С.А., Сотников А.Н. Устройство для измерения местоположения проволок в газовых проволочных камерах. Патент на изобретение № 2602492. ФСИС РФ, Бюлл. №32, 2016.

## Slide 43
Благодарности:
Юрий Васильевич Гусаков
Николай Иванович Азорский
Ирина Александровна Поленкевич
Владимир Владимирович Елша
Евгений Мстиславович Кислов
Александр Николаевич Сотников
Сергей Иванович Какурин
Александр Николаевич Щербаков
Марина Викторовна Зайцева
Светлана Владимировна Кильчаковская
Ника Олеговна Ридингер
Любовь Никитична Тарасова
Татьяна Васильевна Семчукова
Андрей Иванович Зинченко

## Slide 44
Thank you!