## Slide 1: Status of Forward Hadron Calorimeter (FHCal)
A.Ivashkin
Institute for Nuclear Research RAS, Moscow
on behalf of the FHCal group
10th MPD collaboration meeting, Nov., 2022.
FHCal overview;
Status of FHCal modules;
FHCal subsytems;
Integration to MPD;
Mechanical support.

## Slide 2
FHCal
Two arms of hadron calorimeter at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules.
~1x1 m2 each part.
Beam hole 15x15 cm2.
Lead/scintillator sampling calorimeter.
Longitudinal segmentation;
Light readout- WLS-fibers;
7 sections/photodetectors in each module.
FHCal in MPD
FHCal modules

## Slide 3
The centrality of the collision;
The reaction plane orientation;
Physics in forward rapidity;
Minimum bias trigger.
FHCal detects spectators to measure:
X
Centrality:
2D-Fit of energy distributions in FHCal modules
E_max [a.u]
Edep [a.u]
central events
peripheral events

## Slide 4
All (90+spare) FHCal modules are assembled and tested with cosmic rays.
100 Front-End-Electronics (FEE) boards are produced and tested.
Modules are ready for the delivery at MPD site.
The activities with modules:
Calibration with cosmic muons;
Development of readout;
Development of FHCal trigger;
Development of Detector Control System;
Monitoring system.
FHCal modules

## Slide 5
Front-End-Electronics
Two PCBs in each module with:
7 photodetectors ;
Photodetectors – MPPCs;
two-stage amplifiers;
HV channels;
LED calibration source.
MPPC: new type
S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
100 units of FEE were produced and tested.

## Slide 6: Diagram of FHCal readout
FEE
FEE
FEE
1
2
44
…
on detector
ADC64 (1)
(9 modules)
ADC64 (2)
(9 modules)
ADC64 (5)
(8 modules)
…
near detector
Left (Right) FHCal arm
HVsys
DCS Control box
Wiener MPOD (?) power supply
signal cables
General Control System (Tango)
- Ethernet
DAQ
5 Ethernet
5 lemo (trigger)
5 lemo (XOR)
5 optical (WR)
~20m cables
Both FHCal arms have the same readout scheme.
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).

## Slide 7
Detector Control System (DCS)
DCS Tasks:
Control of HV at photodetectors (MPPC’s);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
Status of DCS:
It is practically fully operational;
The performance will be tested in the nearest BM@N runtime (nov’22).
External LED generators for monitoring system were produced.
Synchronization and tests are ongoing!
LAN
FEE
Database
FHCal New Slow Control (proxy)
General Slow Control
System Module
System Module
FEE
FEE
FEE
FEE
FEE
RS485
Connection diagram

## Slide 8
Energy calibration with cosmic nuons
Clear amplitude spectra from cosmic muons allow the energy calibration in self-triggering mode (without external muon trigger).
This is due to high light yield in the longitudinal sections in modules.
With new photodiodes effect of electronic noise is rather small.
A new simplified version of energy calibration is under development.
MPPC: S14160-3010PS
pixel -10x10 µm2;
PDE~18%;
G~1.8x105.
MPPC: S12572-010P
pixel -10x10 µm2;
PDE~12%;
G~105.
Previous MPPC type
New MPPC type
~5 MeV
Corrected to pass length in scintillators.
Raw spectrum
Response of FHCal modules with different types of MPPC to cosmic muons .

## Slide 9: Preparations for FHCal trigger
Dependence of trigger efficiency on the configuration of modules (Au-Au 11 GeV).
Threshold 2 MeV/module
Trigger efficiency ~98%
Adders of analog signals from individual modules were produces for part of FHCal.
For all modules a few additional adders must be produced!
The configuration of modules in trigger would depend on FEE and correlation noises. Flexible configuration is to be developed.
Test of trigger noise on energy threshold in one module
In peripheral collision the energies are mainly deposited in central modules.

## Slide 10: FHCal integration to MPD (ADC readout)
ADC boxes are placed at the lateral sides of FHCal support
Two halves of FHCal.
ADC boards and boxes are ready.
Tests are planned in the nearest time.
ADC cooling with compressed air is planned.
5 pipes from each side are to be available!

## Slide 11: Mechanical support (main elements)
Пластина
Support frame in magnet pole
Basket of FHCal modules
Outer table
Design is finished!
Basket is urgent for production to start the FHCal assembling near MPD.
Design is at final stage!
Design is finished!
Start of production is planned next year.

## Slide 12: Mechanical support (sensitive parts)
Ball joints
Ball heads and holders
screw transmission
These parts are already ordered!

## Slide 13: FHCal installation into magnet pole
Main problem: beam pipe between two FHCal halves
Table with FHCal near pole
FHCal inserted into pole
Two FHCal halves compressed together
Design of FHCal support is at final stage!

## Slide 14
Summary
All FHCal modules were tested and are ready for delivery at MPD site.
FEE was produced and tested. (Power supplies for ADC?)
Detector Control System is ready and will be tested at nearest BM@N runtime.
Energy calibration procedure is under optimization.
FHCal trigger is under development. Flexible configuration of modules is considered.
The mechanical platform is at final stage of design. The production of FHCal baskets is urgent!
We plan to be ready for the calorimeter assembling at MPD site in the middle of 2023.
The baskets for FHCal modules must be produced to this time!
The space an some infrastructure for FHCal assembling must be available!

## Slide 15
Thank you!