## Slide 1: Status of Forward Hadron Calorimeter (FHCal)
A.Ivashkin
Institute for Nuclear Research RAS, Moscow
on behalf of the FHCal group
11th MPD collaboration meeting, Apr., 2023.
FHCal overview;
Status of FHCal modules;
FHCal subsystems and activity;
Integration to MPD

## Slide 2
FHCal
Two arms of hadron calorimeter at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules.
~1x1 m2 each part.
Beam hole 15x15 cm2.
Lead/scintillator sampling calorimeter.
Longitudinal segmentation;
Light readout- WLS-fibers;
7 sections/photodetectors in each module.
FHCal in MPD
FHCal modules

## Slide 3
The centrality of the collision;
The reaction plane orientation;
Minimum bias trigger;
Physics in forward rapidity.
FHCal detects spectators to measure:
X
Centrality:
2D-Fit of energy distributions in FHCal modules
E_max [a.u]
Edep [a.u]
central events
peripheral events

## Slide 4
All (90+spare) FHCal modules are assembled and tested with cosmic rays.
100 Front-End-Electronics (FEE) boards are produced and tested.
Modules are ready for the delivery at MPD site.
The activities with modules:
Calibration with cosmic muons;
Development of readout;
Development of FHCal trigger;
Development of Detector Control System;
Monitoring system.
FHCal modules

## Slide 5
Front-End-Electronics
Two PCBs in each module with:
7 photodetectors ;
Photodetectors – MPPCs;
two-stage amplifiers;
HV channels;
LED calibration source.
MPPC: new type
S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
100 units of FEE were produced and tested.

## Slide 6
Detector Control System (DCS)
DCS Tasks:
Control of HV at photodetectors (MPPC’s);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
Status of DCS:
It is practically fully operational;
Further improvements of functionality are going on.
LAN
FEE
Database
FHCal New Slow Control (proxy)
General Slow Control
System Module
System Module
FEE
FEE
FEE
FEE
FEE
RS485
Connection diagram

## Slide 7: FHCal readout and control
FEE
FEE
FEE
1
2
44
…
on detector
ADC64 (1)
(9 modules)
ADC64 (2)
(9 modules)
ADC64 (5)
(8 modules)
…
near detector
FHCal arm
HVsys
DCS Control box
power supply
signal cables
General Control System (Tango)
- Ethernet
DAQ
~20m cables
Both FHCal arms have the same readout scheme.
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).

## Slide 8
Preparation to the tests of ADCs
FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
Test bench for ADC readout

## Slide 9
FHCal trigger
Threshold 2 MeV/module
Trigger efficiency ~98%
Dependence of trigger efficiency on the configuration of modules (Au-Au 11 GeV).
Scheme of FHCal trigger

## Slide 10: Preparations for FHCal trigger
Adders of analog signals from individual modules were produces for full FHCal.
The configuration of modules in trigger would depend on FEE and correlation noises. Flexible configuration is to be developed.
Test of trigger noise on energy threshold in one module
12-channels signal adders
All adders are working. The noises are under tests.

## Slide 11
Energy calibration with cosmic nuons
The energy calibration is planned in self-triggering mode (without external muon trigger).
The different geometries of muon tracks are to be considered.
The selection of different muon tracks can be done by requiring the coincidence of muon signals in FHCal modules and longitudinal sections.
A new simplified version of energy calibration is under development.
New MPPC type
~5 MeV
Corrected to pass length in scintillators.
Raw spectrum without selection of tracks
Response of FHCal modules to cosmic muons with different track geometries.

## Slide 12: FHCal integration to MPD (ADC readout)
ADC boxes are placed at the lateral sides of FHCal support
Two halves of FHCal.
ADC cooling with compressed air is planned.
5 pipes from each side are to be available!

## Slide 13: FHCal cabling
Prepared by
M. Rumyantsev

## Slide 14: Mechanical support (main elements)
Пластина
Support frame in magnet pole
Basket of FHCal modules
Outer table
Design of all elements was finished a month ago!
The production starts now!

## Slide 15: Assembling of FHCal modules in basket
М10 х30
M8
M6

## Slide 16: FHCal installation into magnet pole
Main problem: beam pipe between two FHCal halves
Table with FHCal near pole
FHCal inserted into pole
Two FHCal halves pressed together

## Slide 17
Summary
All FHCal modules were tested and are ready for delivery at MPD site.
FEE was produced and tested.
Detector Control System is ready and is improved permanently.
Energy calibration procedure is under optimization.
FHCal trigger is under development. Flexible configuration of modules is considered.
The design of mechanical platform is finished. The production starts now!
We plan to be ready for the calorimeter assembling at MPD site in the middle of 2023.
The space an some infrastructure for FHCal assembling must be available!

## Slide 18
Thank you!