## Slide 1: NICA-MPD PLATFORM STATUS
Author:
Alexander Fedunin
Sector No 3; Engineering Support Group
Joint Institute for Nuclear Research
XI MPD Collaboration meeting

## Slide 2: PARTS of NMP
IT RACKS on the NMP
Cooling System
Main electrical distribution board
Structed Cabling(fiber optic)
Access control and management system
CCTV video surveillance system
Аutonomous fire extinguishing system
Monitoring system
XI MPD Collaboration meeting

## Slide 3
The NMP contains the electronics for collecting and processing data from the MPD.
XI MPD Collaboration meeting

## Slide 4
XI MPD Collaboration meeting
Platform (4 separate modules installed vertically)
Each module includes 1 room divided by 2 corridors
Inside modul there are racks with electronics, cooling and power supply equipment and other engineering systems
Three zones: cold corridor, hot corridor, space under the raised floor
Each floor has ventilation and air conditioning systems

## Slide 5: IT RACKS on the NMP
XI MPD Collaboration meeting
First floor
Cold corridor
Hot corridor
Colling system
Main
electrical distribution
board
1
Rack

## Slide 6: IT RACKS on the NMP
Second, third, fourth floor
XI MPD Collaboration meeting
Hot corridor
Cold corridor
Coling system
1
Rack
2
3
4
5
6
7
8

## Slide 7: IT RACKS on the NMP
Rack C3 ECO 48U 600*1200, black, perforated door
MPD equipment racks
PDU controlled C3, 3 phases, 32A, C13-24, C19-12, 3 avt.in IEC 309, kab.3m
GreenMDC ventilation panel, active, 1U
XI MPD Collaboration meeting

## Slide 8: COOLING SYSTEM
XI MPD Collaboration meeting
A visual picture
The NMP cooling system is an integral part.
It is designed for:
Cooling equipment from overheating
Maintenance and regulation of the set air temperature
Ensuring round-the-clock and year-round temperature conditions.

## Slide 9: COOLING SYSTEM
Equipment cooling is provided by Hiref precision
XI MPD Collaboration meeting

## Slide 10: Main electrical distribution board
XI MPD Collaboration meeting
The platform power supply is isolated on each floor.
Each floor has its own power distribution board, which makes it possible to carry out preventive maintenance of the floor without shutting down the entire NMP

## Slide 11: Access control and management system
XI MPD Collaboration meeting
Universal controller CT/L14.1
Lock controller CL211.3
JINR employees will be able to use their badge for access to all rooms

## Slide 12: CCTV video surveillance system

## Slide 13: Аutonomous fire extinguishing system
XI MPD Collaboration meeting
Chladon 125 is used

## Slide 14: Monitoring system
XI MPD Collaboration meeting

## Slide 15: STRUCTED CABLING
XI MPD Collaboration meeting

## Slide 16: Stages of work
 |  | April 2023 |  |  |  | May 2023 |  |  |  |  |  |  |  | May | June-September | September | October
 |  | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 1-30 |  | 15-30 | 1-15
№ | Stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 | Delivery of all engineering systems to JINR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 | Installation of metal structures |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 | Installation of basic structures |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | Installation of raised floor and engineering networks |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 | Connecting the NMP water cooling system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 | The closure of Building 17. Work is stopped |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 | Installation of the structure of the 4th floor and engineering systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 | Testing of all NMP systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
XI MPD Collaboration meeting

## Slide 17
I want to thank my team and everyone who took part
XI MPD Collaboration meeting

## Slide 18: Thank you For Attention
Author: Alexander Fedunin
Email: fediunin@lhep.ru
XI MPD Collaboration meeting