## Slide 1: Investigation of the perspectives of accelerator driven subcritical reactors with ion beams
Mihaela Paraipan
(on behalf of ADSR Collaboration)
1

## Slide 2
ADSR (accelerator driven subcritical reactor)
as energy amplifier
Advantages:
- the reactor works in subcritical regime – safer exploitation
- harder neutron spectrum – better incineration of the actinides
2
Project MYRRHA
Chinese ADS project
European Spallation Source
Linear accelerator – 2 GeV proton,
Beam intensity 1.5·1016
All these projects plan to use proton beams and a lead-bismuth eutectic (LBE) cooled subcritical reactor.

## Slide 3
Factors which influence the efficiency of ADSR
A systematic study of the conditions which maximize the energy gain, ensure
high fuel burnup and long period between refueling:
- factors related with the core structure and composition
- particle beam and energy
- accelerator type
3
M. Paraipan, V. M. Javadova & S. I. Tyutyunnikov (2023), Influence of Particle Beam and Accelerator Type on ADS Efficiency, Nuclear Science and Engineering, DOI: 10.1080/00295639.2023.2175582
The almost generalized opinion is that the optimal beam for ADSR is a proton beam with energy around 1-1.5 GeV [1-3].
In a series of works we showed that ion beams can be more efficient than protons.
Rubbia C. et al. . CERN/AT/93-47, November 1993.
Hashemi-Nezhad S.R. et al. Ann. Nucl. En. 38 (2011) 1144–1155
Zhao, Z. et al. Prog. Nucl. Energy 71 (2014).

## Slide 4
Core optimization
M. Paraipan, V. M. Javadova, S. I. Tyutyunnikov, Aspects of target optimization for ADS with light ion beams at energies below 0.5 AGeV, Progr. Nucl. En. 120 (2020) 103221
M. Paraipan, A. A. Baldin, E. G. Baldina, S. I. Tyutyunikov, Conceptual Design of Accelerator Driven Systems with Light Ion Beams, Nuovo Cimento 42 C (2019) 66
The scheme of the target.
The core is an assembly of fuel rods surrounding the converter and immersed in a bath of coolant.
Fuel composition: metal (alloy U-Pu-Zr), carbide, oxide
Cooling with Pb, Pb-Bi eutectic (LBE), and Na.
The variation in actinide composition and the cooling with metals conserve the shapes of the neutron spectra and the ratio between the energies deposited by different ions.
Regarding the core, three factors are the most relevant for the functioning of ADSR:
- the material used for the converter.
- the level of enrichment
- the working value of criticality coefficient keff.
4

## Slide 5
Light materials are preferable especially for ion beams at low energy.
The best results are obtained with Be converter. Besides the increase in ion range, Be acts as good neutron moderator and reflector.
The energy released increases with the increase of the dimensions of the converter.
The neutron spectra in fuel blanket with Li, Be, C and LBE converters, irradiated with a beam of 7Li with energy 0.3 AGeV.
One relevant advantage of a Be converter with high dimensions is the fact that allows to diminish the level of enrichment, increasing the period of functioning without refueling and the burn-up.
The choice of the converter
5
The level of enrichment
The evolution of 239Pu in cores with 5.6%, 7.8% and 8.9% 239Pu, irradiated with a beam of 7Li with energy 0.25 AGeV and intensity 1.25‧1016.
A lower level of enrichment is preferable because it ensure longer period between refueling and higher burning of the actinides.
With a proper core configuration one can burn in ADSR until 25 % from actinides in one cycle, in comparison with 6-7 % obtained in a fast reactor.
cores with metallic fuel (U-Pu-10%wtZr), keff 0.988, but with different enrichment, irradiated with a beam of 7Li with energy 0.25 AGeV and intensity 1.25·1016. The converter is a Be cylinder with radius 10 cm, and length 120 cm. The thermal power is 550 MW.

## Slide 6
The optimal value of keff must be able to ensure in the same time a safe exploitation and a maximum energy gain.
Beam shutdown
Values of keff below 0.99 are advantageous from the point of view of the evolution of UTOP transient.
In the case of UBOP transient a higher initial value of keff is favorable because conduces to a new steady state at a power level closer to the initial one.
From the point of view of the quick shutdown of the reactor after the beam stopping a keff 0.99 is safe enough.
UBOP (unprotected beam overpower)
Optimal value of keff
The power evolution in UTOP (a), in UBOP (b) transients and after the beam turn off (c) in ADS with U-Pu-10%Zr fuel and keff 0.98, 0.99, 0.996.
6
A working value of 0.985-0.988 for keff would be safe enough.
UTOP (unprotected transient overpower)
a)
b)
c)

## Slide 7
The thermal power as a function of projectile mass number and energy.
The system capacity to remove the heat limits the maximum thermal power in ADSR at approximately 3 GW.
The objective to maximize the efficiency imposes the use of beams with intensity as high as possible.
The values of the energy released correlated with the beam intensity limit the maximum ion energy that can be used in ADSR. In our conditions we can accelerate 7Li and 9Be until ~ 1 AGeV, while 16O and 20Ne at maximum 0.75 AGeV.
The energy gain factor G is used as measure of the energy efficiency. It is defined as the ratio of the produced electrical power Pprod to the power spent to accelerate the beam Pspent :
Beam and accelerator
A core optimized for ADSR (metallic rods U-Pu-Zr, LBE coolant, Be converter with length 110 cm, keff 0.985) was used in simulation. The core was irradiated with protons and ion beams from D to 20Ne, energies from 0.2 AGeV to 2 AGeV and beam intensity 1.5·1016 p/s.
7

## Slide 8
a)
b)
A beam of 7Li 0.25 AGeV realizes the same Pnet as a beam of 1.5 GeV proton with the minimal length of the accelerator (length 2.5 times smaller than for proton).
G (a) and Pnet (b) as a function of projectile mass and energy for particles accelerated in a linac, core with keff 0.985.
Linear accelerator
8

## Slide 9
Values of G slightly lower than in a linac, but Pspent represents only few percent from Pprod and Pnet is almost the same.
Optimal energy of proton beam is ~ 1 GeV with G ~ 12.
A beam of 7Li with energy 0.2 AGeV is equivalent with 1 GeV proton beam with respect to the energy gain and the net power produced.
Ion beams starting with 7Li and energy above 0.3 AGeV realize 2-3 times higher G.
G (a) and Pnet (b) as a function of projectile energy for particles accelerated in a cyclotron, core with keff 0.985.
Cyclotron
b)
a)
9

## Slide 10
Comparison with fusion power plants
Entler S., Horacek J., Dlouhy T., Doctal V., Approximation of the economy of fusion energy, Energy 152 (2018) 489-497
Meier W.R. et al., Fusion technology aspects of laser inertial fusion energy (LIFE), Fusion Engineering and Design 89 (2014) 2489-2492
ITER project – magnetic plasma confinement
LIFE project – laser inertial plasma confinement
G ~ 3
G ~ 4
The values of energy gain that could be achieved in ADSR are significantly higher (until 10 times) that the G values estimated for fusion power plant.
10

## Slide 11
Planned experiments
The most relevant data about the efficiency of proton and ion beams are obtained in experiments with fuel blanket.
The design of the experimental target must reproduce at a small scale the situation in a real ADSR. It should allow also to check the effect of converters with length until 110 cm.
The interest is to determine the minimal dimensions and minimal amount of fuel necessary for a correct reproduction of the ratio of the energy released (amount of fissions) produced with proton and ion beams.
The design of the graphite target GAMMA-4
11
Paraipan M., Kryachko I. A., Javadova V. M., Levterova E. A., Tyutyunnikov S. I., Main Results of Neutronical Study about ADS with Ion Beams and Implications on Experiments Planning, Phys. Part. Nucl. Lett. 19 2 (2022) p. 129-144
a block with dimensions 110x110x120 cm

## Slide 12
Conclusions
The conditions which maximize the efficiency of ADSR were investigated. The main factors related with the core, relevant for the ADSR efficiency are the core keff , the material used for the converter and the level of the enrichment.
The optimal value of keff is in the range 0.985 - 0.988.
The best choice for the converter is Be, especially for ion beams at low energy. A converter with radius 10-20 cm and length 100-120 cm maximizes the energy released and lowers the necessary level of enrichment, ensuring larger period between refueling and higher actinide burn-up. In ADSR until 25 % from the actinides can be fissioned during a cycle, 3.5 times more than it can be achieved in a fast reactor.
The maximum energy gain of protons is obtained at 1.5 GeV when they are accelerated in a linac, and at lower energy (0.75-1 GeV) when a cyclotron is used. In both situations ion beams starting with 4He realize higher energy gain than protons.
When particles are accelerated in a linac, at low accelerator length a beam of 7Li with energy 0.25 AGeV represents the best option.
High energy gain from 20 (with 0.25 AGeV 7Li beam) to 45 (with 0.75 AGeV 16O and 20Ne beam) can be obtained in ADSR, which makes ADSR an efficient source of energy.
The graphite target GAMMA-4 (a block with dimensions 110x110x120 cm) with 4 layers of enriched U fuel rods and a central hole for the placement of different converters allows a correct comparison between the number of fissions and the energy released realized with proton and ion beams.
The chosen length of the target (120 cm) offers the possibility to reproduce the dependence of the energy released on the dimensions of the Be converter for low energy ions.
12

## Slide 13
References
Rubbia C. et al., "An Energy Amplifier for cleaner and inexhaustible nuclear energy production driven by a particle beam accelerator”. CERN/AT/93-47, November 1993.
Hashemi-Nezhad S.R., Westmeier W., Zamani-Valasiadou M., Thomauske B., Brandt R., Optimal ion beam, target type and size for accelerator driven systems: Implications to the associated accelerator power, Ann. Nucl. En. 38 (2011) 1144–1155
Zhao, Z., Chen, Z., Chen, H., Preliminary optimization of proton energy and target for Lead- Bismuth Eutectic target of a demonstration ADS. Prog. Nucl. Energy 71 (2014).
Paraipan, M., Javadova. V., Tyutyunnikov S. I., Aspects of target optimization for ADS with light ion beams at energies below 0.5 AGeV, Progress in Nuclear Energy 120 (2020) 103221
Paraipan M., Baldin A. A., Baldina E. G., Tyutyunikov S. I., “Light Ion Beams for Energy Production in ADS”, EPJ Proceedings MMCP2017, 173 (2018) 04011; Ann. Nucl. En.,110 (2017) p 973.
M. Paraipan, V. M. Javadova & S. I. Tyutyunnikov (2023), Influence of Particle Beam and Accelerator Type on ADS Efficiency, Nuclear Science and Engineering, DOI: 10.1080/00295639.2023.2175582
Yu.K. Alexandrov, V.A. Rogov, A.S. Shabalin, “Main features of the BN-800 passive shutdown rods”, Proceeding of a Technical Committee meeting held in Obninsk, Russian Federation, 3-7 July 1995, IAEA-TECDOC-884, p. 107-112
Paraipan M., Kryachko I. A., Javadova V. M., Levterova E. A., Tyutyunnikov S. I., Main Results of Neutronical Study about ADS with Ion Beams and Implications on Experiments Planning, Phys. Part. Nucl. Lett. 19 2 (2022) p. 129-144
Tohru Suzuki, Xue-Nong Chen, Andrei Rineiski, Werner Maschek, Transient analyses for accelerator driven system PDS-XADS using the extended SIMMER-III code, Nuclear Engineering and Design 235 (2005) 2594–2611
Rui Li, Xue-Nong Chen, Claudia Matzerath Boccaccini, Andrei Rineiski, Werner Maschek, Study on Severe Accident Scenarios: Pin Failure Possibility of MYRRHA-FASTEF Critical Core, Energy Procedia 71 (2015) 14 – 21
ESS Technical Design Report April 23, 2013 ESS-doc-274
Craddock M. K., Symon K. R., “Cyclotrons and Fixed-Field Alternating-Gradient Accelerators”, Reviews of Accelerator Science and Technology, 1(1), pp. 65-97 (2008)
M. Okamura et al., “Demonstration of an intense lithium beam for forward‑directed pulsed neutron generation”, Scientific Reports 12, 14016 (2022) https://doi.org/10.1038/s41598-022-18270-0.
Entler S. et al., Approximation of the economy of fusion energy, Energy 152 (2018) 489-497
Meier W.R. et al., Fusion technology aspects of laser inertial fusion energy (LIFE), Fusion Engineering and Design 89 (2014) 2489-2492
13

## Slide 14
14
Thank you for your attention!