Banana-plot creation details
21.03.2023
Sergey, Dosbol, Vitaly & Dmitriy

---
Straw:
Straw relative
position:
- Rtube = 5 mm
- Anoded = 30 micron
- Va = 1750 V
- Trackcount = 50 000
- Ar/CO2 : 70/30
- Gas gain = 90 k (exp)
- Pressure & Temperature: 1 atm & 20o C
- Em = 1 GeV
- No attachment
Track match condition:
- Rtube – rR - eps < rL < Rtube - rR + eps
- eps is just a algorith parameter
  default value = 25 mm
rL
rR
m
Source: Dosbol presentation

---
Sergey’s old result (Garfield simulation)

---
Test beam banana example
Source: Vitaliy’s images

---
NA62 R-T relation
Note: error is higher
due many wires but
negative tracks only
Source: NA62 Dosbol’s root data

---
Note: single wire data
Source: Sergey’s TDR presentation slide

---
Test beam MPV parameterisation

---
Crystal ball distribution imitation

---
Bana reconstruction from simulated data
//half of the 2D hist bin width
//neagtive coord = 2
Rtube – rR - eps < rL < Rtube - rR + eps

---
Note: lesser events; see slide #10
200k events → 100k pairs but ~73450 entries

---
R-T curve reweight
Source: Dmitriy’s tg correspondence

---
Irregular track positions distribution

---
Overall:
Symmetry of the banana image with respect to the y=x curve is necessity but insufficiency condition for uniform tracks distribution
Is NA62 r-t data was renormalized?