## Slide 1
A.Butenko on behalf of the team
UIPAP Conference “Heaviest nuclei and atoms”, Yerevan, April 2023
NICA accelerator complex

## Slide 2
Introduction (complex NICA)
Two LINACs & ion sources
  LU-20/LILAc (light & pol. ions)
  HILAC (heavy ions)
The Booster ring
The Nuclotron ring
Collider systems status

## Slide 3
NICA complex layout
Nuclotron ring
Nuclotron
Two Linear Injectors & sources
Two linacs:
HILAC & LILAC
Booster & beam line
Booster
Beam lines @ fixed target area
Fixed target area
BM@N
Collider ring
Collider

## Slide 4
p↑, d↑, ions Z/A>0,3
RFQ
Ions Z/A>0,3
LIS
SPI
p↑,d↑
10mA
HILAc
HILAc building
Booster
Injection
channel
Nuclotron
Booster
RF amplifier for LU-20
LU-20 building
Layout of the linear Injectors

## Slide 5
source
LEBT + Buncher
4 wane RFQ
(3 sections)
MEBT LU-20
QT + Bu +QT
Designe has been started in 2012 In collaboration with ITEPH, MEPHI, Snezhinsk.
New fore-injector for LU-20 + SPI for polarized p & d
Commissioned in 2016
4 Nuclotron beam RUNs
was provided
The SPI-project was started more then 10 year ago.
Main purpose is to provide the intensity of the accelerated polarized beams (D+,H+) up to 1010 p/pulse
The SPI provided by polarized d & p Nuclotron complex during two beam RUNs in 2016-17.

## Slide 6
p↑, d↑, ions Z/A>0,3
RFQ
Ions Z/A>0,3
LIS
SPI
p↑,d↑
10mA
HILAc
HILAc building
Booster
Injection
channel
Nuclotron
Booster
RF amplifier for LU-20
LU-20 hall
Layout of the linear Injectors
The new Light Ions Linac LILAC
7 MeV/u for A/q<3, 13 MeV for protons

## Slide 7
p↑, d↑, ions Z/A>0,3
RFQ
Ions Z/A>0,3
LIS
SPI
p↑,d↑
10mA
HILAc
HILAc building
Booster
Injection
channel
Nuclotron
Booster
RF amplifier for LU-20
LU-20 building
Layout of the linear Injectors

## Slide 8
HILAC & Booster injection beam line
A/q (Target Ion Au31+) | 6.25
Beam current | < 10 emA
Repetition rate | < 10 Hz
Output energy | 3.2 MeV/u
Transmission of 2mA Fe14+ ions beam up to 75% from RFQ to the exit of the HILAc, 3.2 MeV/u
Heavy Ion Linear Accelerator
Stable and safe operation during Booster commissioning with Fe 14+ and Xe 28+ beams
Commissioned in 2018
BEVATECH Germany

## Slide 9
In April 2022 the run at HILAC accelerator was started for optimization
of Ar and Xe beams generation and acceleration up to 3.2 MeV/n
KRION-6T alignment on the HILac axis on high Voltage terminal
Run at HILAC with KRION source
KRYON source at the HILac

## Slide 10
Introduction (complex NICA)
Two LINACs & ion sources
  LU-20/LILAc (light & pol. ions)
  HILAC (heavy ions)
The Booster ring
Beam transfer line
The Nuclotron ring

## Slide 11
Beam losses < 10%
just on the first 5 turns.
Beam injection & circulation
26.12.2020
Fast Current Transformer (FCT)
Circulating beam
at the injection energy 3.2 MeV/u
22.12.2020
600 ms circulation of He1+
19.12.2020, 19:56 Moscow time. First beam in the ring.

## Slide 12
Beam acceleration
PCT signal when beam injecting into rising field, capturing (~60%), accelerating & decelerating:
no transient losses on the MF table & after.
1000 1500 2000 2500 3000 3500
Acceleration
Circulation
100 MeV/u
Deceleration
RF off
Magnetic field
Injection
Beam Intensity
Magnetic field
Cycle time, ms
Parametric beam current transformer signal (DC mode)
Beam injection with adiabatic capturing 5 harmonic (>95%),
accelerating up to 65 MeV/u,
recapturing 1 harmonic (close to 100%)
acceleration up to 578 Mev/u
with project ramp dB/dt = 1.2 T/s
Cycle 2 of commissioning
14-23 of September 2021 Fe14+
500 1000 1500 2000 2500 3000 3500
Cycle time, ms
Acceleration
Circulation
578 MeV/u
RF capturing 5 harm.
Acceleration
Magnetic field 1,2 T/s
Injection
Circulation
65 MeV/u
Re-capturing 1 harm.
Fe14+
He1+
Cycle-1 of commissioning
20 of December 2020 He1+
RUN-1
RUN-2

## Slide 13
Contract with BINP
Beam extraction & transfer line
3-rd str. sect.
To Nuclotron
Circulating beam
Beam fast extraction section
3D model of the transfer line

## Slide 14
Beam extraction & transfer line
Autumn of 2021 for the Run#2

## Slide 15
Beam injection to the Nuclotron ring
Installation finished 31 of Dec. 2021
15
SC Lambertson magnet
Designed – JINR,
fabricated – VST (Belgorod)
Four-rod
kicker

## Slide 16
Main results of RUN-3 (Booster + Nuclotron)
Booster and Nuclotron beam DC current transformers signals
Nucloton field
Intencity
RF capture
Acceleration
Booster field
Beam transfer with stripping С4+/С6+ transmission 70%
Beam intensity in the Booster intensity in the Nuclotron
Winter 2022

## Slide 17
124Xe+54 beam extraction (3,9 Gev/u) RUN #4 at NICA complex
Heavy ion beams acceleration
Jan. 2023
124Xe 1*107 Tspill = 3 s, kdc= 99%

## Slide 18
124Хе 28+ at injection energy
Profile width
Time, ms
Booster electron cooling
Electron energy 1,93 keV
Electron current 150 mА
Signals from
Ionization profile monitors
during beam circulation with const. W
Dynamics of the cooling process
Stable operation of the cooling system during a few shifts
Transverse cooling
Electron cooling of Xe beam

## Slide 19
Bunch length
measured with FCT
Without cooling
With cooling
Longitudinal cooling
Electron cooling of Xe beam
I.Meshkov
A.Sergeev

## Slide 20
Fast extraction from the Nuclotron
Design development is in the progress
Delays:
Due to delays of LM for injection;
Due to delays of injection Kicker;
LM1
Not for start configuration
Manufacturing
LM2
Final stage of redesign
Limitation of extracted beam energy by factor 1,6 (~2 GeV/u for Bi)
Doubling of injection LM with the same design and tooling for higher current;
3 section kicker

## Slide 21
Magnetic element | Number | Effective length, m | Max. magnetic field (grad), T (T/m)
Long dipole | 21 | 2 | 1.5
Short dipole | 6 | 1.2 | 1.5
Quadrupole | 28 | 0.35/0,52 | 31
Steerer | 33 | 0.466 | 0.114
Nuclotron-Collider transfer line is under delivery and construction by Sigma Phi
90% of magnets delivered to JINR in February 2021
January 2022 – delivery of first parts of PS, beam diagnostics, support stands.
Fabruary 2022 – delivery of vacuum equipment.
July 2022 – second part of power supplies, profile monitors, control system.
September 2022 – start of commissioning of the channel equipment.
December 2022 – commissioning of the channel with a beam.
Nuclotron-Collider beam transport channel
Sigma Phi
BLOCKED

## Slide 22
Introduction (complex NICA)
Two LINACs & ion sources
  LU-20/LILAc (light & pol. ions)
  HILAC (heavy ions)
The Booster ring
The Nuclotron ring
Collider systems status

## Slide 23
MPD
SPD
Start configuration of Collider
RF-1 (barrier voltage) for ion storage
RF-2 in a reduced version: 2 cavities per ring instead of 4 (50% of HV)
1 channel of S-cooling per ring (cooling in longitudinal space)
Basic configuration
RF-1 (barrier voltage) for ion storage
RF-2 project version = 8 cavities
RF-3 project version = 16 cavities
S-cooling (project vers.)
E-cooling
Back loop system
Result: 22 bunches of the length 2 m
per ring that L~5E25 cm-2s-1.
Result: 22 bunches of the length 0.6m
per ring that L~1E27 cm-2s-1.
Collider rings
Notes: The lattice design and prototyping of most collider elements are completed. The ring circumference is twice as one of the Nuclotron. For the gold beam a Luminosity at the energy above 10 GeV per nucleon will be 10 to the 27

## Slide 24
Collider SC magnetic system
Parameter | Dipole | Lens
Number of magnets | 80+8* | 86+12**
Max. magnetic field (gradient) | 1.8 T | 23.1 T/m
Effective magnetic length | 1.94 m | 0.47 m
Beam pipe aperture (h/v) | 120 mm / 70 mm | 
Distance between beams | 320 mm | 
Overall weight | 1670 kg | 240 kg
Production of magnets and doublet lenses 2018-2023
*- the magnets for the vertical movement of the beams
**- the final focus lens.

## Slide 25
On 28 December, 2021 the first dipole magnet was installed
in the collider tunnel
First collider magnet in the tunnel
Collider SC magnetic system

## Slide 26
Collider SC magnetic system
Status:
100% dipoles are installed and aligned;
40% of quads are installed in tunnel;
BV dipoles are under manufacturing;
Quads for straight sections are under assembling and testing;
Final focus quads are under assembling.

## Slide 27
Collider power supply system
68 Additional power supplies (10В х 300А)
12 energy evacuation keys
was constructed and tested
Each collider ring has its own power supply system based on 3 main current sources
2 sets of main PS for both collider rings are manufactured by NPP "LM Inverter"
and delivered to JINR.
Busbars system model in b.17

## Slide 28
Barrier bucket RF1 and harmonic RF2-RF3 (26 units)
Two RF1 cavities delivered to JINR in 2019
RF3 cavity in BINP
16 RF3 cavities for
full configuration,
Shipment - end of 2023,
beam tests – 2024
4 RF2 cavities for base configuration, passes trough vacuum tests, installation
in 2q of 2023
RF1 cavity in JINR
RF1 cavity in BINP
RF2 cavity in JINR
RF2 under tests BINP
RF3 under tests BINP

## Slide 29
29
Electron Cooling System
Parameter | Value
Electron energy, MeV Energy instability, E/E | 0.2 – 2.5  110-4
Electron beam current, A | 0.1 – 1.0
Cooling section length, m | 6.0
Solenoid magnetic field, T Field inhomogeneity, B/B | 0.05 – 0.2  110-5
Beginning of mounting – Sumer 2023 First beam tests – Autumn 2023
Contract with BINP
Main parts of the E-Cooler delivered to JINR and stored in SPD hall.

## Slide 30: Synchronization and LLRF system
30
Stage 1 (T0 + 7 months) | Development of the NICA Injection complex (Booster+Nuclotron) Synchronization system, its testing on the Executive’s site, and its delivery to the Customer. Two LLRF Prototypes are provided up to this stage and testing is started during the Nuclotron-Booster run.
2.Stage 2/ (T0 + 13 months ) | Development of the first revision of NICA Injection complex LLRF system and on-site testing; Development of NICA Collider Synchronization System
3.Stage 3/ (T0 + 19 months ) | Development and testing of the final revision of synchronization and LLRF systems of the NICA complex.
4.Stage 4/ (T0 + 21 months ) | Services for mounting, final software installation and testing of the NICA Accelerator complex Synchronization and LLRF systems./
5.Stage 5 (T0 + 25 months ) | Services for SAT and commissioning of the NICA Accelerator complex Synchronization and LLRF systems.
Start of Contract with COSY Lab – November 2021
Synchronization and LLRF of Booster and Nuclotron – December 2022
Mounting and testing of NICA synchronization and LLRF – October 2023
Synchronization: 317+31+91 channels. LLRF: 30 channels
COZYLAB

## Slide 31
- Insulating volume and beam pipe vacuum tests (leakage tests)
Test of cryogenic system
Start tuning of the collider main control system
Test of the main power supply and cycle control system on equivalent load
Commissioning of thermometry system (more then 2000 sensors)
Cooling of the rings (arc to arc separately)
Commissioning of quench detection system (more then 600 detectors)
Commissioning of energy evacuation system
Test of the main power supply on superconducting load
Increasing of main magnetic field & SC magnetic system training
Preliminary program of the first technological collider run (2023/2024)

## Slide 32
Thank you for attention