## Slide 1
XIXth Workshop on High Energy Spin Physics
dedicated to 90th anniversary of A.V. Efremov birth
1
Speaker: Kolokolchikov S. 1,2 (sergey.bell13@gmail.com)
Co-authors: Senichev Yu. 1,2, Aksentev А. 1,2,3, Melnikov A. 1,2,4
1Institute for Nuclear Research RAS, Moscow, Russia,
2Moscow Institute of Physics and Technology, Dolgoprudny, Russia,
3Moscow Engineering Physics Institute (MEPI), Moscow
4Landau Institute for Theoretical Physics, Chernogolovka,
Dubna, 04 September 2023.
04/07/2023
Dubna, 2023.
Transition energy crossing of
polarized proton beam at NICA.

## Slide 2
Abstract
At an experiment on acceleration of a polarized proton beam up to an energy at 13 GeV, the possibility of crossing the transition energy at 5.7 GeV by a jump is considered.
The scheme of crossing by a rapid change of transition energy, assumes the longitudinal movement of the beam near the zero value of the slip coefficient.
The jump itself is carried out in the absence of an RF field. The paper presents the influence of the above features on the dynamics of a polarized beam.
2
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 3
TABLE OF CONTENTS
Transition Energy
Orbital Tracking
Spin Tracking
3
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 4
Transition Energy
4
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 5
Momentum compaction factor at Transition
5
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.
MCF
Slip-factor
Energy change 1) momentum change; 2) trajectory change.
1st Ord
2nd Ord
At get for Lorentz-factor , thus, transition energy can be determine.

## Slide 6
Equations of Longitudinal Motion
Slippage factor
– arrival Time drift
– Energy Kick
Synchronious Particle
Classical form
BLonD: https://blond.web.cern.ch/
6
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 7
Coasting Beam
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
7
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 8
Jump-scheme at NICA
– turns before jump
– turns at jump
–
– jump time
Here is a 5 different states of longitudinal
optics based on transition energy:
1) acceleration from injection energy with initial value;
2) smooth increase to peak;
3) jump;
4) smooth recovery till initial transition;
5) initial value till the experiment energy;
First defines 3) state based on the maximum available speed of transition shift and available transition size
Secondly, we can understand states 3 and 4, as they changed parallel to beam energy
Finally, states 3 and 5 also can be understand
1
2
5
4
3
3
2
4
8
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 9
Momentum compaction factor at Transition
9
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 10
Dynamics aperture
10
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 11
Impedance
11
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 12
NICA Elements
12
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 13
Impedances
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349
Definition of Impedance:
13
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 14
Space Charge Impedance
14
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 15
BLonD. Inductive Impedance (SC) – Induced Voltage
BLonD: https://blond.web.cern.ch/
P. F. Derwent, Implementation of BLonD for Booster Simulations, Beams-doc # 8690, 2020
15
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 16
Phase portraits of different BB
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
16
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 17
Fourier Expansion
Mihaly Vadai, Beam Loss Reduction by Barrier Buckets
in the CERN Accelerator Complex, CERN, Geneva, 2021
Square signal
Sigma modulation
Fourier Expansion
RF Kick
17
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 18
18
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 19
Separatrix of BB
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
19
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 20
Orbital Tracking
20
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 21
Effect of High Order MCF
– smooth increase (2nd stage)
NO SC
BB RF
stationary
2
At 2nd stage
Taking into account
get a range of for different particles
21
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 22
Space Charge Impedance Effect at Transition Jump
Jump – (3d stage)
Only SC
No RF
change at a turn
22
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 23
Spin Tracking
23
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 24
Particle Spin Tracking (Acceleration near Transition)
24
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.
T-BMT Equations
For pure magnetic ring

## Slide 25
Particle Spin Tracking (Acceleration near Transition)
25
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.
Parameters
Lattice:
Spin:
RF is turn on
COSY Infinity: https://www.bmtdynamics.org/cosy/

## Slide 26
Polarization (Acceleration near Transition)
26
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.
Parameters
Lattice:
Spin:
RF is turn on

## Slide 27
Lattice Parameters (during Jump)
27
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 28
Particle Spin Tracking (during Jump)
28
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.
Parameters
Lattice:
from to
Spin:
RF is turn off
Shown 4 particles with different initial parameters in

## Slide 29
Polarization (during Jump)
29
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.
Parameters
Lattice:
from to
Spin:
RF is turn off

## Slide 30
Сonclusion
Outcomes:
During the jump procedure the beam hold in separatrix;
And the polarization is not destroyed;
Transition Energy Jump is an available option cross transition energy.
Considered:
Longitudinal Dynamic Modeling near Transition Energy taking into account high orders of MCF and Impedances;
Spin Tracking to consider polarization.
30
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 31
References
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
Mihaly Vadai, Beam Loss Reduction by Barrier Buckets in the CERN Accelerator Complex, CERN, Geneva, 2021
П.Р. Зенкевич, А.А. Коломиец, Электромагнитное моделирование элементов структуры коллайдера NICA, Письма в ЭЧАЯ. 2020. Т. 17, № 4(229). С. 445–452
A. Tribendis and others, Constraction and first test results of the barrier and harmonic RF systems for the NICA collider, IPAC2021, Campinas, SP, Brazil, doi:10.18429/JACoW-IPAC2021-MOPAB365
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15
P. F. Derwent, Implementation of BLonD for Booster Simulations, Beams-doc # 8690, 2020
BLonD: https://blond.web.cern.ch/
COSY Infinity: https://www.bmtdynamics.org/cosy/
31
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 32
Backups
32
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 33
Barrier Bucket
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
33
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 34
Principle of stacking with BB
Jens Schweickhardt, Modeling and Optimization of Barrier-Bucket RF Systems, 2021
34
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 35
Barrier Bucket at NICA
A. Tribendis and others, Constraction and first test results of the barrier and harmonic RF systems for the NICA collider, IPAC2021, Campinas, SP, Brazil, doi:10.18429/JACoW-IPAC2021-MOPAB365
35
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 36
Barrier Bucket at NICA
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15
36
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 37
BB RF1 Impedances
Equivalent circuit of one ring (from the 1st to the 19th).
Last ring and accelerating gap.
System impedance calculated by equivalent circuit impedance
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15
37
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 38
BB RF1 Impedances
System impedance calculated by equivalent circuit impedance
A.M. Malyshev and others, Barrier station RF1 of the NICA collider. Design features and influence on beam dynamics, RuPAC2021, Alushta, Russia, doi:10.18429/JACoW-RuPAC2021-WEPSC15
38
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 39
Dispersion Relation
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349
39
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.

## Slide 40
Vlasov’s Equation and Dispersion Relation
Laclare, J L (ESRF, Grenoble), Coasting beam longitudinal coherent instabilities, CAS - CERN Accelerator School : 5th General Accelerator Physics Course, pp.349-384, DOI: 10.5170/CERN-1994-001.349
40
04/07/2023
XIXth Workshop on High Energy Spin Physics
Dubna, 2023.