## Slide 1: Measurements at PSI in 2022
Egor Shevchik 22/05/2023
OMC4DBD General Collaboration Meeting, 22-24 May 2023

## Slide 2: 2022 PSI measurements
We used the same target unit as for 2021 with minor changes.
The only enriched target for 2022 campaign – 100Mo.
The Ge-detecors installed on the same frame.
Offline measurements at RHL of Mo-nat & Mo-100 for 21 days.
We made few changes in our DAQ scheme.

## Slide 3: Experimental hall
Control rooms
OMC4DBD setup

## Slide 4: Target setup
& C1 & C2 &

## Slide 5: Target setup (C0)
C0
D = 80 mm
Dhole=25 mm
HScint = 10 mm
Bi source at different positions @C0
1 cm ring made of plastic scintillator and wrapped into 5 um mylar film.
The counter is attached to modular PMT by “fishtail” lightguide.
Ligthcollection inhomogeneity doesn’t exceed ~30% from the Bi source measurements in different positions.

## Slide 6: Target setup (C1 &C2)
С1 & С2
D = 80 mm
HScint = 0.5 mm
Cosmic muons @C1
Cosmic muons @C2
Thin 0.5 mm plastic scintillator circle glued into acrylic lightguide.
The lightguide has ring shape with wedge profile.
The counters are covered with 5 um mylar films and separated by the same thickness from each other.
The counters are readout by modular PMTs individually.
We saw different light collection for the counters, especially with beam muons (pictures in Igor’s or Elisabetta’s talks?). One has to fix it for the next beam time

## Slide 7: Target setup (C3)
С3
D = 80 mm
HScint = 5 mm
Cosmic muons @C3
Cup-like scintillator surrounding a target holder
Thickness of the C3 counter walls is 5 mm.
A target holder can be inserted through the cut in the wall of С3. The same way for calibration sources.
The counter is attached to R6091 PMT through a light guide made of polystyrene. For 2021 campaign we used plastic scintillator.

## Slide 8: Target setup (C3)
Some bumps and quite high rate at saturation region. This time we reduced amplitude to avoid saturation, but didn’t understand the bumps origin (Daniya’s talk)
Beam @C3

## Slide 9: Target setup equipment
C0 counter
H10720 x2
Built-in HV power supply
0.5 – 1.1 VDC adjustable
C1, C2 counters
H6780
Built-in HV power supply
0.5 – 1.1 VDC adjustable
C3 Counter
3” PMT R6091
With Traco DC-DC for HV
0-4 VDC adjustable
Remote control with
ICPDAS ET-878P
ICPDAS DAC I-87028UW-G

## Slide 10: Target setup equipment
C3 CUP
Lightguide
C2 Counter
C1 Counter
C1 Counter

## Slide 11: Beam tuning
Optimal conditions:
Minimize C0 and C3
Maximize C1 and C2
Minimize muonic X-rays from oxygen and carbon

## Slide 12: Beam tuning

## Slide 13: Ge-detectors set (actual)
BigMac cryostat with sheet steel frame
CryoPulse 5
(Electrically Refrigerated Cryostat)
BigMac cryostat with ITEM frame
x2
x1
x5
Konstantin Gusev & Nadezda Rumyantseva talks

## Slide 14: Ge-detectors setup assembly
The final configuration
BEGE 3830

## Slide 15: Experimental hall
Trolley with Ge-detectors
Beam line
Racks with electronics
LN Dewars

## Slide 16: Ge-detectors setup
The final configuration
8 Ge-detectors mounted on the frame with 15 cm distance from the beam axis.
6 detectors with LN auto filling system
Neutron detector

## Slide 17: DAQ scheme

## Slide 18: Beamtime schedule
Step | Time
Assembling and tuning of the setup | 22.09.2022-24.09.2022
Calibration runs | 25.09.2022-26.09.2022
natMo measurements (together with beam tunning) | 26.09.2022-29.09.2022
Calibration runs | 30.09.2022
100Mo | 01.10.2022-08.10.2022
Calibration runs | 08.10.2022
Deconstruction | 08.10.2022-10.10.2022

## Slide 19: Count rates for Mo-100

## Slide 20: Main issues during 2022 campaign
Bad/old LEMO cables are the main reason of the lost time. During the setup tunning we saw different impacts:
  Double peaks from germanium detectors;
  Terrible energy resolution;
  Interruption of FADCs channels operation.
Correlation between energy resolution and pulser plugging. Possibly, caused by some cables, but the problem wasn’t solved during the campaign.
Some detectors showed high LN consumption. One should think about pumping the cryostats before the next beamtime.
We had power outage on 26/09/2022 during dewars refilling. Most likely, it was caused by the penetration of condensed water into the power strip
Detector 7 (75%) tripped on 29/09/2022 due to heating. Possible reasons are problems with refilling or low vacuum in the cryostat . We replaced it with 3B (BEGE 3830).

## Slide 21: Beam time distribution
Prleminary, we have more then 70% of time with usefull data. BUT:
18% of test runs is too much for a future campaign. If we start with an already well-configured installation, it will significantly reduce the testing time. However, we were on schedule…
Lost time began with detector 7 tripping (more than 1 day). However, during the replacement, we fixed some problems with the cable connection and recognized its significant impact on data acquisition.
We have more than a half time of Mo-100 data.
During 2022 campaign we had very stable beam with minor interruptions.

## Slide 22: Beamtime data taking navigation
We export MIDAS database to Grafana dashboard to simplify navigation in campaign data taking:
Countrates for the Ge-detecors and the counters are available;
Time stamps for both MIDAS and ALPACA daq systems can be displayed;
Annotations for different measurements;
Usefull for transition runs (during shutter closing or opening);
Unexpected behavior of the setup can be explained together with the data the taking tables.

## Slide 23: Beamtime data taking navigation

## Slide 24: Beamtime data taking navigation

## Slide 25: Beamtime data taking navigation

## Slide 26: Beamtime data taking navigation

## Slide 27: Beamtime data taking navigation
Access:
remotely at http://159.93.76.145:821
install MySQL server and Grafana dashboard, then download database and dashboard json files from https://wiki.tum.de/display/gainmomentum4dbd/Beamtime+2022

## Slide 28: Beamtime data taking navigation
Both ALPACA and MIDAS data taking tables are avaliable at wiki.tum.de
The runs timestamps are synchronized with elog and logbook (2 minutes uncertainty)

## Slide 29: Beamtime data taking navigation
Both ALPACA and MIDAS data taking tables are avaliable at wiki.tum.de
The runs timestamps are synchronized with elog and logbook (2 minutes uncertainty)

## Slide 30: Outlooks
The target device allows tune the beam with enough accuracy, but has several drawbacks:
    Different light yields for C1 & C2 counters assume nonuniform settings (thresholds, ranges, etc.) for the DAQs and require individual tunning approach.
    Hard to distinguish events from muons, electrons and gammas in C3. Replacement of the lightguide didn’t change the spectra shapes. To be investigated…
Proper cabling with “fresh” cables is absolutely necessary. This helps to save time.
We saw vacuum degradation and LN consumption increasing for the cryostats. One should take care about pumping in advance.
Pulser problem hasn’t been solved until now. We don’t understand why the test channel connection drasticaly affects on energy resolution.
Most likely, we will not use our frame for 2023 beamtime.
We need time synchronization for ALPACA and MIDAS server. This will simplify parallel analysis.
Use insect repellents while walking at PSI forests!

## Slide 31: Thank you for your attention!

## Slide 32
C3 spectra 2021 vs 2022 (beam on)

## Slide 33: NIM electronics

## Slide 34: NIM electronics