## Slide 1: Status of the NICA-MPD PLATFORM
Author:
Alexander Fedunin
Sector No 3; Engineering Support Group
Joint Institute for Nuclear Research
XII MPD Collaboration meeting

## Slide 2
The NMP contains the electronics for collecting and processing data from the MPD, power supply(hv,lv) and gas distributors sub detectors.
NICA-MPD-Platform (NMP)

## Slide 3
XII MPD Collaboration meeting
NMP consist of (4 separate modules, which installed vertically).
Each module includes 1 room, which divided by 2 corridors.
Inside module there are racks with electronics, cooling and power supply equipment and other engineering systems.
Three zones: cold corridor, hot corridor, space under the raised floor.
Each floor has ventilation and air conditioning systems.

## Slide 4: PARTS of NMP:
IT RACKS on the NMP
Cooling System
Main electrical distribution board
Structed Cabling(fiber optic)
Access control and management system
CCTV video surveillance system
Аutonomous fire extinguishing system
Monitoring system
XII MPD Collaboration meeting

## Slide 5: IT RACKS on the NMP
XII MPD Collaboration meeting
All floors have 2 corridors: hot and cold.
Main power supply equipment is located on the ground floor.

## Slide 6: Main electrical distribution board
XII MPD Collaboration meeting
The platform power supply is isolated on each floor.
Each floor has its own power distribution board, which makes it possible to carry out preventive maintenance of the floor without shutting down the entire NMP.

## Slide 7: IT RACKS on the NMP
XII MPD Collaboration meeting
On the second, third and fourth floors there are 8 equipment racks and 4 fan coil units.

## Slide 8: IT RACKS on the NMP
Each Rack C3 ECO 48U 600*1200, black, perforated door has
MPD equipment racks
PDU controlled C3, 3 phases, 32A, C13-24, C19-12.
GreenMDC ventilation panel, active, 1U
XII MPD Collaboration meeting

## Slide 9: COOLING SYSTEM
XII MPD Collaboration meeting
The NMP cooling system is an integral part.
It is designed for:
Cooling equipment from overheating
Maintenance and regulation of the set air temperature
Ensuring round-the-clock and year-round temperature conditions.

## Slide 10
Cable system NMP (fiber optic)
XII MPD Collaboration meeting

## Slide 11
Mechanical Transfer Push-On(MTP) 24 fiber optic line.

## Slide 12: Access control and management system
XII MPD Collaboration meeting
Universal controller CT/L14.1
Lock controller CL211.3
JINR employees will be able to use their badge for access to all rooms.

## Slide 13
CCTV video surveillance system
Video control will be carried out in the same way as in MPD Data Center. There will be 3 video cameras installed on each floor.
These cameras archive videos and save them for at least 30 days in motion-based recording mode and the ability to remotely connect to the Video Control system through any browser on any OS, and to a mobile application.

## Slide 14: Аutonomous fire extinguishing system
XII MPD Collaboration meeting
Chladon 125 is used

## Slide 15: Monitoring system
XII MPD Collaboration meeting
The system shows:
• Temperature and humidity. There are 4 sensors, which installed on each floor.
• fire alarm signals on each floor.
• power monitoring by floors and in each rack.
• ventilation system signal.
• signals from access control and management system.
All critical signals: fire, power overload, power supply outage, cooling system leakage will be duplicated by SMS to responsible employees.

## Slide 16: Stages of work
 |  | April 2023 |  |  |  |  |  |  |  |  |  |  |  | May | June-September | September | October
 |  | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 1-30 |  | 1-30 | 1-31
№ | Stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 | Delivery of all engineering systems to JINR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 | Installation of metal structures |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 | Installation of structures |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | Installation of raised floor and engineering networks |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 | Connecting the NMP water cooling system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 | The closure of Building 17. Work is stopped |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 | Installation of the structure of the 4th floor and engineering systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 | Testing of all NMP systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
XII MPD Collaboration meeting

## Slide 17
№ | PARTS of NMP | WORK DONE (%)
1 | IT RACKS on the NMP | 
2 | Cooling System | 
3 | Main electrical distribution board | 
4 | Structed Cabling(fiber optic) | 
5 | Access control and management system | 
6 | CCTV video surveillance system | 
7 | Аutonomous fire extinguishing system | 
8 | Monitoring system | 
9 | Testing of all NMP systems | 
100 %
100 %
100 %
100 %
100 %
100 %
100 %
Results
XII MPD Collaboration meeting
100 %
80 %
0 %
XII MPD Collaboration meeting

## Slide 18
List of cables and pipes
 |  |  | 14 | 12 | 10 | 8 | 6 | 4 | 2 | 1 | 3 | 5 | 7 | 9 | 11 | 13
 | Purpose | Diameter, mm | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty | Qty
EDTC | Data cable | 3 | 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 78
ESNC | Sense cable | 9,4 | 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39
EPWC | Power cable | 14,7 | 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39
ESRL | Service cable(1) | 1х13 | 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39
EWCT | Wotercooling tubes | ~20 | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26
EACT | Air cooling tubes for FE and BOX | ~20 | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26
TSGC | Signal | 13 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 150
THVC | HV | 8,5 | 0 | 4 | 4 | 8 | 8 | 12 | 12 | 16 | 16 | 20 | 20 | 24 | 24 | 28
TLVC | LV Cable | 13 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 8
TUTC | UTP | 6 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 8
TTRL | Trigger (OR) | 10 | 2 | 2 | 4 | 4 | 6 | 6 | 8 | 8 | 10 | 10 | 12 | 12 | 14 | 16
TGST | Gas Pipes | 12 | 2 | 2 | 4 | 4 | 6 | 6 | 8 | 8 | 10 | 10 | 12 | 12 | 14 | 16
 | TPC gas system |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TGTT | Purge TPC (in/out) | 40 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | LV |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TLPC | LVDB: low-voltage cable supply | 12 | 0 | 8 | 8 | 16 | 16 | 24 | 32 | 32 | 32 | 32 | 40 | 40 | 48 | 48
TLSC | LVDB: sense wire | 2,5 | 0 | 4 | 4 | 8 | 8 | 12 | 16 | 16 | 16 | 16 | 20 | 20 | 24 | 24
TCPC | Controller: low-voltage cable supply | 12 | 0 | 2 | 2 | 4 | 4 | 6 | 8 | 8 | 8 | 8 | 10 | 10 | 12 | 12
TCSC | Controller: sense wire | 2,5 | 0 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 6 | 6
TLCC | LVDB: slow control cable | 9 | 0 | 2 | 2 | 4 | 4 | 6 | 8 | 8 | 8 | 8 | 10 | 10 | 12 | 12
 | DAQ |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TDCC | Controller: slow control | 7 | 0 | 2 | 2 | 4 | 4 | 6 | 8 | 8 | 8 | 8 | 10 | 10 | 12 | 12
TDDO | Controller: DATA QSFP | opt. 3.3 | 0 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 6 | 6
TDTO | Controller: data and trigger/ sync SFP+ | opt. 3,9x1,8 | 0 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 6 | 6
TDTC | Controller: trigger | 6 | 0 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 6 | 6
TDRC | Controller: Reset | 6 | 0 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 6 | 6
TDSC | Controller: Sync | 6 | 0 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 6 | 6
TDQO | Reserve cables QSFP | opt. 3.3 | 0 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
TDSO | Reserve cables SFP+ | opt. 3,9x1,8 | 0 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | ROC chamber |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TRAC | for ROC: HV power supply for anode sections | 4,1 | 0 | 0 | 4 | 4 | 8 | 8 | 8 | 8 | 12 | 16 | 16 | 20 | 20 | 24
TREC | for ROC: HV electrode adjusting supply | 4,1 | 0 | 0 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 4 | 4 | 5 | 5 | 6
TRNC | for ROC: HV locking grid | 4,1 | 0 | 0 | 2 | 2 | 4 | 4 | 4 | 4 | 6 | 8 | 8 | 10 | 10 | 12
TRCC | for ROC: cameras electrode (cathode), test signal | 4,1 | 0 | 0 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 4 | 4 | 5 | 5 | 6
TRSC | from ROC: signal cable (anode) | 4,1 | 0 | 0 | 4 | 4 | 8 | 8 | 8 | 8 | 12 | 16 | 16 | 20 | 20 | 24
 | Sensors |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TSSC | Temperature sensor cable Pt100 | 8 | 0 | 0 | 3 | 3 | 6 | 6 | 6 | 6 | 9 | 12 | 12 | 15 | 15 | 18
TSPC | Cables from pressure sensers on pipes cooling + stabilization | 7,8 | 0 | 0 | 4 | 4 | 8 | 8 | 8 | 8 | 12 | 16 | 16 | 20 | 20 | 24
TSTC | Cables from temperature sensers on pipes cooling + stabilization | 7,8 | 0 | 0 | 4 | 4 | 8 | 8 | 8 | 8 | 12 | 16 | 16 | 20 | 20 | 24
 | HV TPC central membrane |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
THEC | Central HV electrode TPC | 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
THRC | low-voltage cable input for resistors (centr). HV electrode | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
 | Thermostabilization |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TTOT | external thermal screen stabilization pipes | 32 | 0 | 0 | 2 | 2 | 2 | 4 | 4 | 6 | 6 | 7 | 8 | 8 | 10 | 10
TTTT | end Thermal Shield Stabilization Pipes | 32 | 0 | 0 | 0 | 0 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 4 | 4
TTIT | inner thermal shield stabilization pipes | 32 | 0 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
TTRT | Pipes stabilisation ROC chambers housings | 32 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 2
TTFT | TPC flange stabilisation pipes with spokes | 32 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 3 | 4 | 4 | 4 | 4 | 4 | 4
TTST | Stabilization pipes FE SAMPA | 32 | 0 | 4 | 4 | 6 | 8 | 9 | 12 | 12 | 15 | 16 | 17 | 20 | 20 | 24
 | Cooling (12 loops) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TCLT | Cooling pipes LVDB, controllers & FE FPGA | 32 | 0 | 0 | 0 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 4 | 4
 | TPC laser system |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TLWC | Cable for WEB camera control system floor laser beam | 7 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2
 | TPC gas system |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TGST | Purge of C1C2 and C3C4 (input/output) | 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
 | Hydraulic actuators |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TSGC | Position centers hydraulic cylinder | 6 | 0 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 8
XII MPD Collaboration meeting

## Slide 19: Cable routing
XII MPD Collaboration meeting

## Slide 20
№ |  | WORK DONE (%) | Completion of work
1 | Data collection |  | -
2 | Grouping cables into trays |  | -
3 | Design |  | 01.11.2023
4 | Purchase of equipment |  | 29.12.2023
5 | Installation |  | 01.03.2024
6 | Cabling |  | -
100 %
100 %
Results
XII MPD Collaboration meeting
100 %
80 %
100 %
0 %
100 %
0 %
100 %
0 %

## Slide 21: Thank you for Attention
Author: Alexander Fedunin
Email: fediunin@lhep.ru
XII MPD Collaboration meeting