## Slide 1: Status of Forward Hadron Calorimeter (FHCal)
A.Ivashkin
Institute for Nuclear Research RAS, Moscow
on behalf of the FHCal group
12th MPD collaboration meeting, Oct., 2023.
FHCal overview;
FHCal modules;
FHCal readout;
FHCal in trigger
Installation to MPD

## Slide 2
FHCal
Two arms of hadron calorimeter at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules.
~1x1 m2 each part.
Beam hole 15x15 cm2.
Lead/scintillator sampling calorimeter.
Longitudinal segmentation;
Light readout- WLS-fibers;
7 sections/photodetectors in each module.
FHCal in MPD
FHCal modules

## Slide 3
The centrality of the collision;
The reaction plane orientation;
Minimum bias trigger;
Physics in forward rapidity?
Tasks of FHCal :
X
Centrality:
2D-Fit of energy distributions in FHCal modules

## Slide 4
All (90+spare) FHCal modules are assembled and tested with cosmic rays.
Modules are ready for the delivery at MPD site.
Mini-FHCal is operating now at INR.
The activities with modules:
Calibration with cosmic muons;
Development of readout;
Development of FHCal trigger;
Development of Detector Control System;
Monitoring system.
FHCal modules
Modules in stockroom

## Slide 5
Readout electronics (FEE)
Two PCBs in each module with:
7 photodetectors ;
Photodetectors – MPPCs;
two-stage amplifiers;
HV channels;
LED calibration source.
MPPC: new type
S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
100 units of FEE were produced and tested.

## Slide 6
ADCs for FHCal
FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
Bench for ADC tests
All 10 ADC boxes were produced last year.
All ADCs were tested this year at JINR.
4 ADCs were repaired during the tests.
All ADCs are ready for installation.
5 ADCs for each part of FHCal

## Slide 7: FHCal readout and control
FEE
FEE
FEE
1
2
44
…
on detector
ADC64 (1)
(9 modules)
ADC64 (2)
(9 modules)
ADC64 (5)
(8 modules)
…
near detector
FHCal arm
HVsys
DCS Control box
power supply
signal cables
General Control System (Tango)
- Ethernet
DAQ
~20m cables
Both FHCal arms have the same readout scheme.

## Slide 8: FHCal cabling
Prepared by
M. Rumyantsev
Patch panel is not ready.
Must be constructed in nearest time

## Slide 9
Detector Control System (DCS)
DCS Tasks:
Control of HV at photodetectors (MPPC’s);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
Status of DCS:
It is practically fully operational;
Further improvements of functionality are going on.
LAN
FEE
Database
FHCal New Slow Control (proxy)
General Slow Control
System Module
System Module
FEE
FEE
FEE
FEE
FEE
RS485
Connection diagram

## Slide 10
FHCal in trigger
Threshold 2 MeV/module
Trigger efficiency ~98%
Dependence of trigger efficiency on the configuration of modules (Au-Au 11 GeV).
Scheme of FHCal trigger

## Slide 11: Preparations for FHCal trigger
Adders of analog signals from individual modules were produces for full FHCal.
The configuration of modules in trigger would depend on FEE and correlation noises. Flexible configuration is to be developed.
Dependence of trigger noise on energy threshold
12-channels signal adders
All adders are working.
The noises are under tests.
It seams that 3 MeV threshold is safe for trigger.

## Slide 12
Energy calibration with cosmic nuons
The energy calibration is planned in self-triggering mode (without external muon trigger).
The different geometries of muon tracks are to be considered.
The selection of different muon tracks can be done by requiring the coincidence of muon signals in FHCal modules and longitudinal sections.
A few versions of energy calibration is under development (with/without correction to pass length).
New MPPC type
~5 MeV
Corrected to pass length in scintillators.
Raw spectrum without selection of tracks
Response of FHCal modules to cosmic muons with different track geometries.

## Slide 13: FHCal integration to MPD (ADC readout)
ADC boxes are placed at the lateral sides of FHCal support
Two halves of FHCal.
ADC cooling with compressed air is planned.
5 pipes from each side are to be available!

## Slide 14: Mechanical support (main elements)
Пластина
Support frame in magnet pole
Basket of FHCal modules
Outer table
Design of all elements was finished!
The production starts now!

## Slide 15: Assembling of FHCal modules in basket
М10 х30
M8
M6

## Slide 16: FHCal installation into magnet pole
Main problem: beam pipe between two FHCal halves
FHCal inserted into pole from inner side
Two FHCal halves pressed together

## Slide 17: Alternative way of FHCal installation from outer side of magnet pole
300
Modification of support is needed
Additional tool is needed

## Slide 18
Summary
All FHCal modules were tested and are ready for delivery at MPD site.
FEE was produced and tested.
Detector Control System is ready and is improved permanently.
Energy calibration procedure is optimized.
FHCal trigger is under development. Flexible configuration of modules is considered.
The design of mechanical platform is finished. The production starts now!
We plan to start the calorimeter assembling at MPD site in the beginning of 2024.
The space an some infrastructure for FHCal assembling must be available!

## Slide 19
Thank you!