## Slide 1: Prolongation Project Baikal-GVD
I.Belolaptikov
DLNP, 07.12.2017

## Slide 2
Gigaton Volume Detector (GVD) in Lake Baikal
Objectives:
  - km3-scale 3D-array of photo sensors
    - flexible structure allowing an upgrade and/or a rearrangement of the main building blocks (clusters)
- high sensitivity and resolution of neutrino energy, direction and flavor content
Central Physics Goals:
- Investigate Galactic and extragalactic neutrino “point sources” in energy range > TeV
    - Diffuse neutrino flux – energy spectrum, local and global anisotropy, flavor content
- Transient sources (GRB, …)
  - Dark matter – indirect search
- Exotic particles – monopoles, Q-balls, nuclearites, …

## Slide 3
Detection Modes – cascades&muons
μ/casc. ~ 1/3 for 1:1:1

## Slide 4
Baikal-GVD : phase 1 (up to 2020)
Cluster: 8 strings
String: 36 OMs
Optical module
 | GVD-1
OMs | 2304
Clusters (8 Strings) | 8
Depths, m | 750 – 1275
Eff. Volume (ESH > 100 ТeV) | 0.4 km3
525 m
120 m
700 m
GVD-1: 8 clusters
Directional resolution
Cascades: ~3
Muons: 0.25 - 0.5

## Slide 5
Assembling the detector
Detector deployment from the ice.
Deployment period: ~20 February … ~10 April

## Slide 6
Stages of deployment of the Baikal-GVD
Live time | Full time | Eff % | Master Records
235d 0h | 302d 15h | 77.7 | 1,796,646,941
Configuration | 2015 | 2016 | 2017
The number of OMs | 192 (8str24) | 288 (8str36) | 576
Geometric sizes | 80m×345m | 120m×525m | 2×120m×525m
Eff. Vol. (E > 100TeV) | 0.03 km3 | 0.05 km3 | 0.1 km3
Cluster-2016 operation

## Slide 7
#3101111 -  candidate
vsec = 0.338 m/ns
Arrival times
Amplitude vs time

## Slide 8
E = 158 TeV, θ = 59°, ρ = 73 m, z = -62 m
shower



## Slide 9
Reconstructed zenith angle distribution with cuts
Polar angle distribution of muons selected with the requirement of at least 6 hit OM's at 3 strings. Data (black dots) is compared to the atmospheric muon flux generated with CORSIKA (dashed histogram) and passed through the detector simulation (histogram)

## Slide 10
Cluster-1: preventive maintenance
Installation of new calibration systems
Cluster-2: deployment
Expedition 2017
The scope of work
The first anchor of the second cluster
Problem
Defective sealant tape
A new way to connect acoustic positioning systems was tested
Calibration system designed for IceCube was installed
Cluster-1

## Slide 11
Cluster-2 deployment
Cluster:
8 strings  36 OMs
4 Acoustic Modems on each string
5 LED calibration units
Size: 525 m   120 m
Fully unified electronics and firmware.
Optical modules are equipped with humidity sensors.

## Slide 12
Detector operation -2017
Cluster 1
Cluster 2
13 April – 15 Jun 2017
 | Full time | Eff., % | Event
Cluster-1 | 64d 7h | 84.4 | 1.87×108
Cluster-2 | 64d 0h | 87.6 | 1.45×108
Eff. Vol. (E > 102 TeV) ~0.1 km3

## Slide 13
~600 m
~1 km
120 m
300 m
April 2017
Taking data
April 2016
Taking data
“Dubna”
Demonstration
Cluster (2015)
BAIKAL-GVD-1
2304 light sensors combined in 8 clusters of vertical strings at 750 – 1300 m depths.
Detection volume 0.4km3
Deployment plan for expedition 2018

## Slide 14
2017 | 2018 | 2019 | 2020
2 clusters (deployed) | 4 clusters | 6 clusters | 8 clusters
Baikal-GVD Stage 1 timeline
GVD Stage 2: extension to 14 clusters
(possibly technologically upgraded) Timeline Phase-2:
2021 | 2022 | 2023
10 clusters | 12 clusters | 14 clusters
A further extension of Phase 2 to more 14 clusters will depends on the worldwide physics situation in the 2020s and last but not least on the performance and physics output of the BAIKAL-GVD detector.

## Slide 15
Status:
The DUBNA cluster installed on April 2015 has been upgraded to a final state one with 288 optical odules in 2016 spring . The second cluster started to operate on April 2017.
The new data taking center at the array site has been installed.
The new shore lab was installed on the site during summer 2017.
The building in Baikalsk is prepared for a local lab and a temporary storage for optical modules of the next stages of the detector.
Infrastructure (site)

## Slide 16
Status (continue):
New living boxes will be deployed on the site up to the end of 2017
Transportation problem from the temporary store in Baikalsk to the shore and cargo handling at the site was resolved by getting 2 cargo vehicles and the crane
All shore infrastructure extension, emergency transportation executed by excavator, track and speed boat.
Infrastructure (site)

## Slide 17: Infrastructure development plans for 2018-2020-21 (on a base of the developed general plan)
Design and build a 30-person canteen and 8-10 person dormitory near the 106 km shore center.
Restore 2 houses: an old shore center at 106 km, and a house at 107 km (both buildings are recognized as a cultural heritage by the Russian government).
Build a pier on 106 km capable of housing 2 boats.
Paperwork and property rights on 460 000 sq. m. of land at 106-107km and 220 000 sq. m. of land in the Baikalsk city.
Renovate mobile housing at 106 km.
Resolve sewage and water supply issues for facilities at 106-107 km.
Build a cable channel underneath the railroad at 106km.
Finish building renovations in Baikalsk.
General improvements for sites at 106-107 km and in Baikalsk.
Due to zoning issues, it is impossible to determine exact time frames for the following tasks. However, while resolving zoning situation might take 1-2 years, all possible preparations will be made so that once the necessary permits are acquired, the infrastructure development plans will be implemented rapidly.

## Slide 18
View of the 106 km shore base

## Slide 19
The assembly and testing of optical modules was carried out in period 21.09.2016 - 10.03.2017
In total, 305 OMs have been prepared and tested
Production rate (including testing) was up to 6 OM/day for 2-3 people
2016
Optical modules assemble

## Slide 20
The optical modules production facility (Rearrangeed 2017)
The facility allows to produce and test up to 12 OM per day
We need to produce and send to the site 600 OM up to end of February

## Slide 21
Long-term testing room (OMs and sections)

## Slide 22
Warm storages

## Slide 23
Prepared place for a container where we are going to make long-term tests at least a one equipped full string

## Slide 24
Expenditures, resources, financing sources |  | Cost of parts (US$), resources needs | Proposals of the Laboratory on the distribution of finances and resources |  | 
 |  |  | 1 year | 2 year | 3 year
Main parts and equipment | 1. Underwater optical module elements 2. Underwater connectors 3. Elements of underwater electronic system of control and data acquisition 4. Elements of underwater cable communications 5. Elements of the acoustic positioning system 6. Infrastructure development and vehicles 7. Electro-optical cable and deployment tool Total | 8 430 K 2 100 K 1 950 K 1 500 K 2 400 K 2 400 K 1 800 K 20 580 K | 2 810 K 700 K 650 K 500 K 800 K 800 K 600 K 6 860 K | 2 810 K 700 K 650 K 500 K 800 K 800 K 600 K 6 860 K | 2 810 K 700 K 650 K 500 K 800 K 800 K 600 K 6 860 K
Recourses needs for the BAIKAL project and proposed schedule of its allocation

## Slide 25
Resources | Standard hour | JINR workshop DLNP workshop | 6 000 3 300 | 2 000 1 100 | 2 000 1 100 | 2 000 1 100
Financial sources | Budgetary resources Budgetary resources | Budget spending | 18 000 K | 6 000 K | 6 000 K | 6 000 K
 | External resources | Contribution from collaboration(s); Grants; Sponsors; Contracts; Other sources | 3 000 K | 1 000 K | 1 000 K | 1 000 K

## Slide 26
№ | Designation for outlays | Full cost | 1st year | 2nd year | 3rd year
 | Direct expenses for the project |  |  |  | 
1 2 3 4 5 6 7 | Networking DLNP workshop JINR workshop Materials Equipment R&D on a contract base Travel expenses | 30.0K US$ 3 300 h. 6 000 h. 14 280.0K US$ 6 300.0K US$ 210.0K US$ 180.0K US$ | 10.0 1 100 2 000 4 760.0 2 100.0 70.0 60.0 | 10.0 1 100 2 000 4 760.0 2 100.0 70.0 60.0 | 10.0 1 100 2 000 4 760.0 2 100.0 70.0 60.0
Total |  | 21 000.0K US$ | 7 000.0K$ | 7 000.0K$ | 7 000.0K$
Estimate of expenditures for the project BAIKAL-GVD, Deep underwater muon and neutrino detector on Lake Baikal
Including budget spending JINR 18 000.0K$ 6 000.0k$ 6 000.0K$ 6000.0K$

## Slide 27: Baikal Collaboration
Institute for Nuclear Research, Moscow, Russia
Joint Institute for Nuclear Research, Dubna, Russia
Irkutsk State University, Irkutsk, Russia
Skobeltsyn Institute of Nuclear Physics MSU, Moscow, Russia
Nizhny Novgorod State Technical University, Russia
Saint Petersburg State Marine University, Russia
Institute of Experimental and Applied Physics, Czech Technical University, Prague, Czech Republic
Comenius University, Bratislava, Slovakia
EvoLogics GmbH, Berlin, Germany
~ 65 physicists and engineers

## Slide 28
A. Avrorin (Moscow, INR) et al., The optical module of Baikal-GVD, Phys.Part.Nucl.Lett. 13 (2016) no.6, 737-746
A. Avrorin et al., Dark matter constraints from an observation of dSphs and the LMC with the Baikal NT200, Published in JETP Vol. 152 (7) (2017) – results in PDG2017
A. Avrorin et al., Data acquisition system for the Baikal-GVD neutrino telescope, Phys.Part.Nucl. 47 (2016) no.6, 933-937
A. Avrorin et al., Neutrino signal at Baikal from dark matter in the Galactic Center, Phys.Part.Nucl. 47 (2016) no.6, 926-932
A. Avrorin et al., Baikal-GVD: first cluster Dubna, PoS EPS-HEP2015 (2015) 418
A. Avrorin et al., Search for neutrino emission from relic dark matter in the Sun with the Baikal NT200 detector, Astropart.Phys. 62 (2015) 12-20
Main publications for 2015-2017 years.
PHD thesis:
Avrorin A.D. Muons registration with deep underwater neutrino telescope Baikal-GVD, Moscow, 2016
Kuleshov D.A. The DAQ system of the telescope NT1000, Moscow, 2014
Sheifler A.A. Optical module of the Baikal deep underwater neutrino telescope Baikal-GVD (development and testing of the detecting system), Moscow, 2016

## Slide 29
JINR group participation
Total FTE (Engineers): 8.8, Total FTE (Scientific staff): 8.3
Assembly and test of OMs and strings
Participation in winter deployment campaigns and summer infrastructure extension expeditions
Access and security service.
Data archive processing and analysis.
Detector calibration and mass processing of data.
Remote control and monitoring systems of detector
Analysis frame software (BARS)
Simulation software and MK production.
On-line software
Development of new methods of event selection and reconstruction.
Data analysis with respect to high-energy neutrinos and neutrinos from dark matter annihilation

## Slide 30
Thank you

## Slide 31
Heavy thunderstorm of June 17, 2017
Cluster-2: critical failure
Both shore PSU failing simultaneously;
Underwater power control system is partially out of operation.
Cluster-1: was not affected
Failed power supplies have been sent to the manufacturer for repairs. At the moment, the second cluster operates on backup power; it is sufficient to keep four out of eight strings operational.
Detector configuration (July – October)
Cluster-1: 8 strings Cluster-2: 4 strings
Power supply problem

## Slide 32
Cluster-1: defective nuts and sealant
~30 OMs were restored during expedition 2017
Defective nuts:
corrosion and destruction
 emersion of underwater
modules.
Defective sealant:
condensate inside the modules
 sharp decrease in reliability
~100 OMs were installed with defective sealant.

## Slide 33
Множественность сработавших ОМ
Фоновое событие - группа мюонов

## Slide 34
Optical module
Angular sensitivity
OM electronics
Mu-metal cage
PMT
Optical gel
Glass pressure-resistant
sphere VETROVEX (17”)
R7081-100 Hamamatsu
D=10 inch. SBA photocathode QE ≈ 35% @ 400nm; Gain ~107, dark current ~8 kHz
Φ220 mm
Quantum efficiency

## Slide 35
Channel
OM: analog output, gain ~108
ADC: 12-bit 200 MSPS (waveform)
Section: 12 optical modules
Trigger: coin. any pairs of nearby OMs
Master records: waveforms of 12 channels
Data transmitting: 2-wire Eth. Extenders (time intervals without pulses are clipped)
String: 3 sections
Section power control
Cluster: 8 strings
Data transmitting: optical line
Event rate: 50 – 250 Hz
DAQ system
GVD Section: 12 channels

## Slide 36
KM3NeT |  |  |  | 
 | 2015 | 2016 | 2017 | 2020
Foreseen |  |  | 24 Str. ARCA 7 Str. ORCA | 230 Str.(ARCA) 115 Str. (ORCA)
Realized so far | 1 DU (36 OMs) ARCA | 2 DUs (72 OMs) ARCA | 1 DU (36 OMs) ORCA | 
Baikal-GVD-1 |  |  |  | 
Foreseen | Dubna 192 OMs | 1 Cluster 288 OMs | 2 Clusters 576 OMs | 8 Clusters 2304 OMs
Realized so far | Dubna 192 OMs | 1 Cluster 288 OMs | 2 Clusters 576 OMs | 

## Slide 37
Deep-water pulsed laser
Wavelength: 532 nm
Pulse energy: 0.37 mJ (~1015 photons)
Flash duration ~1 ns
Attenuation steps: 10-5, 10-4, 10-3, 10-2, 10-1, 1
Purposes:
- inter-cluster calibration
- cascade emulation

## Slide 38
Time
The first Laser Runs: Jun 2017
64 m
LASER
Amplitude
Q, pe
S6
S7
S8
S5
S4
S3
S1
The first tests of the laser operation
Check up of main parameters of the detector with laser:
Uncertainties of the timing calibration of the channels
Precision of the OMs positioning

## Slide 39
Str 8 Section 1
Str 1 Section 1
Str 8 Section 2
New LED light sources for inter-string calibration
3 new LED light sources (LED beacon) for the time calibration of the Strings were installed.
Each LED beacon comprises 12 synchronized LEDs: 6 vertical and 6 horizontal.
Str 1
Str 8
470 nm
LED: Kingbright L7113 PBC-A

## Slide 40
POCAM connection to the DAQ of the Cluster-1
NPort 5250: Ethernet – RS485 converter
300 VDC power commutator
NPort
POCAM
RS-485
300 VDC
Remote access
300 V

## Slide 41
Repair of Cluser-2
String #1 Section #3 Channels #9, #10 (RS485 output of RELE board)
String #2 Section #3 Channels #9, # 10, #11, #12 (restriction on power supply)
String #4 Section #3 Channels #9, #10, #11, #12 (restriction on power supply)
String #6 Section #3 Channels #7, #8, #9, #10, #11, #12 (restriction on power supply)
String #7 Section #1 Channels #1, #2, #3, #4, #5, #6, #7, #11 (restriction on power supply)
1. Repair of cluster center – power module
(thunderstorm)
2. Repair of central modules of the upper sections
String #1 Section #1 Channel #11
String #3 Section #1 Channel #12
- String #8 Section #2 Channel #7

## Slide 42
Counting rates of OMs during
April –September 2014
Amplitude distribution of selected OM recorded pulses
Run 214 – 20 kHz
Run 318 - 50 kHz
1ph.el.= 8 codes
Deep water light background at 1ph.el. level !
Operation - 2014

## Slide 43
Zenith angular distributions of experimental and MC-simulated events after cut on 2 value
- Performance of time measuring systems.
- Reliability of calibration methods.
Efficiency of background suppression.
Selected sample of 2010 string data:
- Trigger condition: >3 hit OMs
- PMT noise: ~15kHz
Noise suppression procedure:
The time difference between the pulses of any pair of OMs should be smaller than the light propagation time.
Muon track reconstruction:
Prototype string: muon reconstruction

## Slide 44
2009
XP1807
R8055
2010
R7081HQE R8055
Prototype string: time calibration
Tests with LED
LED flasher produces pairs of delayed pulses, which are transmitted to each OM via individual optical fibre. Time between pulses dT was calculated from the waveform data.
Time resolution: (dT) = 1.6 ns
=> (1 pulse) ~ 1ns
Tests with LASER
T = <dTEXPECTED – dTLASER >
dTEXPECTED = (r2-r1)cwater
dTLASER - time difference between two channels measured for Laser pulses.
Time error: T ~ 2 ns
97 m
LASER
110 m
OM#7
OM#8
OM#9
OM#10
OM#11
OM#12
OM#1
OM#2
OM#3
OM#4
OM#5
OM#6
97 m
r1
r2

## Slide 45
The site
Shore station
36 km
Location: 104o25’ E; 51o46’ N
Baikal’sk
Workshop&Storage facilities
Baikal water
Abs.Length: 22 ± 2 m Scatt.Length: 30-50 m
Site:
1370 m maximum depth
Distance to shore ~4 km
No high luminosity bursts from biology
No K40 background