DAQ status report
Leonid Afanasyev
on behalf of DAQ group

---
Estimation of raw data flow
Bunch crossing each 80 ns; crossing rate 12.5 MHz,
Collision rate ~3–4 MHz (1st stage about 100kHz)→
Triggerless (or streaming) DAQ to avoid any hardware biases
Data flux was estimated for the maximum luminosity L = 1032 cm-2c-1 and maximum energy √s = 27 GeV.
Within simplified simulation and some safety margin the data flux is estimated as 20 GBytes/s.

---
Front-end electronics for the triggerless DAQ
Front-end electronics of the detectors has to meet the requirements of a free-running DAQ
General FEE requirements from the DAQ system:
Self-triggered (trigger-less) FEE operation
Digitizing on-board
Timestamp included in the output format
Large memory to store the data accumulated in a time slice
Zero suppression
FPGA or ASIC based digital output to DAQ
For the moment only Range System has the Front-End electronics designed according to these requirements (high level of readiness)

---
Data Readout chain
2022

---
Data Readout chain
2024

---
Frontend computer

---
Data collection
Building 17 (SPD)
Building 14

---
Time Synchronization System with TCS-based delivery
Advantages: cheap, easy implantation.
Disadvantages: time calibration of all
synchronization cables required.

---
Time Synchronization System with WR-based delivery
Advantages: time calibration needed
for front-end cards only. Easy adding of
a new branch/detector at any distance.
Disadvantages: expensive, time and
resources consuming implementation.

---
Open questions
Front Electronics cards exists for RS only. Development of dedicated ASICs is started.
Development of L1 Concentrator: Which FPGA circuit ???
Where L1 Concentrator will be installed: inside or outsides the Range system?
(e-link <10m)
Radiation hardness of FPGA, in the case of installation of L1 Concentrator inside the Range system
Which Time Synchronization: White Rabbit or TCS. A working bench for development of the White Rabbit node now is under production.
R&D is required

---
2023 progress
The first attempt to place DAQ elements in place.
Development of some parts of the DAQ software.
Purchase of 5 computers for the DAQ prototype.
Repair of the room for the DAQ prototype in LIT.
Purchase of 3 White Rabbit switches and development kits for TSS development.
Development of the L1 concentrator prototype.
Agreement on the development of the L2 concentrator with Tomsk University.

---
Thank you for your attentions.