## Slide 1
Large-scale tracking detector TREK for cosmic ray muon bundle investigations
at large zenith angles
National Research Nuclear University MEPhI
(Moscow Engineering Physics Institute)
Moscow, 2023
Presenter: Troshin I.Y.
E-mail: IYTroshin@mephi.ru
MEPhI – IHEP Collaboration

## Slide 2: Muon puzzle
where is the logarithm of the measured muon abundance estimate and and are simulations of the estimates for proton and iron showers.

## Slide 3: NEVOD-DECOR experiment
DECOR
System of calibration telescopes (SCT)
Disadvantages: DECOR does not cover full NEVOD side surface and its area is not continuous.
Model of the NEVOD-DECOR
Cherenkov Water Detector (CWD)

## Slide 4: Detector TREK and other detectors of the experimental complex NEVOD
DECOR
System of calibration telescopes (SCT)
SCT
Inner plane
of drift chambers
Outer plane
of drift chambers
The TREK consists of 264 drift chambers
The area of one chamber is 1.85 m2
Detector TREK area is 250 m2
Cherenkov Water Detector (CWD)

## Slide 5: The principle of operation of TREK drift chamber:
Characteristics of DECOR:
DECOR area is 72 m2
Spatial accuracy 1 cm
Angular accuracy 1°
Two-track resolution 3 cm
Field strength
500 V/cm
t
1
t
2
t
3
t
4
250
mm
250
mm
60 mm
–
field-forming wires
–
signal wires
–
cathode wires
–
security wires
Field strength
~7000 V/cm
DECOR chamber:
–
anode wires
Characteristics of TREK:
TREK area is 250 m2
Spatial accuracy 1 mm
Angular accuracy 1.7°
Two-track resolution 3 mm

## Slide 6: Detector TREK
Photo of the TREK detector from the outside
Photo of the TREK detector from the inside

## Slide 7: Reconstructed single-particle event on the TREK
Displaying the reconstructed track
Time scan of signals in the selected chamber
7
Part of the Inner plane
Selected drift chamber

## Slide 8
The event with high muon density in DECOR
A reconstructed event with a large particle multiplicity, blue lines
are particle tracks
Two projections of a multi-particle event

## Slide 9
Reconstruction of the event with a high muon density in TREK
TREK – 51.5°
DECOR – 51.4°
E0 1017 eV
Part of the Inner plane
Selected drift chamber

## Slide 10: Reconstruction of multi-particle events

## Slide 11: Conclusion
We have built the detector TREK, developed the data acquisition system and advanced software tools for efficient data processing.
With a total detector area of 250 m2 and with a two-track resolution of 3 mm, the detector will allow to study muon bundles over a record-wide range of primary particle energies from 1014 to 1019 eV.
The inner plane is complete and is under operation, the outer plane is assembled and will be launched next year
The TREK registers muon bundles with rate 5000 events per day in the zenith angle interval 30° - 90° with multiplicities up to hundreds of muons.

## Slide 12
Thanks for your attention
12
Presenter: Troshin I.Y.
E-mail: IYTroshin@mephi.ru
MEPhI – IHEP Collaboration

## Slide 13: Detector TREK and other detectors of the experimental complex NEVOD
DECOR
System of calibration telescopes (SCT)
SCT
Inner plane
of drift chambers
Outer plane
of drift chambers
The TREK consists of 264 drift chambers
The area of one chamber is 1.85 m2
Detector TREK area is 250 m2
Cherenkov Water Detector (CWD)

## Slide 14: Detector TREK and other detectors of the experimental complex NEVOD
DECOR
Calibration Telescopes System (CTS)
CTS
Inner plane
of drift chambers
Outer plane
of drift chambers
The TREK consists of 264 drift chambers
The area of one chamber is 1.85 m2
Detector TREK area is 250 m2
Cherenkov Water Detector (CWD)

## Slide 15: Extensive air showers
Atmosphere
Earth
Detector
Primary particle
Primary particle
μ
μ
μ
μ

## Slide 16: Reconstructed single-particle event on the TREK
Selected drift chamber
Displaying the reconstructed track
Time scan of signals in the selected chamber
16

## Slide 17
Reconstruction of the event with a high muon density in TREK
TREK – 51.5°
DECOR – 51.4°
E0 1017 eV

## Slide 18: Gas system of detector TREK
СО2
СО2
Ar
Ar
Composition of the gas mixture:
94% Ar + 6% CO2
Gas consumption per cluster is 15 l/h,
per plane is 240 l/h,
for the TREK is 480 l/h

## Slide 19: Software Interface
Noise output block for a certain period of time

## Slide 20
Visualization of single events
20
Section
Number of tracks
Drift chambers
Drift chambers
Number of tracks
20
Single-particle events in the TREK
350,000 events per day

## Slide 21: Data acquisition and TDC
Time-to-digital converter (TDC):
- Altera Cyclone V (FPGA + CPU);
- 8 interfaces for DCs’ connection;
- 32 LVDS channels;
- processing rate up to 1000 s-1.
Server
Computer
~1 300 000
events per day

## Slide 22: The principle of operation of the drift chamber
Characteristics of drift chambers:
Composition of the gas mixture: 94% Ar + 6% CO2
Spatial accuracy 1 mm
Angle accuracy 1.7°
Two-track resolution 3 mm
Electron drift time up to 6 μs
Drift velocity 42 mm/μs
Two types:
1) nDC (field-forming wires from -12 kV to 0 V;
cathodic wires 0 V; signal wires +2.2 kV)
2) pDC (field-forming wires from 0 kV to +12 kV;
cathodic wires 12 kV; signal wires +14.2 kV)
Field strength
500 V/cm
t
1
t
2
t
3
t
4
250
mm
250
mm
60 mm
–
field-forming wires,
–
signal wires,
–
cathode wires,
–
security wires.

## Slide 23: Drift Chamber
Cross section of the drift chamber
Longitudinal section of the drift chamber
23

## Slide 24
Single-particle events in the TREK

## Slide 25: Inner plane TREK is mounted and connected Outer plane TREK is mounted and connected
Chart: 
 | 132
Chart: 
 | 132
–
Filling the outer plane with drift chambers
Filling the inner plane with drift chambers
–
Mounted drift chambers
Mounted drift chambers

## Slide 26: NEVOD-DECOR experiment
DECOR
System of calibration telescopes (SCT)
SCT
Disadvantages: DECOR does not cover full NEVOD side surface and its area is not continuous.
Model of the NEVOD-DECOR