## Slide 2
Ketoprofen - well-known representative of non-steroidal anti-inflammatory drug from the group of propionic acid derivatives.
IUPAC Name: 2-(3-benzoylphenyl)propanoic acid
high analgesic
anti-inflammatory
antipyretic activity
Fig. 1. Chemical structure of ketoprofen
Fig. 2. 3D structure of ketoprofen
2
Formula:
C16 H14 O3
Molecular weight: 254.28 g/mol

## Slide 4
In silico IR and Raman spectroscopy of ketoprofen
DFT calculation on the BP86/def2-SVP level of theory (ORCA)[1]
[1] Neese F. et al. The ORCA quantum chemistry program package //The Journal of chemical physics. – 2020. – Т. 152. – №. 22. – С. 224108.
R enantiomer of ketoprofen
S enantiomer of ketoprofen
(biologically active)
Calculated spectra
4
Raman-spectrum
IR-spectrum

## Slide 5
The melting point of the sample corresponds to the racemic mixture of ketoprofen.
Differential Scanning Calorimetry (DSC) of ketoprofen
DSC curve of ketoprofen sample
NETZSCH DSC 204 F1 Phoenix
calorimeter
Melting point = 95.2 ˚C
5
Heating rate - 10°C/min;
Inert atmosphere (Ar); Temperature range:
25–100°С.
X-ray diffractogram of ketoprofen sample
NETZSCH DSC 204 F1 Phoenix
calorimeter (FLnP JINR)
Radiation: Co metal target; Kα filter; λ=1,7889 Å;
The range 2θ: 5-60°.
X-ray Diffractometer
EMPYREAN (PANalytical) (FLnP JINR)
X-Ray powder diffraction (XRPD) of ketoprofen
By the X-ray powder diffraction and DSC, it was confirmed that the ketoprofen sample is in a crystalline form and corresponds to a racemic mixture of ketoprofen.
X-Ray powder diffractogram of the ketoprofen sample contains sharp peaks which are indicate the crystalline structure of the object.

## Slide 6: Fourier-transform infrared spectroscopy (FTIR) of ketoprofen
Experimental spectrum
6
Nicolet iS5 FTIR spectrometer
The IR spectrum of ketoprofen in a KBr disks (about 0.3% (by weight)) was recorded at the Kurchatov Institute Research Center (Сomplex of NBICS-technologies).
Type: IR transmission spectroscopy
The frequencies were correlated with the oscillation modes by matching the calculated and experimental data.
The range 400-4000 cm-1
Stretching of the carbonyl bonds
Hydroxide group stretching
Stretching with deformation of aromatic rings bonds

## Slide 7: Raman-spectroscopy
Confotec MR200 microspectrometer combined with NIKON Ni upright microscope (FLnP JINR)
λ = 473 nm
Measuring range:
400-4000 cm-1
7
Microimage of a ketoprofen sample
The frequencies were correlated with the oscillation modes by matching the calculated and experimental data.
Experimental spectrum

## Slide 8
Experimental vs in silico IR and Raman spectroscopy of ketoprofen
The selected level of theory (BP86/def2-SVP) corresponds well to the experimentally obtained spectra and is suitable for predicting the parameters of IR and Raman spectrum of ketoprofen.
exp = (0,99± 0,00)*cal
R = 0,99953
For IR spectroscopy
There is a good agreement between the experimental and calculated in the DFT approximation oscillation frequencies of ketoprofen with a values of the coefficients of linear correlation.
exp = (0,984± 0,006)*cal
R = 0,99833
For Raman- spectroscopy
8

## Slide 9
9
Main characteristics of investigated ketoprofen sample determined by experimental methods correspond to those given in the literature for racemic mixture.
By the X-ray powder diffraction and DSC, it was confirmed that the ketoprofen sample is in a crystalline form and corresponds to a racemic mixture of ketoprofen.
A joint analysis of the experimental and molecular modeling data was carried out. As a result, assignment of peaks in the experimental IR and Raman spectra of ketoprofen with main structural fragments of ketoprofen was performed. The most intensive peaks in these spectra corresponds to the v(C-O) and v(C=O) vibrations.
There is a good agreement between the experimental and calculated in the DFT approximation oscillation frequencies of ketoprofen using the selected level of theory (BP86/def2-SVP).

## Slide 10
Acknowledgments
Alexander V. Belushkin,
Gregory M. Arzumanyan,
Tatiana N. Vershinina,
Olga Yu. Ponomareva,
Sergey N. Malakhov
Frank Laboratory of Neutron Physics
Kurchatov Complex of NBICS-nature like technologies
Liudmila I. Savostina
Dorota Marta Chudoba,
Elena V. Raksha,
Alexander B. Eresko,
Kahramon Mamatkulov
Kazan Federal
University
Institute of Physics
10