## Slide 1
MCORD
MPD Cosmic Ray Detector for NICA
by Polish consortium NICA-PL
Speaker: Dr Marcin Bielewicz (NCBJ-Swierk, JINR)

## Slide 2
Outline
Cosmic Ray Detector – Goals
Main tasks and schedule
Our Experience, Challenges and Possibilities in design, modeling and manufacturing
Estimated cost and Team size

## Slide 3
Trigger (for testing or calibration)
Veto (normal mode -
track and time window recognition)
_____________________________________
Additionally
Astrophysics (muon shower and bundles)
- unique for horizontal events
Cosmic Ray Detector – Goals

## Slide 4
Cosmic Ray Detector – Goals
Cosmic ray air shower created by a 1TeV proton hitting the atmosphere 20 km above the Earth. The shower was simulated using the AIRES package.
PRIMARY PARTICLE
GROUND LEVEL

## Slide 5
Cosmic Ray Detector – Goals
ALICE ACORDE

## Slide 6
2. Main tasks and schedule
Pre-Demonstrator (0-1,5 years)
(Fast preparation – useful for testing the scintillator and simulation)
Demonstrator (1,5-3 years)
(Real size object – testing electronics and methodology)
Final Detector (2-4 years)

## Slide 7
Pre-Demonstrator stage
(measurement of cosmic irradiation)
Azimuthal and horizontal distribution
Angular influence of the building (concrete walls and ceilling)
Testing of scintillator shape (length, width, thickness)
Size and number of optical elements
Numerical calculation – simulation (MCNPX, GEANT4 and CORSIKA, Showersim)
- 4 x wheels ;
- steel stand (profiles 80x80x4)
- plate for 2 tables;
- collar and ring fixed to the stand
- 2 x drilling lead screw table with ball bearing spindle
- 2 x hand wheels with retractable handle
- frame for lead
- lead plates (100x100x20)
- shelves for detectors
- indexing plumeger;
- screws

## Slide 8
Pre-Demonstrator stage - scintillators
Characterization of scintillation response to ionizing radiation:
energy spectra
light output
non-proportionality
energy resolution
emission spectra
detection efficiency
temperature dependences
scintillation decay times
coincidence timing
Cooperation with
scintillators
manufacturers and
providers:
C&A
Amcrys-H
Saint-Gobain
Scionix
Tokuyama
Various measurement techniques used for scintillators and photo-detectors characterization:
gamma-ray spectroscopy
Compton Coincidence Technique
Neutron Activation Analysis
LED induced coincidence measurements
cryogenic measurements (at LN2 temperature)
anti-Compton shielded measurements

## Slide 9
Pre-Demonstrator stage
Pre-tests – off the shelf equipment:
two 5” PMT coupled to plastic
scintillators (START - top, STOP - bottom)
CAENT DT5730 digitizer (with CFD method)
Lead shields
Time of Flight distributions.
Radiation Detectors and Plasma
Diagnostic Division at NCBJ
100 mm Lead shield
gamma-ray transmission
<1% (Eg <4 MeV)

## Slide 10
Pre-Demonstrator stage: light readout
Expertise in SiPM (silicon photomultiplier)
or MPPC (multi-pixel photon counters) use
as photodetectors for scintillation readout.
Wide range of size:
1×1 mm2 to 51×51 mm2.
Cooperation with SiPM vendors:
Hamamatsu
FBK
sensL
Detailed timing studies of scintillator+SiPM detectors.

## Slide 11
Energy spectrum reconstruction
Implementation of more complex muon source definition
Launching particle tracking and the coincidence analysis
Design and validation of the pre-demonstration system , which will be built at NCBJ
Evaluate the muon detection for scintillators of various sizes:
  50 – 200 cm length bars
  5 – 20 cm width
  1 – 5 cm thick
Comparison and calibration with experimental data
Pre-Demonstrator stage
Simulations of muon energy deposition in plastic scintillator (MCNPX and GEANT4),
and multi-purpose shower simulation programs of air shower development (CORSICA and Showersim)

## Slide 12
Marcin Bielewicz, tytuł
12
The first MCNPX simulation of muon energy deposition in plastic scintillator for NICA
Energy spectrum reconstruction
Exemplary MCNPX simulation conditions:
300 MeV muons
Cylindrical plastic scintillator Ø20 × 2.5 cm3 – the same used for experiment at NCBJ
Simple geometry for the validation – muon source perpendicular to the detector face
The maximum energy deposition centroid is around 4 MeV - reasonable result, assuming 2 MeV/cm dE/dx energy loss for muons in organic scintillator. Light generation due to ionization in plastic scintillator will be implemented in the near future.
Pre-Demonstrator stage
Fig. 1. Geometry used (40000 tracks)
µ
Fig. 2. Energy deposition spectrum

## Slide 13
Demonstrator stage
3 copies for 6 scintillators in real size with 24 channels MicroTCA module

## Slide 14
Final Detector stage - proposition
Two surfaces on half circumference
One surface on full circumference

## Slide 15
Pi-Mode Accelerating Strucures (PIMS) delivered by NCBJ and installed on LINAC 4 line at LHC in CERN. Diagnostic measurements confirm very good performance of LINAC 4 PIMS.
„I am glad to announce you that Linac4 has reached its design energy of 160 MeV; the beam has gone successfully through the PIMS section and all cavities behave as expected. This is the final confirmation of the quality of the manufacturing realized at NCBJ, the result of a collaboration started back in November 2010 which has been an example of excellent communication and strong commitment to the result…. Please forward our thanks and congratulations to all the staff at NCBJ that has contributed to this achievement.- Maurizio Vretenar”
Our Experience, Challenges and Possibilities in design, modeling and manufacturing – Cooperation with CERN
12 accelerated structure (C/N)
15 elements in each structure

## Slide 16
Our Experience, Challenges and Possibilities in design, modeling and manufacturing
THE MUON DETECTOR SCHEME OF ANALOG SIGNAL PATH
Photomultiplier are not so good for us!!! MPPC are much better !!!

## Slide 17
uTCA based modular muon trigger system
Detector
AFE
AFE
AMC FPGA
FMC carrier
FMC
FMC
AFE
AFE
AMC FPGA
FMC carrier
FMC
FMC
12x
Another sub-trigger system (AFE + FMC + AMC +MCH)
MicroTCA Carrier Hub (MCH Tongue 3)
Xilinx FPGA on board
Main MCH
Another sub-trigger system (AFE + FMC + AMC +MCH)
10G Ethernet / Aurora
MTCA crate
10/40G Ethernet
Muon trigger out
Triggers @ SYNC
Our Experience, Challenges and Possibilities in design, modeling and manufacturing
THE MUON DETECTOR SCHEME OF DIGITAL SIGNAL PATH

## Slide 18: MicroTCA (MTCA) configuration
Standard MTCA crate
5 or 12 AMC modules
Crate number depends on channel count and sampling speed
At 250MS/s: 192 channels / crate
At 125MS/s: 384 channels / crate
At 80MS/s: 576 channels / crate
At 50MS/s: 768 channels / crate
For several MTCAs one main MCH concentrate data from slaves MHCs to generate final muon trigger
Analog Front-End module
FPGA mezzanine card (FMC)
AMC FMC carrier board
MTCA Carrier Hub

## Slide 19
4. Estimated cost
size (cm3) | no. of scintillators | no. of SiPMs | MTCA crates | unit mass (kg) | total mass (tons)
200x10x5 | 660 | 1320 | 4 | 10 | 6.6
100x5x2 | 2640 | 5280 | 14 | 1 | 2.6
Preliminary assumptions:
MPD size: φ6m × 8m
MCORD size: φ7m x 6m (barrel shape)
Circumference: 2π × 3.5m = 22m
Evaluated single module cost:
plastic scintillator: ~ 100 ÷ 500 €
SiPM: ~ 300 ÷ 500 € for size 24x24 mm

## Slide 20
4. Estimated cost – our team
32 people
Including
20 scientists (profesors and doctors) 12 engineers
from
3 universities and 2 science institutes
With knowledge and experience in digital and analog electronics,
scintillators and photodetectors, nuclear and astrophysics,
data acquisition and analysis, simulation and experiments.
Our group is a member of Polish consortium NICA-PL

## Slide 21
Thank You for Attention
Polish consortium NICA-PL