## Slide 1: Forward Hadron Calorimeter FHCal for MPD and BM@N
A.Ivashkin
Institute for Nuclear Researches RAS, Moscow
on behalf of the FHCal MPD group
1st MPD/BM@N collaboration meeting, April 11-13, 2018.

## Slide 2
FHCal will detect the spectators to measure the geometry of ion collisions.
FHCAL
Two arms of hadron calorimeters at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Acceptance corresponds to pseudorapidity 2.0< <5.0
The Forward Hadron Calorimeter in MPD setup.
The centrality of the collisions:
The reaction plane:
Event plane
Spectator spot

## Slide 3: Main stages of FHCal project.
FHCal TDR (INR-MEPhI-JINR).
The final version is (almost) ready.
Collaboration of 3 institutes.
Contribution of CBM/FAIR.
Production of FHCal modules (INR, Moscow)
Beam tests of modules at CERN
(MoU between JINR and CBM)
Use of FHCal/CBM modules for BM@N
(MoU between JINR and CBM)

## Slide 4
Structure of FHCal – two left/right arms.
Each arm:
45 modules;
Beam hole;
Weight – 9 tons.
Modular Lead/Scintillator sandwich compensating calorimeter. Sampling ratio Pb:Scint=4:1.
Light from scintillator tiles is captured by WLS-fibers and transported to SiPM.
Each module:
Transverse size - 15x15cm2 ;
Total length - 106 cm.
Interaction length ~4 λint;
Longitudinal segmentation – 7 sections;
1 section ~ 0.56λint;
7 photodetectors/module;
Photodetectors – silicon photomultipliers (SiPM).

## Slide 5
Event plane and centrality resolution.
Modules 15x15 cm2 are optimum choice and fit the transverse size of hadron showers (interaction length of lead+scint. λI~20 cm).
Energy deposition in FHCal isn’t monotonic due to beam hole and can’t resolve the central and peripheral events.
The event plane resolution of 200-250: two arms of FHCal (maximum spectator multiplicity) and no influence of magnet field.
The ambiguity in centrality determination can be resolved by taking track multiplicity in TPC.
Or by using other observables in FHCal.

## Slide 6: Other FHCal observable for the centrality measurement.
Ein
Eout
Let’s construct energy asymmetry:
d 3He
t 4He
π+ π-
π+ π-
π+ π-
Mainly, fragments are produced in peripheral collisions and located near beam hole.
Depending on centrality there must be difference in the energy depositions in inner and outer parts of calorimeter.
while pions are produced
in central collisions.

## Slide 7
Calculation of centrality from energy asymmetry – energy correlation.
Ein
Eout
The resolution of impact parameter for central events is determined by low spectator multiplicity.
Only energy bins are used for the calculations.
More advanced two-dimensional analysis can improve the resolution.
Inspite of beam hole FHCal can resolve the central and peripheral events.

## Slide 8
Permanent quality control of scintillator tiles,
WLS-fibers and gluing is performing with 90Sr β-source.
Stages of FHCal production: scintillators.
Tests of different grooves and reflectors
Scintillator tiles with WLS-fibers.
Scintillator tiles in TYVEC reflector.
FHCal scintillator tiles and modules are assembled in workshop of INR, Moscow.

## Slide 9
Stages of FHCal production: modules.
At present, about 1/3 of FHCal modules are ready for the tests.
All FHCal modules will be ready in 2019.
Tests of modules with cosmic muons are done in parallel with the development of Front-End-Electronics and readout.
Lead absorbers and mechanics.
Lead and scintillators sandwiches in box.
WLS-fibers are aligned.
Optical connectors are polished.

## Slide 10
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
7 channels:
two-stage amplifiers; HV channels;
LED calibration source.
Photodiodes, FEE and readout electronics.
Front-End-Electronics:
A first samples of FEE with MPPC photodetectors were developed and produced.
MPPC
Integrator
ADC
τ ~ 20ns
Amp
FEE
Dt ~ 50 ns
Hamamatsu MPPC: size – 3x3 mm2;
pixel -10x10 µm2;
PDE~12%.
Photodetectors:
Full readout chain was tested with cosmic muons and at beam!
Dt ~ 200 ns

## Slide 11
Test of calorimeter supermodule at CERN T9 line.
Proton momentum range: 3-10 GeV/c
Supermodule consists of 9 (3x3) CBM modules.
The FEE and readout are designed for MPD (BM@N) experiment.
Each module has 10 longitudinal sections with 10 SiPMs at the end.
Full size 60x60x160 cm3.
Weight ~ 4.5 tons.

## Slide 12
Muons energy deposition spectra in 10 sections
of central module.
Sect. 1
Sect. 2
Sect. 3
Sect.4
Sect. 5
Sect. 6
Muons deposit
~5 MeV
in one section
Calibration of longitudinal sections with beam muons, 6 GeV/c
Identification of muons – equal energy deposition in first and last half of modules.
Sect. 8
Sect. 9
Sect. 10
Sect. 7
E2 [MeV]
E2 [MeV]
E1 [MeV]
E1 [MeV]

## Slide 13
Spectra of energy sum in first n sections in central module,
protons 3 and 6 GeV/c.
Some part of protons has only ionizing energy loss without hadron shower in first sections.
p= 3 GeV/c
p= 6 GeV/c
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
In 7th section the low energy ionizing peak is disappeared. Energy spectrum has Gaussian shape.

## Slide 14
Comparison of amplitude spectra in sections, protons 6 GeV/c.
E [MeV]
----- MC
----- experiment
----- MC
----- experiment
----- MC
----- experiment
----- MC
----- experiment
Section 1
Section 4
Section 3
Section 2
E [MeV]
E [MeV]
E [MeV]
Experimental and simulation spectra are in good agreement.

## Slide 15
Energy resolution for full supermodule.
⨁b ⨁
Linearity of response.
The stochastic term of ~56% practically doesn't depend on the fitting function.
Good agreement with MC results.
The noise term is almost zero.

## Slide 16
Central module
Full supermodule
Dependence of energy resolution on supermodule length.
The energy resolution for central module and for full supermodule is practically constant starting from the 7 longitudinal sections.
Length of 4λI or 7 longitudinal sections is optimum for momentum range 3-6 GeV/c
p= 6 GeV/c
Longitudinal profile of hadron shower in central module.

## Slide 17
Open issues.
Magnet pole with FHCal (left) and endcup detectors (right).
Mechanical support.
FEE and readout. Final variant?
Simulations: detector performance and physics performance.
Calibration. Cosmic muons, geometry of tracks. Simulations.
Power supplies. Mounting of readout elements. Full integration to MPD.
Operation manpower.

## Slide 18
Present ZDC at BM@N
central part consist of 36 modules with sizes 7.5×7.5 cm2,
peripheral part contains 68 modules of 15×15 cm2.
Total number of modules - 104.
No beam hole.
Proposition of FHCal for BM@N.
MPD/CBM synergy for BM@N: Why?
Modern technics;
Light yield ~x10 higher;
Detection of low energies;
Stable operation at high count rates;
Unification of approaches;
Experience in operation for later MPD/CBM experiments.
MPD modules + CBM modules

## Slide 19
No active beam dump;
No backscattered particles;
No heavy fragments!
Active beam dump;
Backscattered particles;
Problems with heavy fragments!
Event plane resolution: the same in both variants!
Variants of FHCal for BM@N.
CBM modules
MPD modules

## Slide 20
Problems with centrality.
Simulations: LA-QGSM
Au+Au@4.5 AGeV
What are these events?
Leak of heavy ions in beam hole.
Some heavy ions with A>100 deposit energy through e.-m. ionizing loss without hadron cascade.
Correlations between energy asymmetry and energy deposition are much worse than in case of MPD/NICA.
Centrality measurements are not simple in both geometries!
Energy deposition is not monotonic in both cases even without beam hole!

## Slide 21
Conclusion.
The FHCal project is well developed.
But there are a few open questions.
New manpower for both hardware and software is desired!
MeV
First CBM module is already installed at BM@N.
Ar-peak in CBM module.
MeV
section#
Shower profile
Notes: That is all. In conclusion I would like to say that:

## Slide 22
Thank you!