## Slide 1
47th PAC for Nuclear Physics
Januar, 17, 2018, JINR, Dubna
Status of the Factory of Superheavy Elements
Targets, Separators, Detectors
A.G. Popeko
Flerov Laboratory of Nuclear Reactions,
Joint Institute for Nuclear Research

## Slide 2
Targets
material availability
radiation safety

## Slide 3: Target isotopes
Isotope | Enrichment % | Isotope | Enrichment %
232Th | 100 | 244Pu | 98.6
233U | - | 243Am | 99.9
238U | 99.3 | 245Cm | 98.7
237Np | 99.3 | 248Cm | 97.4
239Pu | - | 249Bk | >95
240Pu | 99.8 | 249Cf | 97.3
242Pu | 99.98 | 251Cf | 36
Isotope separators are necessary !

## Slide 4: Actinide Targets for Superheavy Element Research & Discovery
Presented at 3rd International Symposium on Superheavy Elements
Jim Roberto Oak Ridge National Laboratory
September 11, 2017 Kazimierz, Poland

## Slide 5: Inventories of selected actinides at ORNL
Isotope | Approximate amount (mg) | Isotopic % | Notes
Np-237 | ~1000 | >99% | 
Pu-242 | >1000 | >99% | 
Am-241 | >1000 | >99% | 
Am-243 | ~1000 | >99% | 
Cm-244 | ~1000 | 75% | 
Cm-248 | >1000 | 80-95% | 71 mg at >95%, remainder requires recovery processing
Bk-249 | ─ | >99% | Requires HFIR production and chemical processing (10-20 mg per campaign when combined with Cf-252 production, up to 30 mg with special campaigns)
Cf-249 | 135 | >99% | 
Cf-251 | 40-150 | ~35% | Requires recovery and processing from old Cf sources (isotopic separation required for higher enrichment)
HFIR/REDC is a unique resource for production and chemical processing of actinides
ORNL is the repository for actinide isotopes for DOE’s Isotope Development and Production for Research and Application Program in the Office of Nuclear Physics

## Slide 6: Target block design (G.N. Ivanov)
old
new
Ø = 120, 1500 r.p.m. synchronous
Beam wobbler or scanner,
Segmented beam diafragm
Is in use at GFS, SHELS, MASHA
Ø = 150, 1500 r.p.m. synchronous,
e-beam & optical diagnostic,
water cooling

## Slide 7: Separators

## Slide 8
Universal gas-filled separator GFS-2:
manufactured
tested at the SigmaPhy’s site
delivered to Dubna
ready for installation

## Slide 9: Dubna Gas Filled Recoil Separator
In operation since 1989, Ist JINR price 1990

## Slide 10
GFS-2, main elements

## Slide 11: Arrangement of GFS-2 at the DC280 cyclotron

## Slide 12: Arrangement of GFS-2 at the beam line No3
Installation of magnets: Feb. - March 2018
Commissioning: March – Sept. 2018
Obtaining licenses and permits : Jan – Nov. 2018
Onset of first-day experiments: 48Ca+ 243Am – Sept.-Nov. 2018;

## Slide 13
First-day experiments at SHE Factory
48Ca+243Am
48Ca+242Pu
Test experiments I:
Test of functionalities of all the systems of the accelerator and gas-filled separator
40Ar+natDy and 18O+208Pb
Test experiments II:
48Ca+242Pu and 48Ca+243Am
Enough material to prepare “big” targets
Well-studied in previous experiments
Relatively large cross sections
Existing experimental data

## Slide 14: Velocity selector SHELS:
symmetric & asymmetric complete fusion reactions;
multi-nucleon transfer reactions;
nuclear spectroscopy @ target & focal plane
In operation at U400.

## Slide 15
Separator for Heavy ELement Spectroscopy (SHELS)
2020: replacement of 200 mm quadrupoles by 300 mm quadrupole lenses in the first triplet will increase the transmission of slow ERs from asymmetric reactions by the factor of 1.5 (contracted)

## Slide 16
Gas-filled preseparator GFS-3:
& gas-catcher, RS-chamber:
Chemistry
fusion and multi-nucleon transfer reactions
mass-spectrometry and nuclear spectroscopy
laser spectroscopy of heavy atoms
Contracted.

## Slide 17: Gas-filled pre-separators (variants)
Warm: QVDQH
Superconducting: DVH
Warm: QVDVH

## Slide 18: Gas-filled pre-separator GFS-3 (QVDHQHQVD)
Reaction | Transmission
244Pu(48Ca,4n)289114 | 60 %
244Pu(58Fe,4n)298120 | 75 %

## Slide 19: Detectors

## Slide 20: Focal plane DSS-Detectors (Micron Semiconductors, UK)
48 × 128 strips
6144 pixels
128 × 128 strips
16384 pixels

## Slide 21
2020: Replacement of 4 single-crystal Ge-detectors by 4-crystal clover-detectors (contracted)
New focal plane detector GABRIELA
(Gamma Alpha Beta Recoil Investigation with the Electromagnetic Analyser)

## Slide 22: 50Ti beam intensity – 3×1012 pps. 50Ti + 208Pb = 256Rf + 2n
3He – neutron detector system
ε(252Cf) = 40%
Neutron multiplicity measured for spontaneous fission of 256Rf
TKE spectra for S.F. of 256Rf isotope
Notes: For the synthesis of elements heavier than 118, the beams of ions heavier than Ca-48 are needed. In cooperation with our colleagues from France the Ti-50 ions were accelerated at the U400. First experiments were dedicated to the measurement of the average number of prompt neutrons from spontaneous fission of Rf, produced in 50Ti+208Pb reaction using the modernized VASSILISSA separator He-3 neutron detector. These set-ups were developed in accordance with the DRIBS-III project. The average number of neutrons was found to be 4.47 n/SF. These measurements are of special interest for understanding properties of SHE and for their search in nature.

## Slide 23: Data taking systems
Old, analog
New, digital

## Slide 24: SHE-factory building
Thank you for your attention!