## Slide 1
The Correction System of the NICA Booster Guiding Magnetic Field
M. M. Shandov
134 SC JINR, September 27, 2023
Report as recommended by the 58th meeting of the PAC for Particle Physics
Veksler and Baldin Laboratory of High Energy Physics,
Joint Institute for Nuclear Research, Dubna, Russia

## Slide 2
Introduction
NICA Booster
Design. Fields Calculations. Magnetic Measurements
Conclusion
Magnetic Measurements of the Lattice Magnets
Corrector Magnets Systems of the NICA Booster. Main Goals
Investigation of the Magnetic Structure Characteristics
CO Correction Algorithms
DA Calculations
Outlines

## Slide 3
NICA Booster. Main Parameters
Technical specifications of the “Object "Booster" NICA”, 2019
Ion | 
Magnetic rigidity, at injection maximum | 
Circumference, | 
Number of super-periods | 
Number of DFO periods | 
Betatron tune | 
Chromaticity | 
Transition energy , | 
Emittances hor/vert , at injection after acceleration | 
RMS momentum spread, at injection after acceleration | 
Revolution period, at injection after acceleration | 
Ion | 
Number of super-periods | 
Number of DFO periods | 

## Slide 4
Correctors in the Booster Lattice
— Dipole correctors: 24
— Multipole correctors: 8
Total: 32 correctors
“Normal” Dipole
“Skew” Dipole
“Skew” Quadrupole
“Normal” Sextupole
“Skew” Sextupole
“Normal” Octupole

## Slide 5
Goals of the System. Magnet Design
Field Types | Corrections goals | Field | Ampere-turns
“Normal” dipole () | Horizontal orbit | 0.08 T | 5500
“Skew” dipole () | Vertical orbit | 0.08 T | 5500
“Skew” quadrupole () | Betatron tune coupling | 0.6 T/m | 4200
“Normal” sextupole () | Chromaticity | 130 T/m2 | 3900
“Skew” sextupole () | Optics errors | 130 T/m2 | 3900
“Normal” octupole () | Fringe field influence | 1200 T/m3 | 2400
Field Types | Corrections goals | Field | Ampere-turns
 | Horizontal orbit | 0.08 T | 5500
 | Vertical orbit | 0.08 T | 5500
 | Betatron tune coupling | 0.6 T/m | 4200
 | Chromaticity | 130 T/m2 | 3900
 | Optics errors | 130 T/m2 | 3900
 | Fringe field influence | 1200 T/m3 | 2400

## Slide 6
2D FEM Calculation. Results
Calculation | Dipole ( ) | Quadrupole ( ) | Sextupole ( ) | Octupole ()
Analytic (vac.) | 0.03857 | 0.01676 | 7.413*10-3 | 2.007*10-3
FEM 2D (vac.) | 0.03486 | 0.01661 | 7.451*10-3 | 2.010*10-3
 | 10.51 | 0.91 | 0.50 | 0.17
Analytic (yoke) | 0.07204 | 0.03239 | 0.01342 | 3.321*10-3
FEM 2D (yoke) | 0.07334 | 0.03232 | 0.01336 | 3.313*10-3
 | 1.78 | 0.21 | 0.42 | 0.17
Calculation |  |  |  | 
Analytic (vac.) | 0.03857 | 0.01676 | 7.413*10-3 | 2.007*10-3
FEM 2D (vac.) | 0.03486 | 0.01661 | 7.451*10-3 | 2.010*10-3
 | 10.51 | 0.91 | 0.50 | 0.17
Analytic (yoke) | 0.07204 | 0.03239 | 0.01342 | 3.321*10-3
FEM 2D (yoke) | 0.07334 | 0.03232 | 0.01336 | 3.313*10-3
 | 1.78 | 0.21 | 0.42 | 0.17
Field @R=30 mm [T]
Analytic calculation:
Bio-Savart law
Image-Current method
Dipole Corrector
Multipole Corrector

## Slide 7
Magnetic Measurements
Field Type | Measurements | FEM 2D
Quadrupole () | 0.03834 | 0.04422
 | 0.02111 | 0.02548
 | 0.01028 | 0.02501
Octupole () | 7.766*10-3 | 8.446*10-3
Field Type | Measurements | FEM 2D
 | 0.03834 | 0.04422
 | 0.02111 | 0.02548
 | 0.01028 | 0.02501
 | 7.766*10-3 | 8.446*10-3
Field @R=41 mm

## Slide 8
Magnetic Measurements. Booster
45 dipole magnets
24 doublets of quadrupole magnets
Parameter | Dipoles |  | Quadrupoles | 
 | Mean | SD | Mean | SD
Injection Energy (1.6 ) |  |  |  | 
(tilt), mrad | -1.3 | 1.7 | — | 0.1
, mm | — | — | — | 0.1
, T*m | — | 0.19 | — | 0.06
 | -0.8 | 0.6 | -2.1 | 4.6
 | — | — | 1.3 | 4.3
 | — | — | 7.6 | 3.1
 | — | — | 4.9 | 0.6
Parameter | Dipoles |  | Quadrupoles | 
 | Mean | SD | Mean | SD
 | -1.3 | 1.7 | — | 0.1
 | — | — | — | 0.1
 | — | 0.19 | — | 0.06
 | -0.8 | 0.6 | -2.1 | 4.6
 | — | — | 1.3 | 4.3
 | — | — | 7.6 | 3.1
 | — | — | 4.9 | 0.6

## Slide 9
Dynamic Aperture
Dynamic aperture (DA) – domain of the particles are located (coordinates) in 6D phase space, where their motion in electromagnetic field of the facility is stable under the influence perturbations:
the perturbations are systematic and random errors of the lattice magnets and RF-stations
space charge force
impedance of the beam pipe etc.
Only transvers DA are considered (without the synchrotron motion)
Let us introduce the concept of the maximal initial amplitude of a particle oscillation:
– geometric acceptance of the facility
The following tasks are necessary solved for checking this condition:
find DA by numerical simulation
estimate the effect of the different perturbation on the DA value
compare this value with the acceptance of the facility
Calculation for 2D and 4D betatron motion are presented:
the particle tracking turns to build-up the phase-plane plot and correspondence the tune vs. initial amplitude (2D DA)
the particle tracking 5000 turns to calculate 4D DA

## Slide 10
2D DA. Results
The DA value is defined as the area inside the phase trajectory:
Calc. Type |  |  |  | 
 | Sext. Off | Sext. On | Sext. Off | Sext. On
Injection Energy (1.6 ) |  |  |  | 
No errors |  |  |  | 
Total |  |  |  | 
Total+Rnd |  |  |  | 
Extraction Energy (25 ) | -0,8 | 0,6 | -2,1 | 4,6
No errors |  |  |  | 
Total |  |  |  | 
Total+Rnd |  |  |  | 
Calc. Type |  |  |  | 
 | Sext. Off | Sext. On | Sext. Off | Sext. On
No errors |  |  |  | 
Total |  |  |  | 
Total+Rnd |  |  |  | 
 | -0,8 | 0,6 | -2,1 | 4,6
No errors |  |  |  | 
Total |  |  |  | 
Total+Rnd |  |  |  | 
(x,x’)

## Slide 11
4D DA. Results
Initial coordinates:
At each azimuth:
Calculation Type |  |  |  | 
 | Sext. Off | Sext. On | Sext. Off | Sext. On
No errors |  |  |  | 
Total |  |  |  | 
Total+Rnd |  |  |  | 
Calculation Type |  |  |  | 
 | Sext. Off | Sext. On | Sext. Off | Sext. On
No errors |  |  |  | 
Total |  |  |  | 
Total+Rnd |  |  |  | 

## Slide 12
CO correction Algorithms
The method of least squares (m≠n)
Inverse matrix (m=n)
SVD algorithms (m≠n)
Harmonics correction

## Slide 13
Diff. Orbits. Orbit Response Matrix
  Differential Orbits Measurements
    Developed and tested software for the ORM measurements
    The measurement time on the Booster was (cycle 3.2 sec)
Шаг 1
Шаг 3
Шаг 5
Steerer 2S1H. Working point:
  Orbit Response Matrix (ORM)

## Slide 14
Differential Orbits Measurements
Steerer 2S5H
Steerer 1S1V

## Slide 15
Steerers Polarities
Horizontal plane
Vertical plane
3 wrong polarities were found

## Slide 16
Modelling
    Accuracy of compatibility with the model
    correspond to 3D calculations

## Slide 17
Dispersion
  Linear case:
    Accuracy of compatibility with the model at
    CO correction increase the measurement accuracy

## Slide 18
CO Correction. Dynamic Mode
    Dynamic correction mode of CO correction was demonstrated
    First time at the NICA injection complex
    Developed software and measured ORM used
    Main limitation:
      3 steerers not used, minimal operating current (injection)
Injection. CO
Extraction. CO

## Slide 19
Conclusion
The calculations of magnetic fields (analytical and 2D FEM) were carried out. Correlation of results with relative accuracy was observed for the analytical and FEM models. The production of Booster corrector magnets (including magnetic measurements) has been completed M. M. Shandov et. al, Correctors’ Magnets for the NICA Booster and Collider // PEPaN Letters, v.17, 2020
CO distortions caused by field errors observed from magnetic measurements are
The corrected CO distortions up to were established by the presented CO correction algorithms
Required dipole kicks: 0.3% (max=1%) or 0.12 A (max 0.4 A) M. M. Shandov & S. A. Kostromin, Closed Orbit Correction Algorithms of the NICA Booster // Physics of Atomic Nuclei , 85, 2022

## Slide 20
Conclusion
The Booster lattice model was developed in the MAD-X software
The methodology for DA calculations has been tried and tested. The 2D DA exceeds the horizontal and vertical acceptance
The tune vs. initial amplitude dependencies were obtained. Agreement with the behavior of particles in the corresponding phase space the dependencies was get
The 4D DA value 12σ was obtained. The maximal initial amplitudes in the and directions correspond to the 2D DA calculation results M. M. Shandov & S. A. Kostromin, Simulation of the Dynamic Aperture of the NICA Booster Synchrotron Based on Magnetic Measurement Data // PEPaN Letters, v.19, 2022

## Slide 21
Conclusion
Developed and implemented software for measuring differential orbits and ORM (; cycle 3.2 sec)
ORM measured and Polarity check
Compatibility with the model:
    Accuracy at
    correspond to 3D calculations
CO correction demonstrated:
    Local bump
    Dynamic correction of CO correction was demonstrated for the first time. CO (Inj.), (Extr.)
    M. M. Shandov et. al, Investigation into the Magnetic Structure Characteristics of the NICA Booster in Commissioning Runs with the Beam in 2020–2022 // PEPaN Letters, v.20, 2023

## Slide 22
THANK YOU FOR ATTENTION !!!

## Slide 23
Spare Slides

## Slide 24
Tracking Parameters
Calculation for 2D and 4D betatron motion are presented:
the particle tracking turns to build-up the phase-plane plot and correspondence the tune vs. initial amplitude (2D DA)
the particle tracking 5000 turns to calculate 4D DA
Calculation results separates into the follow types:
without errors: No errors
misalignment errors: Allign
misalignment errors and deviation of the integral value of the main magnetic field: Allign+Int
only mean values of all error types: Total
the mean and standard deviation values of all error types (2000 “drawing”): Total+Rnd
Calculation conditions:
the harmonics of the magnetic field were determined as absolute thin multipole elements at each of the magnet edges
the initial tracking point in the center of the straight section of the first superperiod (the injection point into the Booster)
the initial state vector in phase-space was defined as:

## Slide 25
2D DA
The use of the Poincaré and Hénon mapping (sections) is a common technique for analyzing complex dynamical systems
transformation of coordinates Poincaré mapping
transformation of the when passing through all elements of the accelerator: one-turn map
the set of all of the one-turn maps : Poincaré section. For a periodical lattice structure:
The Hénon map and action-angle variables could be obtained by transformation to the Normal (Jordan) form of the Floquet solution (Floquet transform):
the radius of the phase-space trajectory:
one-turn mapping is corresponded to a rotation in the phase-space by an angle
the axis of rotation is an elliptic stable point
closed phase trajectories are the one-dimensional Kolmogorov–Arnold–Moser tori

## Slide 26
Orbit Response Matrix
,
Basic relationships
For the periodical structure of the facility:
For m steerers and n BPMs:
CO corrections problem:

## Slide 27
Bump Orbit