## Slide 1: Радиационные испытания концентратора данных на базе ПЛИС Artix-7 для кремниевой трековой системы установки BM@N Шитенков М.О., Дементьев Д.В., Леонтьев В.В., Шереметьев А.Д., Мурин Ю.А.

## Slide 2: Introduction
GBTxEmulator is a board for readout data from modules of the Silicon Tracking System.
GBTx-Emulator
Twinax cable
10m long
STS module
Optical fiber
DPB
x3
Task:
Tests of the SEU rate of the GBTxEmulator board based on FPGA Xilinx Artix7;
SEU mitigation core integration and testing;
GBTxEmulator error rate estimation in BM@N environment.
STS Readout system

## Slide 3
Trenz TE0712-02-100-2C
FPGA Artix7
XC7A200T
FPGA based interface between the Front-End Electronics and the Data Processing board
Features:
Provides GBTx ASIC functionality;
  Fast time deterministic transport of downlink massages;
  high-speed transmission of hit data in the uplink direction;
FPGA platform: Trenz TE0712-02-100-2C from Xilinx;
4.8 Gb/s link optical links connecting with the DPB;
Control interface: IPbus via 100 Mb/s Ethernet, UART, JTAG;
E-Link interface:
  48 E-Links with 80 Mb/s data rate;
  6 clocks (40 MHz);
  6 downlink.
Front-end
GERI
Power
IPbus
GBTxEmu v.2.2
Block diagram of the Firmware GBTxEMU
GBTxEmulator
GBTxEmu v.2.1

## Slide 4: Interactions of Radiation with Electronic Devices
The effects of radiation on electronic devices and materials depend on:
Type of radiation (photon, electron, ion, neutron, …)
Rate of interaction
Type of material (Silicon, GaAs)
Component characteristics (process, structure,…)
Consequences
Ionization: Total ionizing Dose (TID) and Single Event Effect (SEE)
Displacement Damage (DD or TNID)

## Slide 5: Main radiation effects

## Slide 6: Improve FPGA SEU Robustness
Mitigation layer | Strategy | Protection
Logic level | Triple module redundancy | Fabric USER Logic
 | Soft error mitigation | Configuration memory
Device level | Flash scrubbing | Multi-boot with 6 copies
 | Remote JTAG | Scrubbing FPGA or FLASH
Board level | Remote power control | Individual remote power on\off
FPGA architecture
Static RAM

## Slide 7
The main drawback for SRAM-based FPGAs is the vulnerability of the configuration memory.
• Soft Error Mitigation IP (SEM)
• SEM makes use of built-in primitives for the detection and correction of SEUs on the configuration memory (CRAM)
• It is a controller that brings together the ECC FRAME, the ICAP and provides an external interface.
  • ECC/CRC error detection – error correction
  • 13-bit Hamming code
  • UART interface for status/error reporting
  • SEM can detect two bit failures per frame
  • It cannot correct BRAM and Flip Flops
Soft error mitigation
Block diagram of the SEU mitigation interface

## Slide 8: GbtxEmulator radiation test
1000 MeV proton beam (SC-1000 @ PNPI);
Beam diameter: 20 mm;
Time: 45 hours;
Flux: 1*104 - 5*106 cm-2 s-1
Controlled parameters:
  SEU CRAM rate;
  Error classification;
  Power supply current;
  Flux.
BEAM
FPGA
GBTxEmulator board

## Slide 9: SEU & MBU cross section
Total: 2666 SEU; 126 MBU;
Fluence 5,7*1010;
TID: 1,18 kRad
Chart: SEU classification
| Essential, Correctable | Non-Essential, Correctable | Essential, Uncorrectable
 | 1276 | 1264 | 126
Chart: Upset cross section (cm2/bit)
upset cross section/bit/cm2 | 2.8253e-15 | 3.0934e-15 | 2.5079e-15 | 5.3967e-15 | 5.3721e-15 | 4.6515e-15 | 5.9472e-15 | 6.3626e-15 | 4.3692e-15 | 5.8489e-15 | 4.0331e-15 | 5.8984e-15 | 5.8414e-15
Chart: MBU cross section/die
MBU cross section/device | 1.6807e-08 | 7.7778e-09 | 1.6667e-08 | 2.4633e-08 | 2.3077e-08 | 3.0331e-08 | 2.7104e-08 | 1.541e-08 | 2.3148e-08 | 1.4535e-08 | 1.221e-08 | 1.3889e-08 | 1.2077e-08
SEU Cross Section: (3,94 ± 2) E-15 cm2/bit
MBU Cross Section: (2,58 ± 1.3) E-16 cm2/bit

## Slide 10: Comparison Cross Section with other experiments
Facility/Beam | CRAM, [cm2/bit] | BRAM, [cm2/bit]
ПИЯФ (1000 MeV Proton) | 3.94 × 10−15 | N/A
LANSCE (Xilinx, WS Neutron 1-800 MeV) | 6.99 × 10−15 | 6.32 × 10−15
CERN H4 (HE Hadron) | 1.50 × 10−14 | 1.40 × 10−14
TSL (180 MeV Proton) | 8.29 × 10−15 | 8.19 × 10−15
TSL (WS Neutron) | 6.55 × 10−15 | N/A
LANSCE (WS Neutron 1-800 MeV) | 6.89 × 10−15 | 6.15 × 10−15
Facility/Beam |  | 
ПИЯФ (1000 MeV Proton) | 3.94 × 10−15 | N/A
LANSCE (Xilinx, WS Neutron 1-800 MeV) | 6.99 × 10−15 | 6.32 × 10−15
CERN H4 (HE Hadron) | 1.50 × 10−14 | 1.40 × 10−14
TSL (180 MeV Proton) | 8.29 × 10−15 | 8.19 × 10−15
TSL (WS Neutron) | 6.55 × 10−15 | N/A
LANSCE (WS Neutron 1-800 MeV) | 6.89 × 10−15 | 6.15 × 10−15
Good correlation!

## Slide 11: SEU rate in BM@N environment
Location racks with GBTxEmu
Radiation background is 200 times higher than normal background.
Time: 5 years with 3 months beam time
TID: 40 Rad (Total Ionizing Dose)
NIEL: 4*109 n/cm²; (Non-Ionizing Energy Loss)
Neutron flux: 100 cm-2s-1
Hadron flux (>20 MeV): 1 cm-2s-1
MTBF (mean time between failures for CRAM): 8 h (recoverable), 126 h (unrecoverable)
E. Letvinenko ( FLUKE simulations)

## Slide 12: Conclusion
Operation of the FPGA based GBTxEmulator board in the radiation environment was tested;
Usage of the board with existing firmware in BM@N environment was proved;
Artix-7 XC7A200T SEU Cross Section (3,94 ± 2) E-15 cm2/bit (1000 Mev protons)
Mean time between failures: 8 h (soft mitigation), 126 h (full system reboot)
SEU – 95% (recoverable with implemented logic); MBU – 5% (unrecoverable, only detection and reboot);
After the experiment, GBTxEmulator is fully functional ( TIDcollect >> 30 times >> TIDBM@n). Safe dose (< 5 kRad)