## Slide 1
K. Berestov, D. Pugachev
Jinr, Dubna, Moscow Region, Russia
Simulation of the Permanent Magnet System for Compact 14 GHz ECR Ion Source

## Slide 2
Basics of the ECR Ion Sources
Magnets for axial field
Permanent magnet hexapole
f[GHz] | B[T] | nec [cm-3]
2.45 | 0.0875 | 7.44x1010
6.4 | 0.23 | 5.08x1011
10 | 0.36 | 1.24x1012
14 | 0.5 | 2.43x1012
16 | 0.57 | 3.2x1012
18 | 0.64 | 4x1012
28 | 1 | 1013
ECR Ion Source

## Slide 3
Low energy nuclear physics.
Material Sciences.
Scientific motivations:
Characterization of materials through the use of Analytical Techniques of Nuclear Origin:
ERDA, RBS, NRA, PIXE
Production and use of heavy-ion beams with high energy for basic, applied, and cross-disciplinary research
at the 5.5 MV single ended Van de Graaff Accelerator.
The purpose of the work
Beam energy:
E = VT × Z
VT - terminal voltage
Z – charge state of accelerated ion
Multicharged ions
Implantation, crystalline structure modification….
Electron Cyclotron Resonance (ECR) ion source

## Slide 4
SECRAL-II@28 GHz
ECR ion source options
Superconducting type
Hybrid type
Room temperature type
Permanent magnet type
DECRIS-SC2
DECRIS-5
DECRIS-PM
LAPECR2
SUPERNANOGAN
˃ 1m
~ 0.5 m
~ 0.5 m
~ 0.5 m

## Slide 5
High Voltage Terminal
The space available for the ion source
Compact size
Low power consumption: up to 1 kW is available
Low maintenance: This ECRIS should be able to run without any maintenance for no less than 2000 hours.
Requirements to the ECR ion source located at HV terminal

## Slide 6
PM Magnet System for Compact 14 GHz ECR Ion Source №1
Magnetic system for 14 GHz ECR Ion Source №1
PM Magnet
Hexapole
Iron Plug
Magnet

## Slide 7
Axial magnetic field distribution
Axial magnetic system configuration
Configuration №1 | No Plug | With Plug
Magnet Ø, mm | 170 | 170
Chamber Ø, mm | 44 | 44
L, mm | 200 | 200
Bext, T | 1.0 | 1.0
Bmin, T | 0.40 | 0.41
Binj, T | 1 | 1.68
Brad, T | 1.15 | 1.15
W (no hexapole and iron), kg | 26.45 | 26.45
Material | NdFeB (N48SH) | NdFeB (N48SH)

## Slide 8
PM Magnet System for Compact 14 GHz ECR Ion Source №2
Hexapole
Magnet
Iron Plug
Magnetic system for 14 GHz ECR Ion Source №2

## Slide 9
Configuration №1 | No Plug | With Plug
Magnet Ø, mm | 176 | 176
Chamber Ø, mm | 46 | 46
L, mm | 200 | 200
Bext, T | 1.01 | 1.01
Bmin, T | 0.40 | 0.41
Binj, T | 1.04 | 1.74
Brad, T | 1.13 | 1.13
W (no hexapole and iron), kg | 29.12 | 29.12
Material | NdFeB (N48SH) | NdFeB (N48SH)
Axial magnetic field distribution
Axial magnetic system configuration
BECR
Binj
Bext
Bmin

## Slide 10
Magnetic system for 14 GHz ECR Ion Source №3
Iron Plug
Hexapole
Magnet
PM Magnet System for Compact 14 GHz ECR Ion Source №3

## Slide 11
Configuration №1 | No Plug | With Plug
Magnet Ø, mm | 182 | 182
Chamber Ø, mm | 48 | 48
L, mm | 200 | 200
Bext, T | 1 | 1
Bmin, T | 0.4 | 0.41
Binj, T | 1.01 | 1.61
Brad, T | 1.17 | 1.17
W (no hexapole and iron), kg | 30.67 | 30.67
Material | NdFeB (N48SH) | NdFeB (N48SH)
Axial magnetic system configuration
Bext
Binj
Bmin
BECR
Axial magnetic field distribution

## Slide 12
Hexapole configuration
Radial magnetic field distribution
Magnetization configuration (24 sectors): 1 – poles (0о), 2 – middle sectors (45о), 3 – inter-pole sectors (90 о)
Hexapole Ø, mm | 105 | 110 | 115
Brad, T | 1.13 | 1.15 | 1.17
105 mm

## Slide 13
Results
Configuration № | Сhamber Ø, mm | L, mm | No plug/With Plug |  |  | Brad, T | W, kg
 |  |  | Bext, T | Bmin, T | Binj, T |  | 
1 | 44 | 200 | 1/1 | 0.4/0.41 | 1/1.68 | 1.15 | 37.35
2 | 46 | 200 | 1/1 | 0.4/0.41 | 1.04/1.74 | 1.13 | 38.47
3 | 48 | 200 | 1/1 | 0.4/0.41 | 1.01/1.61 | 1.17 | 40.89
Axial field distribution
Configuration 2
Axial field distribution Configuration 1
Axial field distribution
Configuration 3

## Slide 14
Conclusion
Compact magnetic plasma-confinement system for 14 GHz ECR Ion Source was simulated;
The weight of the permanent magnets for axial magnetic field is about 37, 38, 40 kg;
Simulated permanent magnetic system for 14 GHz ECR Ion Source satisfies the specified requirements.

## Slide 15
Thanks for your attention!

## Slide 16
Magnetic System Parameters
Magnetic Plasma-Confinement System Parameters Binj, Bext and Bmin as a function of parameters (a) L3 and (b) L4