## Slide 1
Metallic ion beams production for SHE at FLNR
Dmitry Pugachev
pugachev@jinr.ru

## Slide 2
The heaviest target for experiments on synthesis of superheavy elements in heavy-ion reactions is 249Cf, so further progress in the synthesis of elements with Z > 118 requires the production of intense beams of accelerated neutron-enriched isotopes, such as 50Ti, 54Cr, 58Fe, 64Ni, etc.
Up to 5 pmkA
243Am
249Bk
249-251Cf
248Cm
120
119
50Ti
54Cr

## Slide 3
Low temperature oven – Ca, Mg, Bi, etc.
Inductive/foil oven - Cr and Ti in near future
MIVOC – Cr, Ti, Al, Zr, Fe, etc.
Insertion into plasma – Al
Sputtering – Al, Ta, Cu
Metallic ion beams production
Up to 1000 oC
More than 1000 oC

## Slide 4: DECRIS-PM
Parameters of DECRIS-PM | 
UHF frequency | 14 GHz
Binj | ≥ 1.3 T
Bmin | 0.4 T
Bextr | 1.0 ÷1.1 T
Br | 1.05÷1.15 T
Plasma chamber internal diameter | 70 mm
Magnetic structure of DERIS-PM.
1÷5 – PM rings;
6, 7 – soft iron rings;
8÷11 – soft iron plates;
12÷14 - auxiliary elements;
15 – hexapole; 16 – coil.
Axial magnetic field distribution
Radial magnetic field distribution

## Slide 5
The 48Ca ion spectrum, optimized for Ca10+
Production of 48Ca beam
Faraday Cup | Current, eµA | Efficiency of beam transfer
Iinj1 | 116.642 | 100.0%
Iinj2 | 110.131 | 94.42%
Iinj3 | 100.518 | 86.18%
IRP2-1 | 77.161 | 66.15%
IRP2-2 | 66.103 | 56.67%
IFCI | 55.1 | 47.24%
Total working time, h | 12000
Average consumption, mg/h | 0.5
Average operating current of 48Ca10+, pµA | 8
Global efficiency of the Ca ionization | 16%
48Ca10+

## Slide 6: Calcium consumption
Old
New

## Slide 7
The 54Cr ion spectrum,
optimized for Cr10+ (10 pµA)
The 48Ti ion spectrum,
optimized for Ti9+ (5.5 pµA)
Production of 48Ti and 54Cr beams (MIVOC)
(CH3)5C5Ti(CH3)3
C10H10Cr

## Slide 8
Faraday Cup | Current, eµA | Efficiency of beam transfer
Iinj1 | 47.4 | 100%
Iinj2 | 45.5 | 95.9%
Iinj3 | 40.9 | 86.3%
IRP2-1 | 30.7 | 64.8%
IRP2-2 | 26.4 | 55.7%
IFCI | 21.2 | 44.7%
48Ti9+
Accelerating of 48Ti and 54Cr
Faraday Cup | Current, eµA | Efficiency of beam transfer
Iinj1 | 97.5 | 100%
Iinj2 | 95.2 | 97.6%
Iinj3 | 82.2 | 84.3%
IRP2-1 | 60.7 | 62.3%
IRP2-2 | 54.3 | 55.7%
IFCI | 43.2 | 44.3%
54Cr10+
3 pmkA?
5 pmkA?

## Slide 9
ECR ion source plasma chamber
Ti foil
He + SF6
UHF
Ti + F TiFx
Volatile compounds
*Recycling effect of germanium on ECR ion source P. Leherissier et al.
Nuclear Instruments and Methods in Physics Research B 211 (2003) 274–280
*Production of multiply charged metallic ions by compact electron cyclotron
resonance ion source with SF6 plasma Y. Saitoh et al.
REVIEW OF SCIENTIFIC INSTRUMENTS VOLUME 69, NUMBER 2 FEBRUARY 1998
Ti ion production using SF6 plasma*

## Slide 10
The 48Ti ion spectrum, current of the Ti11+ - 65 eµA
Ti ion production using SF6 plasma
The 48Ti ion spectrum, current of the Ti11+ - 45 eµA
MIVOC - (CH3)5C5Ti(CH3)3
Ti foil

## Slide 11
Screen with Ti foil after operation with SF6 plasma
Seff ≈ 600 mm2
Seff ≈ 4500 mm2

## Slide 12
ECR ion source plasma chamber
Ta screen
He + SF6
UHF
Ti ion production using SF6 plasma*
Ti biased-electrode
R=15mm
S = 707 mm2
Seff ≈ 254 mm2
Seff screen ≈ 20 ∙ Seff bised-electrod

## Slide 13
Ti ion production using SF6 plasma
Seff ≈ 5100 mm2 (Ti screen)
Seff ≈ 250 mm2 (Ti biased-electrode)
He
He
Ti11+=65 emkA
Ti11+=30 emkA
Ti7+=80 emkA
Ti7+=40 emkA

## Slide 14: future plans

## Slide 15
Technical drawings are developed in collaboration with VINCA (Belgrade)
“FOIL” OVEN (GANIL type)
Foil thikness – 0.05 mm
Outer diameter (with screen) – 20 mm
Power consumption – 57 W
Tcrucible, °C - 1500°C
Tfoil, °C - 1700°C
Touter surface, °C - 800°C

## Slide 16
UHF injection
Injection plug
Ø 70
1700⁰C
Inductive oven

## Slide 17
Resonance circuit
Power supply:
EA-PSI 9080-60
0÷80 V, 0÷60 A, 0÷1500 W
Waveguide
Pre-pumping volume
Water cooling of the inductor
water cooling of the crucible holder
Water cooling of the cooper plug

## Slide 18
Inductive oven

## Slide 19: Results and future plans
Calcium consumption was 3.5 mg/h for a high-intensity ion beam (25 pµA 48Ca10+) and 0.3 mg/h for a low-intensity beam (4 pµA 48Ca10+). Average consumption of calcium 0.5 mg/h. Total working time with a calcium beam around 12000 h.
Titanium and chromium beams were obtained on the DC-280 cyclotron. The issues of modernization of the design of some elements of the ion source, contributing to an increase in the intensity of the ion beam using the MIVOC method, are being solved.
“foil” oven will be manufactured, induction oven will be tested in near future. If every tests will be finished successfully we will prepare all equipment to install it on the DECRIS-PM ion source to obtain Ti and Cr ion beams.

## Slide 20: Thank you for your attention