## Slide 1
seminva@jinr.ru
Development of the
FLNR Accelerator Complex and Experimental Setups (DRIBs-III)
and projects within the framework of this LRI for 2024
(03-5-1129-2024/2028)
Head of FLNR Accelerator department
Vasiliy Semin

## Slide 2
DC-280
U-400
U-400M
Mt-25
Sum time of work of accelerator facilities (hours) | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 16904 | 20110 | 15124 | 15065 | 16834 | 16583
IC-100
2
Chart: Time of work (hours)
| 2019 | 2020 | 2021 | 2022 | 2023
U-400 | 5867 | 5654 | 6240 | 6571 | 6595
U-400M | 6755 | 2937 | 0 | 0 | 0
DC-280 | 3377 | 3705 | 5357 | 6037 | 6182
New experimental hall U-400R
stopped 11.11.23
Accelerated complex FLNR
work in 2023
Notes: New experimental hall is in the stage of building completion

## Slide 3
30.01.23
Modernization of U-400M (MC-400)
03-5-1129-1-2024/2028
15.01.24

## Slide 4
Modernization of U-400M (MC-400)
03-5-1129-1-2024/2028

## Slide 5
U-400 → U-400R
03-5-1129-1-2024/2028
Increasing of intensity of beam for ion with
A ≈ 50 from 1.2 pμA to 2.5 pμA;
Smooth variation of energy up to 5 time ;
Decrease of magnetic field from 1.9  2.1 Т to 0.8  1.8 T.
Main cyclotron parameters |  | 
Parametersс | U400 | U400R
A/z range | 5÷12 | 4÷12
Magnetic field | 1.93÷2.1 T | 0.8÷1.8 T
K factor | 530÷625 | 100÷500
RF modes | 2 | 2, 3, 4, 5, 6
Injection potential | 10÷20 kV | 10÷50 kV
Ion energy range | 3÷20 MeV/n | 0.8÷27 MeV/n
Number of sectors | 4 | 4
Number of dees | 2 | 2
Beam extraction | stripping | Stripping, deflector
Power consuption | ~1 MW | ~0.4 MW

## Slide 6: Layout of U400R extraction system :
U-400 → U-400R
recharging method
(foil probes FP1 and FP2)
Start of modernization 2nd half of 2024
03-5-1129-1-2024/2028
Increasing of intensity of beam for ion with
A ≈ 50 from 1.2 pμA to 2.5 pμA;
Smooth variation of energy up to 5 time ;
Decrease of magnetic field from 1.9  2.1 Т to 0.8  1.8 T.
electrostatic deflector (ESD, MC1, MC2, MC3)

## Slide 7
ТМ2 (190, R=2.2m)
ТМ3/ТМ4
(80, R=3.1 m)
U-400 → U-400R
Start of modernization 2nd half of 2024

## Slide 8
The building computer model
The building will have 4 floors:
1st floor: placement of technological systems;
2nd floor: experimental halls, transport gallery and sanitary lock;
3rd floor: measuring and server rooms;
4th floor: power supplies for physical installations.
Area for New building: 2073 m2 ;
Total area of New building: 4565,7 m2 ;
New experimental hall for U-400R
03-5-1129-1-2024/2028

## Slide 9
New experimental hall for U-400R
Beginning of pouring the grillage (rostverk) 21.12.23
First pile 27.07.23
Completion of the pile field 08.12.23
JSC “Electrocentromontazh”
Piles:
763 pcs Ø 0.6m x 18m
Concrete volume:
~4000 m3
Metal reinforcement:
~740 t.
Grillage (rostverk): Concrete volume:
~2771 m3
Metal reinforcement:
~402 t.

## Slide 10
New experimental hall (U-400R)
plans of New experimental hall project realization 06.23 – 06.26
JSC “Electrocentromontazh”
03-5-1129-1-2024/2028

## Slide 11: Planned U400R accelerator complex
Building 131
New experimental hall U-400R
U-400R
Modernization of U-400 into U-400R
in the second half of 2024.
Delivery of new cyclotron components and removal of old elements
JSC “Electrocentromontazh”
Project intersections:
In the process of upgrading
U-400 to U-400R,
the delivery and export of large-sized cyclotron units and components is required
Construction
zone
03-5-1129-1-2024/2028
Construction
zone

## Slide 12
New experimental hall U-400R
New experimental setups (U-400R)
03-5-1129-1-2024/2028
Components of the spectrometer STAR
1. Rotating platform (angle from +10o to +60o)
2. Separator:
2.1. Quadrupole triplet;
2.2. Electric deflector;
2.3 Magnetic deflector (dipole magnet);
3. Clover detector system GABRIELA;
STAR
studying the characteristics of MNT reactions and properties of radioactive decay of neutron-rich isotopes of heavy elements formed in MNT reactions

## Slide 13
New experimental setups (U-400R)
03-5-1129-1-2024/2028 ACTIVITY
Components of the spectrometer SCIF-D
CORSET time-of-flight spectrometer;
Bragg cameras;
Magnetic spectrometer;
Assembly of semiconductor detectors;
Neutron spectrometer;
Gamma spectrometer;
Spectrometer for measuring evaporation residues.
New experimental hall U-400R
to study MNT and quasi-fission reactions near the Coulomb barrier:

## Slide 14
General circuit of a cyclotron DC-140
Complex for applied research based on the DC-140 cyclotron
Energy 4,8 MeV/nucleon |  |  |  | Energy 2,214 MeV/nucleon |  | 
Ion | A/Z | I, µA |  | Ion | A/Z | I, µA
209Bi38+ | 5,5 | 20,67 |  | 209Bi26+ | 8,038 | 0,416
197Au36+ | 5,472 | 19,58 |  | 197Au24+ | 8,208 | 3,84
132Xe25+ | 5,28 | 13,6 |  | 158Gd20+ | 7,9 | 3,2
86Kr16+ | 5,375 | 8,7 |  | 142Nd18+ | 7,889 | 2,88
56Fe11+ | 5,091 | 5,98 |  | 132Xe16+ | 8,25 | 2,56
40Ar8+ | 5 | 4,35 |  | 98Mo12+ | 8,167 | 1,92
16O3+ | 5,333 | 1,63 |  | 90Zr11+ | 8,182 | 1,76
22Ne4+ | 5,5 | 2,18 |  | 86Kr11+ | 7,818 | 1,76
20Ne4+ | 5 | 2,18 |  | 16O2+ | 8 | 0,32
03-5-1129-1-2024/2028

## Slide 15
15
Short-circuiting plates
Pole assembling
Connection loop
Cyclotron vacuum chamber
Trimmer of AFT
Magnet channel
Deflector
PMQ
Cyclotron DC-140 elements
Elements of RF system
Inflector
DECRIS-5M on the test bench
Cyclotron vacuum chamber vacuum test
90% of the equipment has been manufactured and arrived at FLNR

## Slide 16
30.01.23
Cyclotron DC-140
Mounting of DC-140 main magnet
03-5-1129-1-2024/2028

## Slide 17
LLC "MASTERPROM"
Placement of DC-140 in building 101
03-5-1129-1-2024/2028
25.01.24
Control room,
Accelerator hall,
Experimental channels halls
Engineering systems hall
General layout of the DC140 facility

## Slide 18
12.12.23
Cyclotron DC-140
03-5-1129-1-2024/2028
LLC "MASTERPROM"

## Slide 19
Cyclotron DC-280
Year | Total work time | Ions
2018 | First Beam | 84Kr
2019 | 3377 | 12C, 40Ar, 48 Ca, 84Kr
2020 | 3705 | 40Ar, 48 Ca, 48Ti
2021 | 5357 | 48 Ca, 48Ti , 52Cr
2022 | 6037 | 40Ar, 48Ca, 48Ti , 52,54Cr
2023 | 6182 | 26Mg, 40Ar, 48Ca, 48Ti , 52,54Cr, 56Fe
SHE factory
03-5-1129-2-2024/2028

## Slide 20
Effectivity of acceleration on DC-280
48Са10+
Chart: 48Ca10+
| IFC1 | IFC2 | IFC3 | RP2_263 | RP2_300 | RP2_400 | RP2_500 | RP2_600 | RP2_700 | RP2_800 | RP2_900 | RP2_1000 | RP2_1100 | RP2_1200 | RP2_1300 | RP2_1400 | RP2_1500 | RP2_1600 | RP2_1700 | RP2_1770 | T0FC2
I=0,5 pmkA | 1 | 1.0094 | 0.97172 | 0.75627 | 0.74188 | 0.7274 | 0.72269 | 0.72218 | 0.72008 | 0.72092 | 0.72092 | 0.72008 | 0.72025 | 0.71991 | 0.71823 | 0.71697 | 0.71646 | 0.71411 | 0.70056 | 0.67682 | 0.44976
I=7,7 pmkA | 1 | 0.94633 | 0.86628 | 0.62619 | 0.6204 | 0.6107 | 0.59885 | 0.5961 | 0.59185 | 0.58046 | 0.57641 | 0.5792 | 0.57541 | 0.57536 | 0.57466 | 0.57391 | 0.57571 | 0.56966 | 0.55331 | 0.53998 | 0.37985
Chart: 48Ti9+
| IFC1 | IFC2 | IFC3 | RP2_263 | RP2_300 | RP2_400 | RP2_500 | RP2_600 | RP2_700 | RP2_800 | RP2_900 | RP2_1000 | RP2_1100 | RP2_1200 | RP2_1300 | RP2_1400 | RP2_1500 | RP2_1600 | RP2_1700 | RP2_1770 | T0FC2
Iecr=5.07pmkA; P=300W; I=1.66pmkA | 1 | 0.93704 | 0.81062 | 0.54858 | 0.53659 | 0.52714 | 0.51778 | 0.51463 | 0.51406 | 0.49824 | 0.491 | 0.48772 | 0.48412 | 0.47998 | 0.47503 | 0.46994 | 0.46271 | 0.43692 | 0.42609 | 0.41436 | 0.32661
Iecr=4.83pmkA; P=242W; I=2.13pmkA | 1 | 0.92048 | 0.81292 | 0.59289 | 0.58273 | 0.57765 | 0.57482 | 0.57174 | 0.57201 | 0.56056 | 0.55686 | 0.55647 | 0.55477 | 0.55342 | 0.5527 | 0.54951 | 0.54753 | 0.5264 | 0.51751 | 0.51022 | 0.44003
Iecr=4.74pmkA; P=198W; I=2.12pmkA | 1 | 0.9595 | 0.86111 | 0.64673 | 0.63956 | 0.63242 | 0.6274 | 0.62628 | 0.62443 | 0.61562 | 0.61227 | 0.61056 | 0.60951 | 0.60806 | 0.60597 | 0.60415 | 0.59862 | 0.58637 | 0.5644 | 0.5555 | 0.44682
Chart: 52Cr10+
| IFC1 | IFC2 | IFC3 | RP2_263 | RP2_300 | RP2_400 | RP2_500 | RP2_600 | RP2_700 | RP2_800 | RP2_900 | RP2_1000 | RP2_1100 | RP2_1200 | RP2_1300 | RP2_1400 | RP2_1500 | RP2_1600 | RP2_1700 | RP2_1770 | T0FC2
Iecr=2.5pmkA; P=130W; I=0.9pmkA | 1 | 0.77326 | 0.73013 | 0.56367 | 0.5537 | 0.53651 | 0.54052 | 0.54052 | 0.53534 | 0.52615 | 0.52215 | 0.51218 | 0.52054 | 0.51897 | 0.51976 | 0.51658 | 0.51536 | 0.501 | 0.50022 | 0.48625 | 0.37237
Iecr=5.3pmkA; P=280W; I=2.09pmkA | 1 | 0.858 | 0.80886 | 0.55697 | 0.54034 | 0.52371 | 0.50613 | 0.51148 | 0.50956 | 0.50708 | 0.50669 | 0.50613 | 0.50783 | 0.50344 | 0.48223 | 0.47191 | 0.4612 | 0.46656 | 0.46387 | 0.46464 | 0.39283
Iecr=6.3pmkA; P=172W; I=2.6pmkA | 1 | 0.90665 | 0.82911 | 0.59968 | 0.57437 | 0.56329 | 0.53956 | 0.54589 | 0.54272 | 0.54589 | 0.53956 | 0.5269 | 0.53639 | 0.53956 | 0.53481 | 0.53006 | 0.52848 | 0.48892 | 0.51266 | 0.51108 | 0.41456
Iecr=7pmkA; P=235W; I=2.33pkmA | 1 | 0.828 | 0.73535 | 0.4925 | 0.48441 | 0.47113 | 0.4658 | 0.46638 | 0.46594 | 0.46552 | 0.46479 | 0.4645 | 0.46552 | 0.46162 | 0.45381 | 0.44214 | 0.43796 | 0.44011 | 0.43074 | 0.43866 | 0.33051
48Ti9+ from
(CH3)5C5Ti(CH3)3
52Сr10+ from
Cr(C5H5)2
Spectrum from DECRIS-PM in optimal regime
03-5-1129-2-2024/2028
SHE factory

## Slide 21
Schematic view of the GASSOL magnetic separator.
03-5-1129-2-2024/2028
SC solenoid, cryogenic system, control equipment
Contract with XI'an Superconducting Magnet Technology Co., Ltd.
Delivery at the end of 2024.
Installation of ion transport channel in the experimental hall at the SHE factory, Preparation for equipment placement
During 2024
SC solenoid-based spectrometer for the chemical studies of short-lived super-heavy nuclei is expected to be completed and delivered in Dubna by the end 2024.
SHE factory
GASSOL
Test coil (October 2023)
GASSOL
transmission efficiency > 40%
Focus to spot < Ø1 cm
(T1/2< 0.5 s)

## Slide 22
Block diagram of the mass spectrometer.
The ion source for the spectrometer is a gas-filled ion stopping cell
at the outlet of the gas filled recoil separator.
General view of cryogenic gas catcher:
1 - entrance window;
2 - external warm vacuum shell;
3 - internal cold chamber;
4 - cylindrical electrodes of constant electric field;
5 - radio-frequency multielectrode cone;
6 - head of cryo-refrigerator;
7 - supersonic nozzle;
8 - transport radio frequency quadrupole.
MR TOF spectrometer
Accuracy of about 300 keV
relative accuracy of 10-6
for a mass of 300 a.m.u.
SHE factory
MR ToF
Diagram of a mass spectrometer:
1 - node of the multi-turn time-of-flight mass analyzer;
2 – node of quadrupole mass filters;
3 - node of the channel for introducing sample ions;
4 - node of the channel for introducing calibrant ions;
5 - node of detectors.
03-5-1129-2-2024/2028
Main characteristics of the spectrometer.
The length of the time-of-flight base of the mass analyzer is 1000 mm.
The maximum number of revolutions in the analyzer is 500.
Required vacuum in the analyzer chamber < 10-8 Torr.
Range of measured masses А=12÷500.
Mass resolution М/ΔМ=1.5∙106.
Accuracy of mass determination with event statistics >100 ∆M/M=10-7.
Minimum lifetime of analyzed nuclides τ>50 ms.
Sensitivity of statistically significant measurement ~10 ions;
Measurement frequency up to 400 Hz;
Transmission efficiency up to 95%;
Measurement dynamic range >104.
Availability of the ability to analyze single
and doubly charged ions without loss of efficiency.

## Slide 23
MR TOF spectrometer
SHE factory
MR TOF
03-5-1129-2-2024/2028
Cryogenic gas stopping cell (gas catcher) 1. Done:
Mechanical design,
Vacuum system,
Gas inlet,
Cryogenic,
Control system
2. Offline testing started
MRTOFMS 1. Ion-opting system calculation done 2. Draft mechanical design done 3. Development of design documentation was started

## Slide 24
Production of high-intensity ion beams 48Ti+10 at the DC-280 cyclotron
iThe 48Ti ion spectrum, optimized for 48Ti10+
Axial injection system |  | Cyclotron |  | Transport channel (T0FC2), pµA
After separation (IFC2), pµA | Before injection (IFC3), pµA | R=400 mm, pµA | R=1770 mm, pµA | 
13,2 | 10,6 | 4,6 | 4,1 | 3,26
80,0% |  |  |  | 
 | 43,5% |  |  | 
 |  | 88,4% |  | 
 |  |  | 79,7% | 
24,5% |  |  |  | 
Accelerated beam stability 48Ti+10
11 hours
03-5-1129-2-2024/2028
*Recycling effect of germanium on ECR ion source P. Leherissier et al.
Nuclear Instruments and Methods in Physics Research B 211 (2003) 274–280
*Production of multiply charged metallic ions by compact electron cyclotron
resonance ion source with SF6 plasma Y. Saitoh et al.
REVIEW OF SCIENTIFIC INSTRUMENTS VOLUME 69, NUMBER 2 FEBRUARY 1998
Development of
refractory metals
ion production methods

## Slide 25
INDUCTIVE OVEN
Adaptation to DECRIS-PM
Development of
refractory metals
ion production methods
Thermocouple15000С
Test Ni wire
03-5-1129-2-2024/2028

## Slide 26
DC-280 beam intensity and efficiency of acceleration
Ion | Energy (MeV) | Intensity (pµA) |  |  |  | Transport Channel | Efficiency (%) |  |  |  | 
 |  | Axial injection |  | Cyclotron |  |  |  |  |  |  | 
 |  | after separation | before injection | R=400 mm | R= 1770 mm |  | Axial injection | Capture | Cyclotron | Extraction | Total
48Ca+10 | 240 | 1,2 | 1,15 | 0,86 | 0,80 | 0,5 | 96% | 75% | 93% | 67% | 45%
48Ca+10+ | 240 | 9 | 8,1 | 5,6 | 5,1 | 4,7 | 90% | 69% | 91% | 91% | 50%
48Ca+10 | 240 | 20 | 17,6 | 12,4 | 11 | 7,7 | 87% | 70% | 88% | 71% | 38%
48Ti+9 | 265 | 4,8 | 3,9 | 2,8 | 2,5 | 2,1 | 81% | 71% | 88% | 86% | 44%
48Ti+10 | 244 | 13,2 | 10,6 | 4,6 | 4,1 | 3,2 | 80% | 43% | 88% | 80% | 25%
52Cr+10 | 250 | 6,3 | 5,2 | 3,6 | 3,2 | 2,6 | 83% | 69% | 91% | 81% | 42%
54Cr+10 | 270 | 9,8 | 8,2 | 5,8 | 5,4 | 4,3 | 86% | 71% | 93% | 80% | 44%
56Fe+10 |  | 5,0 | 4,5 | 3,5 | 3,4 | 2,8 | 90% | 77% | 97% | 82% | 55%
SHE factory
Thank you for your attention

## Slide 27
RF-kicker:
  Test of new measuring system
  Local radiation shield design
  Radiation safety control
Development of the infrastructure of the ACCULINNA-2 fragment separator in 2024
Tritium target complex:
  Precommissioning of tritium supply equipment
  Mounting of system for storage and transport of pure gases