## Slide 1
Answers to the DAC questions for the MPD TOF
V. Babkin on behalf of the TOF MPD group
MPD Detector Advisory Committee, Dubna, January 2018

## Slide 2
Time of Flight system of the MPD
Z-direction detectors layout
 | Number of detectors | Number of readout strips | Sensitive area, m2 | Number of FEE cards | Number of FEE channels
MRPC | 1 | 24 | 0.192 | 2 | 48
Module | 10 | 240 | 1.848 | 20 | 480
Barrel | 280 | 6720 | 51.8 | 560 | 13440 (1680 chips)
φ-direction TOF modules layout
Triple-stack MRPC cut view
Notes: At the beginning, let me remind you about the current design of the barrel part of the TOF system.
It looks like a cylinder composed of 14 sectors. It is convenient for integration with ECal since it consists of 28 sectors.
The radius of the TOF cylinder is about one and half meters. The radius of the TOF cylinder is about one and half meters.
Detectors are arranged inside module with small angle to the beam line for better registration and geometrical efficiency.
In this table I present the numbers of the main parts of the barrel TOF.
Total the TOF contents 280 detectors and covers the area of 52 square meters. The total number of the electronics channels is 13440

## Slide 3
Question 1

## Slide 4
Geometric efficiency
We calculate the geometrical efficiency which depends on the geometry of whole TOF system and arrangement of the MRPCs in the TOF. The efficiency in Fig. 3.13 is differential efficiency (dε/dZ) along the Z direction with step of 1 cm and averaged (integrated) over the angle φ (sum of particles for all 14 modules/14).
It follows from the Fig. 3.13 that 93,5% of all particles flying in direction of the TOF fall into the active region of detectors. The others (inefficient) fly through the gaps between the modules.

## Slide 5
Geometric efficiency
Two adjacent TOF modules
~93% eff
~94% eff
The origin of the zigzags in the efficiency. The upper zigzag peak corresponds to the lower edge of the detector in adjacent modules. In this position, the active regions of adjacent modules are closest to each other. Therefore, more particles are detected at this location.
~94% eff
~93% eff
A
Z – cross-section
φ – cross-section

## Slide 6
These are different efficiencies. Efficiency measured in the beam or cosmic tests (for example on fig.2.10) is only intrinsic registration efficiency of the MRPC due to primary ionization and avalanche statistic. This efficiency doesn’t depend on the TOF system position or geometry but depends on the width of the gas gap, gas composition, applied voltage, etc. Since all detectors that we tested have intrinsic efficiency about 99%.
Addition Question
Geometric efficiency

## Slide 7
Question 2

## Slide 8
Particles registered in TOF (Eloss>0). Primary&secondary. All materials. B = 0.5 T!
Particle type | Mean multiplicity
Total | 394.2
Protons | 30.29
Neutrons | 0.38
Pions +- | 345.8
Kaons +- | 15.93
Electrons | 0
Positrons | 0
Gamma | 0.3
Muons +- | ~0
Other | 1.5
Particle type | Mean multiplicity
Total | 678
Protons | 65.43
Neutrons | 2.56
Pions +- | 409.61
Kaons +- | 16.22
Electrons | 42.18
Positrons | 39.79
Gamma | 40.26
Muons +- | 55
Other | 6,9
Primary
Primary+Secondary
Total 678
Occupancy =
Conditions: LAQGSM vertex: AuAuss11_5mb5_mer.r12, 60000 events, √S = 11 GeV, b < 3fm (central)

## Slide 9
TOF geometry in MPD ROOT
0%
30%
0%
5 mm
10 mm
2.5 mm
Experimental

## Slide 10
Occupancy (hits per event per one channel of the TOF)
Cuts: 1) time of particles crossing TOF >30 ns (separated by electronics)
2) do not take into account the electrons generated inside the TOF detectors
Particles/(channel*Z*dφ)
all particles
primaries

## Slide 11
Occupancy (efficiency of the reconstructed track on the TOF)
Efficiency
Reconstructed by the TPC track with one TOF hit without background hits
All tracks with and without background
Efficiency =

## Slide 12
Occupancy (separation of two hits on one strip)
t, ns
W2=13 ns
Hit1
Hit2
Hit1
Hit2
Summa
THit1
THit2
FEEleft
FEEright
LEFT
t, ns
15 ns
13 ns
Hit1
Hit2
Summa
17 ns
THit2
THit1
Right
W1=15 ns
Wsumm=17 ns
t, ns
W2=13 ns
Hit1
Hit2
Hit1
Hit2
Summa
THit1
THit2
FEEleft
FEEright
LEFT
t, ns
15 ns
13 ns
Hit1
Hit2
Summa
THit2
THit1
Right
W1=15 ns
ΔT=16 ns
2 ns
1) ΔT > W1 – can separate both particles with ToT correction
2) |THit1-THit2|< (D*0,06) ns – can separate both particles without ToT correction
D (cm)

## Slide 13
Question 3

## Slide 14
We take into consideration only reliably reconstructed tracks that have reached the TOF barrel. Number of these tracks is Nrec_tracks for the efficiency and contamination calculation.
Matching
In the TOF detector each track has an extrapolated point with spatial window, determined by the accuracy of the reconstructed track extrapolation (3σ).
Hits in the TOF - candidates for matching are selected in each track window (even if they overlap). Such candidates can be more than one in one window.
The first iteration selects only tracks with one candidate hit that fall into the window. It is considered that a match is found for them.
The second iteration considers two-candidate tracks. We search the nearest to track hit and exclude these pairs from consideration. Iterations are repeated for all multi-candidate tracks.
If, as a result of matching, the track and the TOF hit correspond to the correct particle, then such track is considered to be well-matched or true (Nt). If matched track correspond to the wrong particle, then such a track is considered wrong-matched (Nw).
In a real experiment, we cannot distinguish between true and false combinations. Therefore, the matching efficiency is calculated as: eff=(Nt+Nw)/Nrec_tracks
Contamination means the ratio of wrong-matched to the sum of wrong and true matched pairs: cont=Nw/ (Nt+Nw)
Hit1
Hit2
FEEleft
FEEright
Well-matched track
TPC points
Track extrapolated point with 3σ spatial window

## Slide 15
Matching efficiency
eff=(Nt+Nw)/Nrec_tracks
The slow decrease in efficiency in the Pt range between 0.5 and 3 GeV/c is due to dependence of the matching efficiency on the multiple scattering, which in turn depends on the momentum of the particle.

## Slide 16
Backup slides

## Slide 17
all | 2017,00 | 609,90 | 551,20 | 558,70 | 509,00 | 436,20 | 394,20
proton | 153,80 | 38,27 | 37,78 | 34,18 | 33,87 | 30,57 | 30,29
neutron | 183,40 | 45,67 | 45,67 | 43,25 | 43,33 | 0,42 | 0,38
pion+- | 895,90 | 465,80 | 408,20 | 426,60 | 378,00 | 387,00 | 345,80
kaon+- | 64,90 | 19,47 | 18,84 | 18,05 | 17,35 | 16,48 | 15,93
electron | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00
positron | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00
gamma | 36,41 | 24,71 | 24,70 | 21,96 | 21,94 | 0,48 | 0,30
muon+- | ~0 | ~0 | ~0 | 0,00 | 0,00 | ~0 | ~0
pi0 | 564,60 |  |  |  |  |  | 
SUM: | 1899,00 | 593,90 | 535,20 | 544,00 | 494,50 | 434,90 | 392,70
SUM%: | 94.1% | 97.4% | 97.1% | 97.4% | 97.2% | 99.7% | 99.6%
-- |  |  |  |  |  |  | 
SECONDARY: |  |  |  |  |  |  | 
all | -- | 1103,00 | 1054,00 | 5208,00 | 4980,00 | 467,90 | 283,80
proton | -- | 25,21 | 24,18 | 60,63 | 58,52 | 35,94 | 35,14
neutron | -- | 46,40 | 47,86 | 1841,00 | 1854,00 | 2,14 | 2,18
pion+- | -- | 57,33 | 46,10 | 88,85 | 72,13 | 75,85 | 63,81
kaon+- | -- | ~0 | ~0 | 0,33 | 0,34 | 0,28 | 0,29
electron | -- | 30,71 | 4,82 | 218,50 | 44,91 | 125,40 | 42,18
positron | -- | 14,20 | 4,36 | 154,10 | 41,71 | 117,70 | 39,79
gamma | -- | 839,30 | 845,80 | 2750,00 | 2835,00 | 33,91 | 39,96
muon+- | -- | 86,06 | 77,49 | 84,76 | 62,84 | 71,19 | 55,00
-- | -- |  |  |  |  |  | 
SUM: | -- | 1099,20 | 1050,60 | 5198,20 | 4969,50 | 462,40 | 278,40
SUM%: | -- | 99.7% | 99.7% | 99.8% | 99.8% | 98.8% | 98.1%
Vertex
Cylinder, B=0.5T
Cylinder, B=0T
Cylinder, B=0T
All materials
Cylinder, B=0.5T
All materials
TOF, B=0T
All materials
TOF, B=0.5T
All materials

## Slide 18
Particles on the cylinder at the TOF distance. Primary&secondary. All materials. B = 0.5 T!
Particle type | Mean multiplicity
Total | 509
Protons | 33,87
Neutrons | 43,33
Pions +- | 378,0
Kaons +- | 17,35
Electrons | 0
Positrons | 0
Gamma | 21,94
Muons +- | 0
Other | 14,5
Particle type | Mean multiplicity
Total | 4980
Protons | 58,52
Neutrons | 1854
Pions +- | 72,13
Kaons +- | 0,34
Electrons | 44,91
Positrons | 41,71
Gamma | 2835
Muons +- | 62,84
Other | 10,5
Primary
Secondary
Total 5489
Cylinder (virtual TOF) R = 152, Z =[-300,+300] // [cm]
Conditions: LAQGSM vertex: AuAuss11_5mb5_mer.r12, 60000 events
√S = 11.5 GeV, b < 3fm (central)

## Slide 19
cont=Nw/ (Nt+Nw)