## Slide 1
Status of development of high-power semiconductor RF amplifiers for basic facilities of FLNR JINR
Engineer of the
HF Accelerator Systems Group
Belozerov Dmitriy

## Slide 2
High Frequency amplifier of U400
Amplifier structure

## Slide 3
High Frequency amplifier of DC-280
Amplifier structure

## Slide 4
High Frequency amplifier of U400M (MC400)
Amplifier structure

## Slide 5
 | U400М (MC400) | U400 | DC-280 | 
 |  |  | Main res. sys | Flat-Top res. sys
Range of operating frequencies | 11 ÷ 22 MHz | 5,9 ÷ 12 MHz | 7,2 ÷ 10,4 MHz | 21,6 ÷ 31,2 MHz
RF power for a single resonator | Up to 30 kW | Up to 35 kW | Up to 25 kW | Up to 2 kW
quantity of resonators | 4 | 2 | 2 | 2
Required power and frequency parameters

## Slide 6
Structure of a high-power semiconductor amplifier

## Slide 7
Air-cooled HF amplifier
Parameters of the amplifier:
Case (form factor 3U)
Usupply = 220 V
Power dissipation up to 1 kW
*F — 11 ÷ 22 MHz
HF gain by power ≥ 60 dB
HF output power up to 0,5 kW
* it is determined by the parameters of the internal filter

## Slide 8
Breadboard of a new 1 kW semiconductor water-cooled HF amplifier
Preamplifier:
Usupply = 24 V
Power dissipation up to 60W
F — 5,5 ÷ 32 MHz
HF gain by power ≥ 40 dB
HF output power up to 30W
Powerful cascade:
Usupply = 48 V
Power dissipation up to 2,5 kW
F — 5,5 ÷ 32 MHz
HF gain by power ≥ 27 dB
HF output power up to 1,25 kW

## Slide 9
50 Ω
Input
Output
HF filter-duplexer
Filter parameters:
Bandwidth 11 ÷ 22 MHz
Power dissipation of the absorbing resistor = 150 W

## Slide 10
The power summing unit
Ready:
Device case (form factor 2U)
Power summation circuit
Measuring section
In the manufacturing process:
Power divider circuit
Radiator for ballast resistors
Panels for mounting connectors
Water cooling system
Air cooling system
Protection device

## Slide 11
Plans for the near future
1. Finish assembling the power summing unit (in the first iteration without protection device)
2. Test the power summing unit with air-cooled HF amplifiers and dummy load
3. Improve the breadboard of the high power HF amplifier (combining the electrical circuits of pre- and powerful cascades)

## Slide 12
Thanks for your attention