## Slide 1
JINR Association of Young Scientists and Specialists Conference “Alushta-2024”
Measurements of nuclear reaction cross-sections at VITA
BINP
Sokolova Evgeniia

## Slide 2: Accelerator based neutron source VITA
1 - vacuum insulated tandem accelerator
2 - target (A, B, C, D, E position)
3 - beam shaping assembly

## Slide 3: Scheme of the cross-section measuring
135°
15°
168°
1 - vacuum insulated tandem accelerator
2 - collimator
3, 5 - α-spectrometer PDPA-1K (IPTP, Dubna, Russia)
4 - target
6 - radiation shielding
7 - γ-ray spectrometer SEG1KP-IPTP (IPTP, Dubna, Russia)

## Slide 4: Li + proton/deuteron
7Li(p,n)7Be
7Li(p,p’g)7Li
7Li(p,a)4He
6Li(d,a)4He
6Li(d,p)7Li
6Li(d,p)7Li*
7Li(d,a)5He
7Li(d,na)4He
7Li(d,n)8Be
Boron neutron capture therapy
Powerful source of fast neutrons

## Slide 5: Lithium target manufacturing
System for thermal vacuum evaporation
Lithium 100 µm
Glove box with argon 99,9998 %
Lithium on air

## Slide 6: 7Li(p,n)7Be Neutrons for BNCT (Boron neutron capture therapy)
7Li(p,n)7Be - is the best reaction for BNCT
only calculations of the neutron yield
the calculations of different groups of scientists vary greatly
Experimental confirmation of neutron yield is needed!

## Slide 7: 7Li(p,n)7Be Neutrons for BNCT (Boron neutron capture therapy)
Precise neutron yield measurements are carried out based on the number of 7Be [1]
Result:
The neutron yield from the developed lithium target, measured at proton energies from 2 to 2.2 MeV, agrees with the calculated one with an accuracy of 5%.
[1] M. Bikchurina, et al. Biology 10 (2021) 824.

## Slide 8: 7Li(p,p’γ)7Be γ-quanta in BNCT (Boron neutron capture therapy)
γ-quanta with an energy of 478 keV in the reaction 7Li(p,p‘γ)7Li are generated from the lithium target
The 478 keV γ-quanta yield is comparable to the neutron yield
γ-quanta provide an undesirable dose of gamma-radiation and must be taken into account when planning therapy
Data on γ-quanta yield are scarce and contradictory
The measurement of γ-quanta yield is needed!

## Slide 9: 7Li(p,p’γ)7Be γ-quanta yield
NIM B 502 (2021) 85
IBANDL
EXFOR
E, MeV

## Slide 10: 7Li(p,p’γ)7Be cross-section of the reaction
NIM B 502 (2021) 85
IBANDL
EXFOR

## Slide 11: B + proton/deuteron
11B(p,a0)8Be
11B(p,a1)8Be*
10B(d,a )8Be 10B(d,p)11B
11B(d,a)9Be 11B(d,p)12B
3a Aneutronic fusion reaction
Technological applications

## Slide 12: Boron target manufacturing
Glove box with magnetron sputtering system (Mbraun, Germany)
Glove box with magnetron sputtering system
(Izovac, Belarus)
Boron 1 µm
Laboratory of Plasma Sources HCEI SB RAS
(thanks to Oks E.M., Nikolaev A.G., Yushkov G.Yu.)

## Slide 13: 11B(p,a)aa Reaction mechanism and cross-section
11B + p → 12C* → a + a +a + 8.681 MeV
11B + p → 12C* → a0 + 8Be + 8.587 MeV
8Be → a01 + a02 + 0.094 MeV
11B + p → 12C* → a1 + 8Be* + 5.557 MeV
8Be → a11 + a12 + 3.124 MeV

## Slide 14
11B(p,α1)8Be*
11B(p,α0)8Be

## Slide 15: Conclusion
The cross-sections of 19 nuclear reactions were measured with high accuracy at VITA:
7Li(p,n)7Be, 7Li(p,p’g)7Li, 7Li(p,a)4He, 6Li(d,a)4He, 6Li(d,p)7Li, 6Li(d,p)7Li*, 7Li(d,a)5He, 7Li(d,na)4He, 7Li(d,n)8Be [1, 2];
11B(p,a0)8Be, 11B(p,a1)8Be* [3]; 10B(d,a)8Be, 10B(d,p)11B, 11B(d,a)9Be, 11B(d,p)12B.
Cross-sections of the reactions 7Li(p,p'g)7Li [4] and 7Li(p,a)4He [5] are included in the IBANDL and EXFOR nuclear reaction databases maintained by the IAEA.
[1] Taskaev et al. NIM B (2024) - sent for publication 02.24, after corrections and responses to comments 05.24
[2] Meshchaninov et al. Physics of Atomic Nuclei (2024) - sent for publication 02.24
[3] Taskaev et al. Physics of Atomic Nuclei (2024) - sent for publication 02.24
[4] Taskaev et al. NIM B 502 (2021) 85-94
[5] Taskaev et al. NIM B 525 (2022) 55-61
Thank you for attention!