## Slide 1: JINR Association of Young Scientists and Specialists Conference "Alushta-2024" Remote reconfiguration, debugging, testing and synchronization of Electronics Cards for the TPC/MPD Detector of the NICA project
Alushta, 2024
Denis Potapov, an engineer of the
TPC/MPD group, VBLHEP, JINR

## Slide 2: TPC/MPD Detector of NICA Complex
1. Front-End Cards (FECs) position;
2. End cap thermal screen;
3. Read-Out Chamber (ROC) based on Multi-Wire Proportional Chamber (MWPC);
4. High Voltage (HV) electrode;
5. Field cage position.
2
Time-Projection Chamber (TPC)
3
1
4
MPD layout and TPC section
5

## Slide 3
JTAG programmer USB Blaster
FEC controller
SAMPA FEC
1 ROC:
62 FECs
24 ROCs:
1488 FECs
FEC connection for remote access & synchronization
Test setup of 62 FECs on 1 ROC
FEC assembly
Micro coaxial cables assemblies
FECs integration on ROC

## Slide 4
Test setup for remote access prototype unit
Tested prototype
This remote access prototype unit uses JTAG (up to x7 FECs) for:
  FPGA reprogramming;
  FPGA debugging;
  An additional channel for accessing the digital part of the Data acquisition subsystem (DAQ).
Prototype of functional unit

## Slide 5: Block diagram of remote access unit for Control & Synchronization System
Same chips
Out con. (JTAG)
In con. (JTAG)
SCANSTA112
Programmer
USB Blaster
Out con. (JTAG)
…
6
…
6
JTAG
Control &
Synchronization System
…
11
FEC_1
FEC_6
JTAG
JTAG
JTAG via LVDS
Tested prototype
Out con. (JTAG)
SCANSTA112
Out con. (JTAG)
…
6
…
6
JTAG
FEC_61
RCU-64
JTAG
Remote access unit
for each ROC
JTAG via LVDS
JTAG via LVDS
Inside
MPD magnet

## Slide 6: Prototype of functional unit
Test setup for synchronization prototype unit
Readout and Control Unit-64
Tested prototype
This synchronization prototype unit fanout transceiver reference clock to 62 FECs (1 ROC sync.)
Synchronization unit of System will fanout 5 external signals to FECs:
  3 types reference clocks;
  Data trigger;
  Reset.

## Slide 7: Block diagram of synchronization unit for Control & Synchronization System
In con. (LVDS)
RCU-64
…
8
MAIN
ZL40226
ZL40226
ZL40226
LVDS
LVDS
Out con. (LVDS)
FEC_57
FEC_64
…
8
Optical links
Out con. (LVDS)
FEC_1
FEC_8
…
8
LVDS
LVDS
LVDS
Tested prototype
Synchronization
unit for each ROC
RCU-64
24
…
5
Outside MPD magnet
Inside
MPD magnet
Same chips
External
sync. unit
Control &
Synchronization System
5
5
5
5
5

## Slide 8: Control & Synchronization System is under design
3D model of device Control & Synchronization System(top/bottom view). Size is 810 x 60 mm
JTAG over LVDS. Сable length is about 2m
Part of PCB trace

## Slide 9: Сonclusion
Comprehensive tests of prototypes of remote access and synchronization units have been carried out;
Electrical circuit of control & synchronization units has been developed;
Size and location of control & synchronization units on TPC are determined;
Tracing of PCB has been partially completed.
Future plans:
  Accompany production of device;
  Perform full-featured device testing;
  Develop external fanout (for 24 RCUs).

## Slide 10: JINR Association of Young Scientists and Specialists Conference "Alushta-2024" Remote reconfiguration, debugging, testing and synchronization of Electronics Cards for the TPC/MPD Detector of the NICA project
Alushta, 2024
Denis Potapov, an engineer of the
TPC/MPD group, VBLHEP, JINR